README CTD dataContact Rik Wanninkhof, wanninkhof@aoml.noaa.govLast update October 19, 1998Oct 19:  Added CTD stations 204-217 which were inadvertently left out of original dataThe folders contain 1-dB averaged CTD data from the GAS EX-98 cruise. The SEABIRD CTD was equipped with dual temp and conductivity sensors.The data was processed by Geoff Samuels and are off-the-ship data.  No post-cruise corrections have been applied.This folder contains the following files (as comma delimited files). All files are comma delimited with one header line.Explanation of column headers:A: direction= downcast (d) or upcast (u)B: CTD= CTD cast # starting at cast 132C: MonthD: DayE: yearF: time (GMT)= hour:minute: second when CTD acquisition program was startedG: JD = Julian day  (year day)H: Lat = latitude (decimal)I: Long = longitude (decimal)J: pressure [db]K: primary t sensor, t068: temperature, IPTS-68 [deg C]L: secondary t sensor t168: temperature, sec, IPTS-68 [deg C]M: primary conductivity sensor:  c0S/m: conductivity, primary [S/m]N: secondary conductivity Sensor: = c1S/m: conductivity, secondary [S/m]O: salinity from primary t and C sensors, PSS-78 [PSU], T0, C0P:  salinity from secondary t and C salinity, PSS-78 [PSU], T1, C1Q: potential density from primary sensor: sigma-_00: density, sigma-theta [kg/m^3], T0, C0R: Potential density from secondary sensor sigma-_11: density, sigma-theta [kg/m^3], T1, C1S: potential temperature from primary sensor: potemp068: potential temperature, IPTS-68 [deg C]T: potential temp from secondary sensor: potemp168: potential temperature, sec, IPTS-68 [deg C]U: QC flag (see SEABIRD manualDowncast: 1-dB averages of each downcast as one big file Upcast : 1-dB averages of each upcast as one big file Top_70_m: 1-dB averages of each up- and downcast down to 70-m as one big fileMixed_depth: mixed layer depth estimated from up and downcast using the criteria that the surface mixed layer ends where the temperature decreases by 0.1 C.