RON BROWN GASEX '98 Cruise dataM-AERI skin temperaturesThe M-AERI skin temperatures are stored in ASCII files, one file per UTC day.The file names are yymmdd.mlt and the data are stored in columns in the file; the column descriptions are given at the start of each file, e.g.#MLT; Air and Sea-surface Temperatures from MAERISST                           #Id: maerisst.for 1.33 1998/02/17 17:39:22 BenH Exp BenH $                     #Date of observations (YYMMDD): 980722                                         #label 1 DayOfYear                                                             #label 2 Hour                                                                  #label 3 AirTemp                                                               #label 4 StdDevAirTemp                                                         #label 5 MeanUncertaintyAirTemp                                                #label 6 SkinTemp                                                              #label 7 StdDevSkinTemp                                                        #label 8 MeanUncertaintySkinTemp                                               #label 9 Latitude                                                              #label 10 Longitude                                                            The M-AERI operates continuously and temperatures are retrieved irrespective ofwhether the instrument is covered by a tarpaulin, as in conditions of heavy rain or sea spray, or is looking at the sea surface. The skin temperature is derived from measurements at ~7.7um at a zenith angle of 55 degrees, and the derivation takes into account the effect of reflected sky radiance, using a constant surface emissivity. The air temperature is deteived from measurement swhere the atmospehric path length is short and so are a measure of the air temperature a little way form the ship.BEWARE - These files contain the entire data, ie they include data when the instrument was under the tarp.  Quality-controlled data, excluding these occurences will be available shortly.For further information, please contact  Peter J. Minnett  Meteorology and Physical Oceanography  Rosenstiel School of Marine and Atmospheric Science  University of Miami  4600 Rickenbacker Causeway  Miami, FL  33149-1098  Tel: +1 (305) 361-4104	      Fax: +1 (305) 361-4622  email: 	pminnett@rsmas.miami.edu  peter.minnett@arm.gov	pminnett@netscape.net           pminnet@ibm.net	http://www.rsmas.miami.edu/people/pminnett.html