Cruise:  ABACO, Eastern Boundary Current

Ship:  R/V Ronald H. Brown

Dates:  February 11 – 14, 2003

Chief Scientist:  Molly Baringer

Equipment:  24 bottle CTD with dual C, T, and O2 sensors and LADCP

Number of Stations:  54

Sample Collection

DIC:

5 stations, 62 samples each 500-ml, 6 sets of duplicate samples

PI:  Dr. Rik Wanninkhof, AOML

Analyzed by:  Esa Peltola, AOML

O2:  O2 in umol/kg

Sample Analysis

DIC:

Analysis Date: February 7 – 14, 2003.

Coulometers used: AOML1 and AOML2

Blank range: 12.0-29.8 counts/min

CRM # used and assigned value (include both DIC and salinity): Batch 42, c:1985.1 umol/kg, S:33.364; and Batch 43, c:1988.64 umol/kg, S:33.598.

CRM value measured:  AOML 1: offset 0.9 umol/kg (1985.99 umol/kg, Batch 42)

AOML-2: offset 2.2 umol/kg (1982.9 umol/kg, Batch 42;

offset 1.7 umol/kg (1983.4 umol/kg, Batch 43)

The average run time was 9 minutes, the minimum run time was 8 minutes and the maximum run time was 20 minutes.

Reproducibility: (# samples and average difference): 6 sets of duplicate samples, average difference 2.1 umol/kg.

CRM, salinity and HgCl2 correction applied: yes

# Remarks-

The salinity sensor did not work on AOML1.

Comments

The Sample_ID is the rosette niskin bottle number from which the discrete samples were drawn.