Cruise:  SKO0414

Ship:  M/V Skogafoss

Dates:  October 16 - 22, 2004

Chief Scientist:  not applicable

Equipment:  Surface samples collected.

Total number of stations:  VOS Underway Cruise

Sample Collection

The discrete samples were collected by Kevin Sullivan at a tap on the side of the TSG enclosure in the engine room.  The underway pCO2 instrument and the TSG were supplied with water from the flow used for engine cooling.  The water flowing through the TSG is believed to be 0.2 degrees C warmer than in-situ SST.  The date and time listed in the data file are UTC when each sample bottle was collected.

DIC:

10 locations, 20 samples each 500-ml, 8 sets of duplicate samples

Sample_ID#:  TR1 - TR20

PI:  Dr. Rik Wanninkhof

Analyzed by:  Esa Peltola

TAlk:

The samples analyzed for DIC were later analyzed for TAlk.

PI:  Dr. Frank Millero

Analyzed by:  Fen Huang

Salinity_1:

10 locations, 24 samples each 180-ml, 6 duplicates, 4 triplicates

Sample_ID#:  817 - 840

PI:  Dr. Hedinn Valdimarsson

Analyzed by:  Magnus Danielsen, Icelandic Marine Research Institute

Sample Analysis

DIC:

Analysis date: Nov 12, 2004

Coulometers used: AOML1 and AOML2

Blank range: 17.7-24.3 counts/min

CRM # used and assigned value (include both DIC and salinity): Batch 59, c:2007.1 umol/kg,S:33.316

CRM value measured:  AOML 1: offset 4.1 umol/kg (2003.1 umol/kg)

AOML-2: offset 0.5 umol/kg (2006.7 umol/kg)

Average run time, minimum run time, maximum run time:  15 min, 9 min, 20 min

Reproducibility: (# samples and average difference): 8 sets of duplicate samples, average difference 1.2 umol/kg

CRM, salinity and HgCl2 correction applied: yes

Comments

A GPS transducer was connected to the underway pCO2 instrument as well as a thermosalinograph (TSG).  The GPS and the TSG, a Seabird SBE-21, were maintained by the Ship of Opportunity Program at AOML (http://www.aoml.noaa.gov/phod/tsg/soop/index.php).

The latitude, longitude, temperature and salinity reported with the DIC and TAlk measurements were taken from the raw TSG data file.  The merging of the discrete measurements with the TSG data was done on the basis of date and time.  The TSG values are provided for reference; no post-cruise assurance of accuracy has been done to this data.  The results of the analyses of discrete salinity bottles appear on separate lines.

The Sample_ID is the sample bottle number for the discrete samples.