Calibration for fluorometer 1990:

Spectrophotometer readings

wavelength               ext. coeff.

750                      0.0054
664                      0.0521
663                      0.0517
647                      0.0513
630                      0.0177

Concentration of chla for live algal culture = 11.85(.0521-.0054) - 1.54(.0513-
.0054) - 0.08(.0177-.0054)
= 0.481725 ug/ml

Therefore, stock solution is 0.482 ug/ml
Diluted stock to 60:40 mixture of 12ml stock: 8ml DMSO

Ranges of concentrations used for calibration:
0.0289
0.0202
0.00867
0.00289
0.00231
0.00173
0.00116
0.000578
0.000145

1/Kc = concentration chla/Fb

scale           mean 1/Kc

31.6x           0.000015
10x             0.000053
3.16x           0.00017
1x              0.000053

Calibrated only on 1x door because all readings were on this door

Tau = Fb/Fa

scale           mean Tau    Tau Factor ( Tau/Tau-1 )

31.6x           1.89        2.12
10x             2.05        1.95
3.16x           2.12        1.89
1x              2.24        1.81

Equation to determine chla conc. from samples :

Conc.( ug/L ) = (1/Kc)*(Tau/Tau-1)*(Fb-Fa)*(vol extr.ml/Vol filt.L)

Equation to determine phaeopigments :

Conc.( ug/L ) = (1/Kc)*(Tau/Tau-1)*(Tau*Fa-Fb)*(vol extr.ml/Vol filt.L)

Calibration 1991:

Spectrophotometer readings

wavelength         ext. coeff.

665                1.771
750                0.325

after acid addition:

665                1.118
750                0.327

Corrected 665 values = 1.446 
after acid = 0.791

Chlorophyll a concentration = 26.7(corr. 665 before acid - corr.665 after 
acid) = 17.488 ug/ml

Range of concentrations used for calibration:

0.0525 - 0.0001749 ug/ml

1/Kc values:

door      scale         mean 1/Kc     Tau      

100x      3.16x         0.0000131     1.78
100x      1x            0.0000481     1.74
1x        10x           0.0006263     2.17
1x        31.6x         0.0001955     2.02

Almost all readings corresponded to these scales. However, there were some 
readings on other scales that were not directly calibrated. These 
concentrations were calculated using values extrapolated from the values 
obtained from the equation :

1/Kc*Tau/Tau-1

The full range of values for 1/Kc*Tau/Tau-1 is:

door       scale         value

100x       1x            .0001131
100x       3.16x         .00003
100x       10x           .0000095
100x       31.6x         .000003
1x         1x            .0116
1x         3.16x         .00367
1x         10x           .00116
1x         31.6x         .000387

Concentrations of chlorophyll a and phaeopigments were calculated using the 
same equations as in the 1990 data.

References for all Methods:

Parsons, T.R., Maita, Y. and Lalli, C.M. ( 1984 ) A manual of chemical and 
biological methods for seawater analysis. Pergamon press.

Shoaf, W.T. and Lium, B.W. (1976) Improved extraction of chlorophyll a 
and b from algae using dimethyl sulfoxide. Limnol. Oceanogr. 21, 926-928

Smith, R.C., Baker, K.S., and Dustan, P. ( 1981 ) Fluorometric techniques 
for measurements of oceanic chlorophyll in support of remote sensing. SIO 
Ref. 81-17, 14pp., Scripps Inst. of Oceanography, La Jolla, Ca.