# Webb Research Corporation

# 82 Technology Park Drive, E. Falmouth, MA 02536-4441   (508) 548-2077  FAX (508) 540-1686

USER MANUAL – APEX-SBE PROFILER

APEX-SBE INSTRUMENTS

REV DATE: 5-15-02

WRC Job no. 802

This manual applies to units with 260 cc pumps

With 05-04-02 Software (to be used with Apf 8 only)

Not to be used with Apf8b

I.	ALKALINE BATTERY WARNING	2

II.	Reset and Self Test	2

III.	Deployment	3

IV.	PARK and PROFILE Feature	4

V.	ARGOS DATA	5

A.	SERVICE ARGOS PARAMETERS	5

B.	DATA FORMAT	6

C.	TEST MESSAGE FORMAT	10

D.	FLAG BYTE DESCRIPTION	11

E.	CRC	13

F.	Conversion from hexadecimal to useful units	14

VI.	RECORDS & CALIBRATIONS	15

# ALKALINE BATTERY WARNING

The profiler contains alkaline "D" cells.

There is a small but finite possibility that batteries of alkaline cells will release a combustible gas mixture.  This gas release generally is not evident when batteries are exposed to the atmosphere, as the gases are dispersed and diluted to a safe level.  When the batteries are confined in a sealed instrument mechanism, the gases can accumulate and an explosion is possible.

Webb Research Corp. has added a catalyst inside of these instruments to recombine Hydrogen and Oxygen into H2O, and the instrument has been designed to relieve excessive internal pressure buildup by having the upper endcap release.

Webb Research Corp. knows of no way to completely eliminate this hazard.  The user is warned, and must accept and deal with this risk in order to use this instrument safely as so provided.  Personnel with knowledge and training to deal with this risk should seal or operate the instrument.  Webb Research Corp. disclaims liability for any consequences of combustion or explosion.

# Reset and Self Test

Profilers are shipped to the deployment site in Hibernate mode.  Shortly before deployment, reset the profiler by passing a magnet over the marked location on the pressure case.  The profiler will run a self-test, transmit for 6 hours with the bladder extended, and then begin its pre-programmed mission.

The six ARGOS transmissions during self-test and the transmissions during the initial 6 hour period contain data about the instrument and are outlined in  (V) ARGOS DATA, part (C) TEST MESSAGE FORMAT.

Procedure:

- Secure float in horizontal position,  using foam cradles from crate.

- Carefully pry black rubber plug out of bottom center of yellow plastic cowling to verify bladder inflation (per below).  Be sure to replace plug before deployment.

Purpose of  plug is to prevent silt entry if float contacts sea floor.

- Hold the provided magnet at RESET position marked on the hull for several seconds.

Note:  The internal magnetic reed switch must be activated (held) for at least one second to reset the instrument.  (This is to provide a safety against accidental reset during transport.)  Thus, if the float does not respond as below, the instrument was probably not reset.

- The air pump will operate for 1 second.

- The PTT will transmit 6 times at 6 second intervals.  Place the ARGOS receiver/beeper close to the antenna to detect transmissions.

- The piston pump will begin to operate.  The piston will move to the retracted Ballast Position, if not already there, pause 2 seconds and then move to full extension.

- The oil bladder will expand, this should take 15 - 25 minutes.

- After the piston pump stops, the air pump will inflate the air portion of the bladder taking 20 - 30 seconds.   Verify bladder expansion by inserting finger into hole in cowling.

- The PTT will transmit at the mission specified ARGOS rate.

- 6 hours after reset, transmissions will cease, the piston pump will retract and the bladder will deflate, the profiler begins its programmed mission.

- Reminder - replace black rubber plug in cowling hole before deployment.

During self-test, the controller checks the internal vacuum sensor.  If the internal pressure has increased above a preset limit (i.e. hull leakage caused loss of vacuum), the instrument will not pump.  If you do not detect the 6 test transmissions, and if the bladder does not inflate, then the self-test has failed and the instrument should not be deployed.

# Deployment

- RESET instrument.

- SELF-TEST starts automatically (see above).

- When piston pump stops, air pump inflates, external bladder is full, PTT will transmit for 6 hours at ARGOS Repetition rate intervals.  Normally 90 seconds.

- Six hours after reset, the piston pump will retract and bladder will deflate.  Deploy before this time is up or reset the instrument again to re-initialize the 6 hour period.  The purpose is to have the instrument on the surface and receive test transmissions.

- Pass a rope through the hole in the damper plate.

- Holding both ends of the rope, carefully lower the float into the water.

- Take care not to damage the antenna.

- Do not leave the rope with the instrument, release one end and retrieve the rope.

- The float will remain on the surface until the 6 hour interval has expired.

# PARK and PROFILE Feature

APEX floats with park and profile feature can be set to profile from a maximum depth (profile depth) after a given number of profiles from a shallower depth (park depth).

Terminology:

PARK:      intermediate depth at which the float drifts

PROFILE: maximum depth to which the float descends before profiling up.

DOWN time: spent during descent and at park depth.

UP time:  includes descent from park to profile depth (~6 hr), ascent, and time at surface.

Ascent rate: approximately .08 meters per second.

Integer multiples of “trip interval” T are used to define Up time (U x T) and Down time (D x T).   See section VI, Missions.

Total Up time is typically set to 12 to 20 hours, increasing proportional to depth and amount of data to be transmitted per profile.  Another factor is deployment location:  due to the polar orbit of ARGOS, the number of passes per day increases at high latitudes.

Parameter PD determines the frequency of deep profiles.

Schematic examples:

# ARGOS DATA

## SERVICE ARGOS PARAMETERS

The user must specify various options to Service ARGOS.  These choices depend on how the user wishes to receive and process data.  Typical parameters are listed below:

- Standard location.

- Processing: Type A2 (pure binary input; hexadecimal output)

- Results Format: DS (all results from each satellite pass), Uncompressed.

- Distribution Strategy:  Scheduled, all results, every 24 hours.

- Number of bytes transmitted:  32 per message

Note:  Webb Research strongly recommends all users to use ARGOS “Multi Satellite Service”, which provides receptions from 3 satellites instead of 2 for a small incremental cost.

## DATA FORMAT

Data is sent via ARGOS in 32 byte hex messages.  The number of 32 byte messages sent depends on the programmed quantity of temperature measurements per profile

Format for message number 1 only:

# Byte #

- 01  CRC, described in section C.

- 02  Message number, Assigned sequentially to each 32 byte message (Total number of messages per profile is shown below).  Messages are transmitted in sequential order starting with 1 and incrementing by one for the data set.

- 03  Message block number, begins as 1 and increments by one for every ARGOS message 	data set.  This, combined with the ARGOS repetition rate (section VI), allows the user to 	track surface drift.  Byte 03 will roll-over at 256 and will reset to 1 on each new profile.

- 04 & 05  Serial number, identifies the controller board number.  (This may not be the same 	as instrument number.)

- 06  Profile number, begins with 1 and increases by one for every float ascent.

- 07  Profile length, is the number of six byte STD measurements in the profile.  Total 	number of bytes of STD data from each profile depends on the sampling strategy 	chosen.

- 08  Profile termination flag byte 2 -see section D

- 09  Piston position, recorded as the instrument reaches the surface.

- 10 & 11  Pump motor time, in two second intervals. (multiply by 2 for seconds)

- 12  Battery voltage, at initial pump extension completion

- 13  Battery current. at initial pump extension completion, one count = 13 mA

- 14  Profile piston position

- 15  Surface piston position

- 16  Air bladder pressure measured in counts - approximately 148 counts

- 17  Battery voltage, with air pump running.

- 18  Battery current, with air pump running.

- 19&  20  Park temperature, sampled just before instrument descends to target depth.

- 21 & 22  Park salinity, sampled just before instrument descends to target depth.

- 23 & 24  Park pressure, sampled just before instrument descends to target depth.

- 25  Park battery voltage, no load

- 26  Park battery current

- 27 & 28 Surface Pressure as recorded just before last descent with an offset of +5 dbar

- 29  Internal vacuum measure in counts- approximately 101 counts

- 30  Park piston position

- 31  Battery voltage at Sbe pump time

- 32  Battery current at Sbe pump time

Format for message number 2 and higher:

# Byte #

- 01  CRC, described in section C.

- 02  Message number

- 03 to 32  6 bytes in sequence:

2 bytes temperature

2 bytes salinity

2 bytes pressure

Message Format and Sampling Depths

| BTYE # | MSG 1 |
| --- | --- |
| 19 & 20 | Tp* |
| 21 & 22 | Sp* |
| 23 & 24 | Pp* |
| 27 & 28 | Ps** |

| BTYE # | MSG 2 | MSG 3 | MSG 4 | MSG 5 | MSG 6 | MSG 7 | MSG 8 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3 & 4 | T1 | T6 | T11 | T16 | T21 | T26 | T31 |
| 5 & 6 | S1 | S6 | S11 | S16 | S21 | S26 | S31 |
| 7 & 8 | P1 | P6 | P11 | P16 | P21 | P26 | P32 |
| 9 & 10 | T2 | T7 | T12 | T17 | T22 | T27 | T32 |
| 11 & 12 | S2 | S7 | S12 | S17 | S22 | S27 | S32 |
| 13 & 14 | P2 | P7 | P12 | P17 | P22 | P27 | P32 |
| 15 & 16 | T3 | T8 | T13 | T18 | T23 | T28 | T33 |
| 17 & 18 | S3 | S8 | S13 | S18 | S23 | S28 | S33 |
| 19 & 20 | P3 | P8 | P13 | P18 | P23 | P28 | P33 |
| 21 & 22 | T4 | T9 | T14 | T19 | T24 | T29 | T34 |
| 23 & 24 | S4 | S9 | S14 | S19 | S24 | S29 | S34 |
| 25 & 26 | P4 | P9 | P14 | P19 | P24 | P29 | P34 |
| 27 & 28 | T5 | T10 | T15 | T20 | T25 | T30 | T35 |
| 29 & 30 | S5 | S10 | S15 | S20 | S25 | S30 | S35 |
| 31 & 32 | P5 | P10 | P15 | P20 | P25 | P30 | P35 |

| BTYE # | MSG 9 | MSG 10 | MSG 11 | MSG 12 | MSG 13 | MSG 14 | MSG 15 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3 & 4 | T36 | T41 | T46 | T51 | T56 | T61 | T66 |
| 5 & 6 | S36 | S41 | S46 | S51 | S56 | S61 | S66 |
| 7 & 8 | P36 | P41 | P46 | P51 | P56 | P61 | P66 |
| 9 & 10 | T37 | T42 | T47 | T52 | T57 | T62 | T67 |
| 11 & 12 | S37 | S42 | S47 | S52 | S57 | S62 | S67 |
| 13 & 14 | P37 | P42 | P47 | P52 | P57 | P62 | P67 |
| 15 & 16 | T38 | T43 | T48 | T53 | T58 | T63 | T68 |
| 17 & 18 | S38 | S43 | S48 | S53 | S58 | S63 | S68 |
| 19 & 20 | P38 | P43 | P48 | P53 | P58 | P63 | P68 |
| 21 & 22 | T39 | T44 | T49 | T54 | T59 | T64 | T69 |
| 23 & 24 | S39 | S44 | S49 | S54 | S59 | S64 | S69 |
| 25 & 26 | P39 | P44 | P49 | P54 | P59 | P64 | P69 |
| 27 & 28 | T40 | T45 | T50 | T55 | T60 | T65 | T70 |
| 29 & 30 | S40 | S45 | S50 | S55 | S60 | S65 | S70 |
| 31 & 32 | P40 | P45 | P50 | P55 | P60 | P65 | P70 |

*       Tp, Sp, and Pp are Park Temperature, Salinity, and Pressure values

**     Ps is surface Pressure

***   T, S, and P are Temperature, Salinity, and Pressure values

**** FFFF: Invalid data points

Data format chart above  assumes that bottom pressure (maximum hydrostatic pressure at start of profile) is 2000dbar.  Data format will change if bottom pressure varies.

APEX records a profile during ascent (ie upcast).  Bottom pressure may change due to several causes, such variation of insitu density, internal waves, float grounding in shallows, change of float mass, etc. APEX automatic depth adjustment will compensate in most, but not all, cases.

The number of sample points taken is proportional to depth, as per sample depth table below.

The first (i.e. deepest) sample is taken at the first point in the depth table above bottom pressure.

Depth Table No. 26

| Sample | Pressure | Sample | Pressure | Sample | Pressure |
| --- | --- | --- | --- | --- | --- |
| Point | (dbar) | Point | (dbar) | Point | (dbar) |
|  | Bottom |  |  |  |  |
| 1 | 2000 | 27 | 700 | 53 | 180 |
| 2 | 1950 | 28 | 650 | 54 | 170 |
| 3 | 1900 | 29 | 600 | 55 | 160 |
| 4 | 1850 | 30 | 550 | 56 | 150 |
| 5 | 1800 | 31 | 500 | 57 | 140 |
| 6 | 1750 | 32 | 450 | 58 | 130 |
| 7 | 1700 | 33 | 400 | 59 | 120 |
| 8 | 1650 | 34 | 380 | 60 | 110 |
| 9 | 1600 | 35 | 360 | 61 | 100 |
| 10 | 1550 | 36 | 350 | 62 | 90 |
| 11 | 1500 | 37 | 340 | 63 | 80 |
| 12 | 1450 | 38 | 330 | 64 | 70 |
| 13 | 1400 | 39 | 320 | 65 | 60 |
| 14 | 1350 | 40 | 310 | 66 | 50 |
| 15 | 1300 | 41 | 300 | 67 | 40 |
| 16 | 1250 | 42 | 290 | 68 | 30 |
| 17 | 1200 | 43 | 280 | 69 | 20 |
| 18 | 1150 | 44 | 270 | 70 | 10 |
| 19 | 1100 | 45 | 260 | 71 | 4 or Surf. |
| 20 | 1050 | 46 | 250 |  |  |
| 21 | 1000 | 47 | 240 |  |  |
| 22 | 950 | 48 | 230 |  |  |
| 23 | 900 | 49 | 220 |  |  |
| 24 | 850 | 50 | 210 |  |  |
| 25 | 800 | 51 | 200 |  |  |
| 26 | 750 | 52 | 190 |  |  |

*  The SeaBird CTD is not sampled at zero pressure, to avoid pumping the cell dry and/or

ingesting surface oil slicks.  The shallowest profile point is taken at either 4 dbar or at the last

recorded surface pressure plus 5 dbar, whichever value is larger.

## TEST MESSAGE FORMAT

The test message is sent whenever an I2 command is given, the six transmissions during the startup cycle, and during the six hour surface mode period prior to the first dive.  Each test message has 32 bytes, in hex unless otherwise noted, with the following format:

# Byte #

- 01  CRC, described in section C.

- 02 Message block number, begins as 1 and increments by one for every ARGOS message.

- 03 & 04 Serial number, identifies the controller board number.  (This may not be the same    as instrument number.)

- 05 & 06  Time from start up, in two second intervals (Hex)

- 07 Flag (2) byte

- 08 & 09  Current pressure, in dbar

- 10  Battery voltage

- 11  Current Bladder pressure, in counts

- 12  Flag (1) Byte

- 13  Up time, in intervals

- 14 & 15  Down time, in intervals

- 16  Interval time, in hours

- 17 & 18  Park pressure, in dbar

- 19  Park piston position, in counts

- 20  Depth correction factor, in counts

- 21  Ballast piston position, in counts

- 22  Fully extended piston position, in counts

- 23  OK vacuum count at launch, in counts

- 24  Ascend time, in intervals

- 25  Target bladder pressure, in counts

- 26 & 27  Profile pressure, in dbar

- 28  Profile piston position, in counts

- 29  Deep profile cycle counts

- 30  Month, software version number (in decimal).

- 31  Day, software version number (in decimal).

- 32  Year, software version number (in decimal).

* Flag (2)  byte:  1  Deep profile                                  **Flag (1)  byte:  1  Trip interval time

2  Pressure reached zero                                                2  Profile in progress

3  25 minute Next Pressure timeout                              3  Timer done

4  piston fully extended before surface                         4  UP/ DOWN

5  Ascend time out                                                        5  Data entry error

6  Test message at turn on                                             6  Measure battery

7  Six hour surface message                                          7  Piston motor running

8  Seabird String length error                                        8  Negative SBE number

## FLAG BYTE DESCRIPTION

Two memory bytes are used, one bit at a time, to store 16 different bits of program flow information.  Both of these bytes are telemetered in the test messages sent at startup and for the initial 6 hour surface period. Only flag byte 2 is sent in the data messages, as part of message number 1.  Bit one is set for each deep profile and bit 8 is set each time the last SBE sensor value used an arithmetic round up.

Below is a list of what each bit in each byte signifies.

bit

Flag (2) byte:   1 Deep profile

2 Pressure reached zero

3 25 minute NextP timeout

4 Piston fully extended

5 Ascend timed out

6 Test message at turn on

7 Six hour surface message

8 Seabird String length error

bit

Flag (1) byte:  	1 Trip interval time

2 Profile in progress

3 Timer done (2 min bladder deflate time.)

4 UP/DOWN

5 Data entry error

6 Measure battery while pumping

7 Piston motor running

8 Negative SBE number

The flag bytes are transmitted as two hex characters with four bits of information encoded in each character.  Each hex character can have one of 16 different values as shown in the following table.

1        0       0000				            10        9       1001

2        1       0001					11        A       1010

3        2       0010					12        B       1011

4        3       0011					13        C       1100

5        4       0100					14        D       1101

6        5       0101					15        E       1110

7        6       0110					16        F       1111

8        7       0111

9        8       1000

Bit 8 is the most significant bit and bit 1 is the least significant bit in the byte.

As an example: if a deep profile ended with the piston fully extended and ascend had timed out, then bits 1, 4 and 5 would be set in the termination byte. This binary pattern, 0001 1001, would be transmitted as the two hex characters, 19.

As another example: if a regular profile ended with the piston fully extended and the 25 minute next pressure had timed out, then bits 3 and 4 would be set in the termination

byte.  This binary pattern, 0000 1100, would be transmitted as the two hex characters, 0C.

## CRC

Because ARGOS data may contain transmission errors, the first byte of each message contains an error checking value.  This value is a Cyclic Redundancy Check (CRC), and is calculated as a function of the message content (bytes 2 to 32).

- For each message, calculate a CRC value

- Compare the calculated CRC to the transmitted CRC (byte no. 1)

- If the calculated and transmitted CRC values are not equal, the message has been corrupted and should be deleted before further data processing.

Below is a sample program (in BASIC) to calculate the CRC value for a message.  This program can be provided upon request in Basic, Fortran or C.

# DECLARE FUNCTION CRC% (IN() AS INTEGER, N AS INTEGER)

‘CRC routine to check data validity in ARGOS message.

‘Bathy Systems, Inc. RAFOS Float data transmission.

‘3 December, 1990.

‘The 1st of 32 bytes in an ARGOS message is the CRC.

‘The function CRC will compute CRC for byte 2 through 32.

‘Hasard is used for Random because Random is reserved by BASIC.

‘Stored as file CRC in C:\RAFOS\RAF11.

DECLARE SUB Hasard (ByteN AS INTEGER)

# DEFINT A-Z

# DIM in(32) AS INTEGER

‘RAF11F message number 08 HEX ID 11502 01-02-93   CRC is O.K.

# A$ = “8F00081C8E47239148A4D2E9743A1D0E070381C06030984C2693492492C964B2”

# N = 32

# FOR I = 1 to N

in(I) = VAL(“&H” + MID$(A$, 2 + I - 1, 2))

# NEXT I

# PRINT in(1); CRC(in(), N);

# FUNCTION CRC% (IN() AS INTEGER, N AS INTEGER) STATIC

# DIM ByteN as INTEGER

# I = 2

ByteN = in(2)

# DO

CALL Hasard(ByteN)

# I = I + 1

ByteN = ByteN XOR in(I)

# LOOP UNTIL  I = N

CALL Hasard (ByteN)

CRC = ByteN

# END FUNCTION

# DEFINT A-Z

# SUB Hasard (ByteN AS INTEGER) STATIC

x% = 0

IF ByteN = 0 THEN ByteN = 127: EXIT SUB

IF (ByteN AND 1) = 1 THEN x% = x% + 1

IF (ByteN AND 4) = 4 THEN x% = x% + 1

IF (ByteN AND 8) = 8 THEN x% = x% + 1

IF (ByteN and 16) = 16 THEN x% = x% + 1

IF (X% AND 1) = 1 THEN

ByteN = INT(ByteN / 2) + 128

# ELSE

ByteN = INT(ByteN / 2)

# END IF

# END SU

## Conversion from hexadecimal to useful units

The pressure is measured every 6 seconds.  Temperature, salinity and pressure are measured and stored at each point in the depth table.

Two hex bytes are stored for each sensor.  The decimal numbers from the STD sensors are converted to hex for compression in the ARGOS transmission as follows:

Temperature:	5 digits, 1 milli-degree resolution.

Salinity:  	5 digits, .001 resolution

Pressure:  	5 digits, 10 cm resolution.

To convert the hex ARGOS message back to decimal numbers:

hex 	( 	dec	=	converted	units

Temperature:	 3EA6  (	16038  =	16.038 	   C

Temperature*:  F58B  (	02677  =	-2.677		   C

Salinity**:	 8FDD (        36829	=          36.829

Pressure:	 1D4C	(	7500	=	 750.0 		decibars

Current	       0A(	    10    =	  130		  mA

Volts		       99 (	   153   =	  15.7		 volts

Voltage (V)  =  counts/10 + .4  (counts is in decimal number) nominally 15 V and decreasing.

Current (mA) = counts *13 (counts is in decimal number)

Vacuum (inHg)  =  counts *-0.209 + 26.23  (counts is in decimal number) nominally 5 inHg.

*Note regarding negative temperatures ( T (C < 0 )

Positive temperature range is 0 to 62.535C (0 to F447 hex)

Negative temperature range is -0.001 to -3.000C (FFFF to F448 hex).

If (hex value) > F448, then compute FFFF - (hex value) = Y
Convert Y to decimal = dec_Y
(dec_Y + 1) / 1000*-1  =  degrees C

**The 5 most significant salinity digits are telemetered.  The 6 digit salinity number is rounded up and converted to hex.  36.8286 rounds to 36.829 and converts to 8FDD.

# RECORDS & CALIBRATIONS

# Text boxes

PD = 2

deep profile every 2nd cycle

PD = 1

deep profile every cycle

UP time

DOWN time

Surface

DEPTH

Park

Profile

TIME