Summary of cruise AX181015 between Zarate and Durban

AX181015 was conducted aboard the Triumph Ace. I boarded the ship at Zarate on the afternoon of the October 19th 2015 and I did the installation and testing of the equipment on the next morning. One test drops was done before leaving Zarate on the 21th october. There was a low isolation problem (again) detected in engine control room, the extension electrical cord had a bad function, the chief engineer agreed to set the alarm values to higher levels.

The drops for the AX18 commenced on the 22 nd october until the ship reach 200 meters deep near Cape Town shore (aprox long. 019º 00 East) during the morning of the 31 th october.

In total 276 XBT’s were deployed. High density deployments commenced from a depth of 200m once we leave de la Plata river, the first test drop fail, no splash, no transmited, no recorded. I return to the sampling schedule (every 15km) until reach 40º West on 23th  October 10:41 am gmt time, after this stage I begun the Intermediate Density stage (very 25 km) until reach 001º East on 28th  October Finally, High density drops commenced from that point and continued until 30 th October when depth of 200m was reached near Cape Town shore. There were a few bad readings and that was the cause of hand launches at the end of cruise The humidity inide the rope store (AFT Station) it is so high the make the computers an connectors working bad.

There are four meters between the automatic launcher and the sea surface and the strong winds make the XBT wire some time touch the ship structure making the profile turn erratic.

After a couple rough sea days, the captain decide change the ship direction to 060º Sout I must the change the sample interval to one drop every 40 km and every 25 km the last stage overall the voyage went well. I had good weather for most of the trip. The Triumph Ace is an ideal ship for XBT deployments since it maintains a very steady speed and the point of release is not very far to the water resulting in few faulty drops due to launching position. The distance from the cabin to the launcher and antenna is very far too making installation a lot hard.

The Captain and crew were extremely hospitable during the crew and eager to assist during the voyage.

Luis R. yurquina

Oceanographic Department- Hidrographic Navy Service

Buenos Aires (C.A.B.A) Argentina.