## Slide 1: Launch, command and control test flight of BAE’s Coyote UAS using NOAA’s P-3 aircraft
Joseph Cione NOAA/Hurricane Research Division
Nancy Ash NOAA/AOC
Eric Uhlhorn NOAA/AOML/HRD
Sylvie Lorsolo NOAA/AOML/HRD
September 20th, 2009

## Slide 2: Coyote UAS Test Flight 090920I1
Coyote Flight 9/20/2009 Into Warning Area 174 (NW of Key West)
Mission Plan: Launch, command & control Coyote using NOAA P-3 aircraft
Three Coyote UAS were brought onboard the manned aircraft. The plan was to deploy two UAS with the third to at as a back up.
Science team members. Cione, Uhlhorn, Lorsolo (HRD); Ash (AOC); Corcoran, Osbrink (BAE Systems)
Mission Synopsis: Takeoff: 930am local out of MacDill Air Force Base
~1030am: First Coyote deployed. Parachute malfunction resulted in fast fall. First UAS test release was unsuccessful.
Coyote 2: BAE had problems with initialization. Effort aborted.
~1230pm: Began initializing Coyote #3.
Third (and final) Coyote UAS launch was a success. Release time ~1pm local
Operational plan: Fly UAS within a 3mi x 3 mi ‘box pattern’. Coyote deployed from P-3 @10,000ft . Before activating the UAS’ (electric) motor remotely, the Coyote was required to establish 5,000 ft separation with 43. After several minutes of controlled glide descent, the Coyote was fully operational @5000ft. Coyote continued descent to 1,000ft. The remainder of the flight consisted of repeated ascending and descending controlled soundings between 600-1000ft. The last 5-10 minutes of the flight included control stair-step descent from ~600ft UAS down to ~64ft.
4 GPS sondes were released during the 50-minute UAS test flight. The last drop occurred as the UAS was at ~100ft altitude. 5000 ft vertical/3-5min horizontal separation was maintained. The P-3 conducted ‘multiple spirals’ centered on the Coyote 3mi x 3mi boxed flight plan below. (Planned) ‘lost comms’ checks worked as expected.
Other issues/lessons learned:
BAE’s difficulty in attaining timely UAS pre-flight initialization. Not a straightforward process. It was however the 1st time BAE operated/worked with the P-3/AOC personnel.
Weaker than expected P-3/UAS in-flight communications. This, despite 3-5mi/5000kft minimal separation in clear air. After speaking with BAE engineers, they are confident gain can be greatly improved with a stronger antenna/receiver system. BAE says they already have a fix for this and expect no issues going forward.
Short battery life. The 50minute duration will be dramatically increased once a shorter pre-flight routine is established. Reducing/eliminating ‘up soundings’ would also increase duration. BAE also feels that increased battery power (for enhanced duration) is very possible and should not be a major issue going forward.

## Slide 4
A New (and improved) Concept of Operations for Low Altitude Hurricane Missions
….using the Coyote unmanned aircraft
Fill existing critical low altitude data void in hurricanes
    Safely provide continuous observations of T,P,V, q below 200ft
    Enhance future observational capabilities (via payload development)
Ensure safety
    No need for low level manned flight in hurricanes (i.e. below 5000ft)
    Operations fall within NOAA’s existing comprehensive ORM
    Onboard P-3 command and control maximizes efficient communication
Fully integrate with NOAA’s existing research, operational & manned aircraft assets
    Leverage existing NOAA resources (AOC, HRD, NHC, EMC, HFIP)
Complement existing NOAA-P3 onboard systems & observational tools
  Utilize existing P-3 AXBT deployment system
  Utilize existing P-3 communication systems
  Complement existing P-3 GPS AXBT/dropsonde observational systems
Minimize cost (vs. traditional deploy/launch/recover TC UAS low altitude conop)
    No forward deployment costs/teams required
    No pre-mission site survey missions required
    No complicated ground-to-plane communications required
Minimize mission and air-space regulatory risk:
    No ingress and egress

## Slide 5: Assuming we have one or more Coyotes available for testing in a Hurricane, and met instrument sensor payload development $$ becomes available soon…What’s next? 2010 LALE UAS Coyote Hurricane Demo?
(A few) Coyote UAS Mission Possibilities…
    EYE SOUNDINGS/LOITERING/EYE/EYEWALL EXCHANGE EXPTS-
    Research objectives:
      Improve understanding of TC eye/eyewall heat moisture and momentum exchange processes;
      Continuously monitor TC intensity with the possibility of capturing a rapid intensity change event. (This particular module would likely require 2-3 consecutive UAS launches)
      Improve accuracy for TC wind and pressure center fixes? Highly accurate wind center required for studies investigating radial wind/inflow.
      Mode of UAS transport: As the “launch, command and control” P-3 conducts orbits within the eye at altitude (10,000ft), the Coyote UAS could circumnavigate (r=50km) the hurricane at low altitude alternating between the the eye and adjacent eyewall regions. For the TC intensity change/monitoring/center fix modules, the UAS would remain in the eye and monitor MSLP/ locate/refine wind and pressure center locations. Occasional eye soundings up to a predetermined altitude would also be possible.
    Potential operational benefits?
    1. Unique -continuous- measurements of near-surface winds in the eyewall. Should greatly help NHC better estimate “maximum surface wind speed”.
    2. Possible early detection of a rapid intensity change process as ‘loitering’ in the eye takes place.