## Slide 1: HRD Science Meeting 8 October, 2009 Brad Klotz and Eric Uhlhorn NOAA/HRD

## Slide 2: Why?
SFMR allegedly performs poorly in heavy rain/weak-to-moderate winds
Hypothesis: Microwave absorption by rain is not properly budgeted in RTE
Obtain SFMR measurements in such conditions
10/7/2009
Notes: 2

## Slide 3
15K
10K
7.5K
5K
1.5K
5K
Notes: 3

## Slide 4: SFMR Algorithm - Improvements
1st step:
  Collocate (in time) SFMR TB to GPS dropsonde sfc-adjusted winds
    Data pairs NOAA P3's 2006-2009, some high wind data from 2005
    Calculate RR for each pair using the current model
    Eliminate pairs with RR > 1 mm/hr or RR > 25 mm/hr for winds > 50 m/s
    Solve for a new wind/emissivity function – similar to Uhlhorn et al. 2007
      Emissivity here refers to the mean excess emissivity (ɛw):
      ɛ*i = ɛwi a(fi) , where a = 1.0 + 0.15f , ɛ*i = ɛi - ɛsi
10/7/2009

## Slide 5: Rainrate Verification
10/7/2009
Need to first make sure that the data reflect the no rain condition (i.e. < 1 mm/hr)

## Slide 6: New wind/emissivity function
10/7/2009
ɛw = 6.3339E-04(Us) Us < 7 m/s
ɛw = 3.668E-05(Us)2 + 1.201E-04(Us) + 1.797E-03 7 m/s < Us < 49.7 m/s
ɛw = 3.765E-03(Us) – 8.877E-02 Us > 49.7 m/s
- R2 = 0.91
- Model difference:
(New - Old)
overall = -3.219E-03
< b1 = 8.114E-04
b1 -- b2 = -3.529E-03
> b2 = -1.097E-03