## Slide 1: REALTIME DROPSONDE DATA DECODING
Dropsonde travels horizontally as it falls,
sometimes more than 1 km.
Time from release until splash is at least
5 minutes
Synoptic scale data-assimilation assumes single time & horizontal location (launch time (1 min) / location(.1 deg)
High resolution modeling / data assimilation requires accurate time and position data in order to resolve smaller scale features
Tempdrop messages contain release and splash times / locations since 2009
Real time tempdrop messages can now be decoded in a format better suited to data assimilation

## Slide 2: Original Encoded Message Format
SONDE #062839307
UZNT13 KWBC 070726
XXAA 57077 99163 70817 04561 99007 26819 25019 00058 26419 25022
92743 21410 26020 85475 17822 26520 70119 09836 25019 88999 77999
31313 09608 80714
61616 NOAA3 WXWXA PALOMA1 OB 20
62626 REL 1625N08167W 071428 SPG 1626N08164W 071933 WL150 25021 0 85 DLM WND 25521 006644 MBL WND 25521 SST 281=
XXBB 57078 99163 70817 04561 00007 26819 11993 25819 22922 21209
33874 19633 44820 16205 55763 14250 66686 08821 77674 08443 88643
06832
21212 00007 25019 11859 27020 22808 23519 33766 27024 44714 26521
55692 24517 66675 26022 77643 25025
31313 09608 80714
61616 NOAA3 WXWXA PALOMA1 OB 20
62626 REL 1625N08167W 071428 SPG 1626N08164W 071933 WL150 25021 0 85 DLM WND 25521 006644 MBL WND 25521 SST 281=

## Slide 3
Estimate time elapsed between levels
Ptop – Pbottom / ttop – t bottom (Drop Average)
Ws = ( 2mg/CdAρ)1/2 (Hock & Franklin, 1999)
Estimate horizontal distance traveled from dropsonde measured U, V
ΔLat = U Δt ΔLon = VΔt
Calculate from surface to flight level and reverse & use average
Precision to .01 degree Lat/Lon (1km), 1 minute
Interpolation Method

## Slide 4: Decoded HSA Format
1 7. 643 18.800 81.800 1070.0 25.8 -99.0 1008.0 -12.7 -12.7 MANL
1 7. 643 18.750 81.800 1008.0 25.8 -99.0 -99.0 -99.0 -99.0 SIGL
1 7. 643 18.750 81.800 1008.0 -99.0 -99.0 -99.0 -12.7 -12.7 SIGL
1 7. 643 18.750 81.800 1007.0 25.6 89.8 -99.0 -99.0 -99.0 SIGL
1 7. 643 18.749 81.801 1000.0 25.0 92.1 70.0 -14.2 -11.9 MANL
1 7. 643 18.748 81.803 970.0 -99.0 -99.0 -99.0 -13.4 -11.2 SIGL
1 7. 643 18.748 81.803 969.0 22.4 100.0 -99.0 -99.0 -99.0 SIGL
1 7. 642 18.747 81.804 938.0 -99.0 -99.0 -99.0 -18.5 - 13.0 SIGL
1 7. 642 18.747 81.805 931.0 21.8 83.5 -99.0 -99.0 -99.0 SIGL
1 7. 642 18.747 81.805 925.0 21.6 85.6 752.0 -17.8 -10.3 MANL
1 7. 642 18.748 81.805 904.0 19.8 94.9 -99.0 -99.0 - 99.0 SIGL
1 7. 641 18.751 81.801 850.0 17.2 98.7 1481.0 -21.6 0.0 MANL
1 7. 641 18.753 81.798 826.0 -99.0 -99.0 -99.0 -20.5 1.8 SIGL
1 7. 640 18.754 81.795 813.0 15.8 94.8 -99.0 -99.0 -99.0 SIGL
1 7. 640 18.758 81.783 754.0 -99.0 -99.0 -99.0 -15.4 1.3 SIGL
1 7. 639 18.759 81.774 721.0 10.4 100.0 -99.0 -99.0 -99.0 SIGL
1 7. 639 18.760 81.771 711.0 -99.0 -99.0 -99.0 -11.8 8.3 SIGL
1 7. 639 18.760 81.768 700.0 9.6 85.2 3121.0 -10.5 7.4 MANL
1 7. 638 18.760 81.756 661.0 7.0 79.2 -99.0 -99.0 -99.0 SIGL
1 7. 638 18.760 81.750 644.0 5.6 97.9 -99.0 -99.0 -99.0 SIGL
1 7. 638 18.760 81.750 644.0 -99.0 -99.0 -99.0 -10.7 5.0 SIGL
~
P T RH GPH U V
Interpolated Time Lat / Lon

## Slide 5: Accuracy
Dropsonde trajectories (solid) vs interpolations
(one leg Paloma flight 081107i1)

## Slide 6: Status
Fortran code for decoding tempdrop message
Linux shell script to read concatenated (.xmt) files or tempdrop and call program
Output format is YYYYMMDDHHMM.hsa
Software availability in approximately 1 week (after code cleanup)
Error statistics calculations are ongoing
Future Consideration : add height observations to
significant level data