## Slide 1: Validation of Tropical Cyclone Precipitation in HWRF using Satellite Observations
Jon Zawislak, Kathryn Sellwood, and Frank Marks
HURRICANE EDOUARD (2014)

## Slide 2
Compare the distribution of model synthetic brightness temperatures with those distributions quantified at similar frequencies available from PMW sensor observations
PROJECT GOALS
Quantify biases in the organization and structure of precipitation (convection) in TCs within HWRF forecasts using simulated brightness temperatures from CRTM
Frequency distribution of TB (PCT) within some area (e.g., inner core)
Representation of common TC structures (e.g., eyewall, rainbands)
Radial and azimuthal distribution of shallow, moderate, and deep precipitation (convection)

## Slide 3
Approach: case study or composite larger sample of cases
METHODOLOGY
Hurricane Edouard (2014)
PMW Time Series of 85-91 GHz PCT
Operational HWRF initialized
0600 UTC 14 September
Community Radiative
Transfer Model (CRTM)
37, 85 GHz TB/PCT
IR TB

## Slide 4
SYN
OBS
PCT Observation
AMSR2 9/15 0549Z
24 h Forecast
AMSRE 9/15 0600Z
Compare TB
distributions within
200 km

## Slide 5
H-pol Observation
AMSR2 9/15 0549Z
24 h Forecast
AMSRE 9/15 0600Z
SYN
OBS

## Slide 6
V-pol Observation
AMSR2 9/15 0549Z
24 h Forecast
AMSRE 9/15 0600Z
SYN
OBS

## Slide 7
OBSERVATION
MODEL
Joint Distribution of 37- and 89-GHz H-pol

## Slide 8
OBSERVATION
MODEL
Joint Distribution of 37- and 89-GHz H-pol

## Slide 9
Progress towards developing a framework for comparisons (raining area, deep convective area, convective intensity)
CONCLUSIONS / LOOKING AHEAD
Identify model configurations (physical parameterizations) (and/or weaknesses in the CRTM) that ultimately reduces bias
37-GHz H-pol and 89-GHz V-pol distributions are encouraging…and still work to be done with the CRTM (37-GHz v-pol)
Framework for comparing reflectivity (precipitation structure) and rainfall rates/accumulation
Larger case sample / seasonal verification using a set of comparative products