## Slide 1: P3DWL Observation Verification
Lisa Bucci
HRD Science Meeting
March 9, 2017

## Slide 2: Background
Mounted a Doppler wind lidar to the P3 for the first time (P3DWL)
Wind profile data from the 2015 & 2016 seasons:
  TS Erika (1) Forward side-to-side sweep
  TS/Hurricane Earl (3) Conical down and up
  TS Javier (2) Conical down and up

## Slide 3: Overview
What has been done?
  Shown P3DWL obs complement TDR obs
  Qualitatively compared P3DWL obs to dropsonde
  Shown impact in analysis using HEDAS
In progress:
  Quantitatively comparing P3DWL observations to other observing platforms on P3

## Slide 4: Verification– DWL/GPS speed
Color indicates altitude in meters
y=1.0116*x + 0.5672
n=251
corr=0.9537

## Slide 5: Verification– DWL/GPS speed
Color indicates distance in km
y=1.0116*x + 0.5672
n=251
corr=0.9537

## Slide 6: Verification– DWL/GPS speed
Color indicates distance in km
5km or less:
y=1.0622*x - 0.6162
n=114
corr=0.9914
y=1.0116*x + 0.5672
n=251
corr=0.9537

## Slide 7: Verification– DWL/GPS speed
10km threshold
5km threshold
n=1200
y=0.9467*x + 1.4104
corr=0.9235
n=497
y=1.0474*x - 0.4104
corr=0.9680

## Slide 8: Verification -- DWL/GPS direction
n=497
y=0.9851*x + 4.2349
corr=0.9207

## Slide 9: Verification -- DWL/SFMR speed
n=106
y=0.9939*x + 3.3515
corr=0.8139

## Slide 10: In Progress: TDR Comparison
Still working on getting DWL data in “distance from center”
DWL
TDR

## Slide 11: Continued Verification Work
Compare SFMR to lowest DWL measurements (height varies depending scanning pattern)
Compare flight level to highest DWL winds
Comparison profiling code

## Slide 12: 2017 Season
P3DWL to be flown second half of season
  Target higher (hurricane force) wind speeds for verification
Training for operators (held at HRD) this spring

## Slide 13: Verification– DWL/GPS speed
y=0.7127*x + 7.1941
n=143
corr=0.5150
Color indicates altitude in meters