## Slide 1
SHOUT: NOAA-NASA Global Hawk Project-
Vision for the Future: Rapid Responder
Peter Black1, Gary Wick2, Jason Dunion3
1NOAA/OAR/UASPO
2NOAA/ESRL/PSD
3NOAA/AOML/HRD

## Slide 2
NASA-NOAA EPOCH Operational Demo Project
Building on recent successes with ENRR, HRR and rapid response cost reductions
Joint NASA-NOAA Hurricane Rapid Response (HRR) program
One-month: August, 2017: 6 flights, ~350 dropsondes
Collaborative with NOAA/HRD HFP Module: AIPEX (G-IV, WP-3D)
Focus on sampling hurricane inner core and near environment
Test dropsonde assimilation into NCEP/EMC TC models: HWRF and GFS in 4 steps:
  TEMPDROP TXT- mandatory and significant levels: inner sondes < 60 nm denied
  TEMPDROP TXT- mandatory and significant levels: Aberson dead-reconning
    for estimated position, no data denial.
  TEMPDROP BUFR- mandatory and significant levels with position
  Native full resolution BUFR: raw 10-m super-obed to model vertical resolution
Last will provide sonde location at all altitudes, not previously available

## Slide 3
Ongoing NASA-NSF Platform/ Instrument Hardware Upgrades
NASA Armstrong standing up second generation ‘Block-10’ platform now,
  joint with Northrop Grumman: second ‘Block-10’ in 3 years
NSF-NCAR-EOL investment in new technology: now building ‘3rd generation’
  dropsonde: NRD-41 (minisonde), RD-41 to replace NRD-94 and RD-94,
  joint with Vaisala
EOL to provide ~100 new NRD-41 sondes for testing during EPOCH
NHC to provide 60 RD-94 sondes for G-IV deployment
Result: NASA and NSF investing in NEXTGEN platform and instrument technology
  for collaboration supporting ‘Extended Response’ and ‘Backup Recco’ capability

## Slide 4
Operational Global Hawk Forecast Demo Project CONOPS
supported by EMC, NHC and OFCM Working Group (TCORF/IHC 2017): AI 16-43
Target improvements in TC intensity forecasts through improved dropsonde sampling of EMC
  ensemble model determined high uncertainty regions of the TC near-environment
Test performance of dropsondes in the TC inner core with new position information provided by
  BUFR formated data.
Collaborate with NHC-approved HRD AIPEX field program module utilizing joint flights with
  NOAA G-IV in the TC inner core to further intercompare dropsonde deployments from 12 km (GIV)
  and 20 km (GH).
Consider Global Hawk a ‘Rapid Responder’ in the NOAA toolkit for High Impact Weather such as
  Hurricanes, first and foremost, but also Winter Storms (Bombs) and Atmospheric Rivers.
Then consider use as a ‘backup’ for operational reconnaissance when multiple storms
  threaten U.S. assets simultaneously.

## Slide 5
G-IV- octagon
Total Distance: ~3200 nm
Avg GS: 420 kt
Total Duration: ~7.5 hr
Ferry Time: ~1.5 hr
Max Altitude: 44 kft
Global Hawk
Total Distance: 2640 nm
Avg GS: 360 kt
Total Duration: 7.3 hr
Ferry Time: 16.7 hr
Max Altitude: 63 kft
HRD AIPEX
+
NASA/NOAA EPOCH
Collaboration

## Slide 6
G-IV-hexagon
Total Distance: ~2960 nm
Avg GS: 430 kt
Total Duration: ~7 hr
Ferry Time: ~2 hr
Max Altitude: 44 kft
Global Hawk
Total Distance: 3080 nm
Avg GS: 360 kt
Total Duration: 8.5 hr
Ferry Time: 15.5 hr
Max Altitude: 63 kft
HRD AIPEX
+
NASA/NOAA EPOCH
Collaboration

## Slide 7
Backup Slides
AIPEX
+
EPOCH
Collaboration

## Slide 8
G-IV Module 1 Mission Descriptors:
What to Target: Sample the environment and near environment of the TC
When to Target: Every 12 h [optimal] or every 24 h [minimal], preferably in coordination with a
  corresponding P-3 mission (P-3 Module 1).
Pattern: G-IV Circumnavigation (octagon [optimal], hexagon [minimal]). Should be storm centered
  and oriented such that the left and right of shear semicircles are sampled equally by dropsondes.
Flight altitude: 40–45 kft
Leg length or radii: 200 n mi (370 km), 120 n mi (222 km), and 60 n mi (111 km) (radii). The innermost
  radii can be adjusted outward if necessitated by hazard avoidance (outer two radii rings
  should be similarly adjusted, if time allows).
Estimated in-pattern flight duration: ~ 5–6 h
Expendable distribution: Dropsonde at each turn point; 24 in total (octagon) [optimal], or 18 in
total (hexagon) [minimal].
Global Hawk SHOUT/EPOCH Mission Descriptors:
What to Target: Sample the surrounding environment and near-environment as well as the inner core
When to Target: Every 24 hours.
Patterns: Rotated Butterfly out to 240 nm (4 deg) radius or Large (4 deg) followed by rotated small
(2 deg radius) butterfly patterns.
Flight Altitude: 57-64 kft
Leg Length: Large- 6 legs of 480 nm for rotated butterfly; For large/small pattern, 3 legs of 480 nm plus
6 legs of 240 nm with rotated small inner core pattern.
Estimated on-station flight duration: 10-11 hr, 24-hr total duration including ferry (~13 hr round trip)
Expendables deployed: A total of ~60 sondes per flight will be deployed, approximately 10 per leg for
an evenly spaced sampling strategy or in an asymmetric distribution depending on convective features.