## Slide 1: An Update on the SMART Radar Observations of Hurricane Matthew
Addison Alford and Mike Biggerstaff
School of Meteorology, University of Oklahoma, Norman, OK

## Slide 2: Dataset
SMART Radar 2 (C-band, dual-pol) and KJAX dual-Doppler 3D wind retrievals
NOAA P-3 Dropsondes within dual-Doppler domain
NASA Global Hawk Dropsondes within dual-Doppler domain
OU Portable Integrated Precipitation Sensors (PIPS) data – T, Td, u, v, p, DSD (Parsivel2)

## Slide 3: PIPS Retrieval
3 Parsivel2 Disdrometers oriented differently so as to record DSDs with little wind bias as wind directions shifted.
“Composite” DSD created from quality controlled PSD (see Tokay et al. 2014). 5 m s-1 wind speed limit imposed.
DSD records were used if the 10s wind direction was ±20° from the orientation of the opening of the disdrometer.

## Slide 4: PIPS Retrieval
Results of the composite retrieval from PIPS 1A, 1B, and 2A. Times were only considered for 10 s winds less than 5 m s-1 and within 50% of the accepted fall speed. Several problems with large drops likely continue to exist and are being considered.

## Slide 5: PIPS Retrieval
SMART Radar 2 ZH
KJAX ZH
The black line in each figure is the T-Matrix calculated variable (Z or ZDR) from the PIPS and the red line is the radar derived variable over the PIPS. In the bottom panels of each figure, the difference between the disdrometer quantity and the radar quantity is shown by the blue line with the red dashed line displaying the linear trend through time.
SMART Radar 2 ZDR
KJAX ZDR

## Slide 6: Radar and Soundings
Left: SMART Radar 2 reflectivity (colors), dual-Doppler lobe (black line), radar locations (blue dot), and sounding location (blue = drop, red = ground).
Right: NOAA P3 Sounding

## Slide 7: Radar and Soundings
Left: SMART Radar 2 reflectivity (colors), dual-Doppler lobe (black line), radar locations (blue dot), and sounding location (blue = drop, red = ground).
Right: NOAA P3 Sounding

## Slide 8: Thank You for Listening! Questions?
Acknowledgements
Hui Christopherson
HRD Coordination of Dropsondes
This work was partially funded by NASA Grant 16-EARTH16F-101.
References
Tokay, A., D. Wolff, and W. Peterson, 2014: Evaluation of the new version of the laser-optical disdrometer, OTT parsivel. J. Atmos. Tech., 31, 1276-1288.