N42RF ERROR SUMMARY

H. IKE NEAR EASTERN CUBA/FERRY TO MACDILL AFB

Flight ID: 080907H

Sensor or system						Number or Name

Inertial  							INE1

Accelerometer						ACC1

Temperature Probe				                      TT1

Dew Point Probe						TDM2X (EdgeTech)

Static Pressure						PSF

Dynamic Pressure						PQF1

Vert. Wind						           GPS(Blended)

Constants File                                                                  n42_hur08v3.adc

Project Directory						/acdata/2008/hur08

Notes:

There was one data gap: 222101Z – 222104Z. Beginning with the H080829 H. Gustav flight and continuing through the H080912 H. Ike flight, there was observed a 3 to 4 second lag between all INE1 and INE2 outputs. INE1was selected since it best corresponded with the analog output.

There were no liquid water sensors available for the flight.

The APN-159 (RA159X) was inop for the entire flight. The blended GPS altitude from INE1 (ALTI1) was used.

Measured dewpoint temperature #2 (EdgeTech)...TDM2...exhibited a couple of  time periods of erroneous data during the flight.  For 000251Z – 000526Z the erroneous data was removed by substituting TDM3(Maycomm/TDL) output,

TDM2 = TDM3

For 002051Z – 002150Z  the erroneous TDM2 data was removed by substituting TDM1(Buck) output,

TDM2 = TDM1

Fuselage dynamic attack pressure (PQAF) had a erroneous data between

175801Z – 180324Z. The erroneous data was removed by substituting fuselage dynamic pressure (PQF1) output,

PQAF = PQF1

All other instruments worked optimally during the flight.

Seventeen (17) GPS dropsondes were deployed with15 being good. Four (4) tempdrop messages were sent to NHC.

Takeoff		Landing

1801Z		0127Z

Aircraft Static Pressure                   1010.0mb	1014.9mb

Corrected Tower Pressure               1011.5mb	           1015.2mb

Flight Director:	A. Barry Damiano       (813) 828-3310 ext. 3073

# Text boxes

1