N42RF ERROR SUMMARY

TS KYLE OVER OPEN ATLANTIC

Flight ID: 080926H

Sensor or system						Number or Name

Inertial  							INE1

Accelerometer						ACC1

Temperature Probe				                      TT1

Dew Point Probe						TDM2X (EdgeTech)

Static Pressure						PSF

Dynamic Pressure						PQF1

Vert. Wind						           GPS(Blended)

Constants File                                                                  n42_hur08v3.adc

Project Directory						/acdata/2008/hur08

Notes:

There was one (1) data gap: 011511Z – 011523Z.

No lag was observed between INE1 and INE2 outputs.

There were no liquid water sensors available for the flight.

The APN-159 (RA159X) was inop for the entire flight. The blended GPS altitude from INE1 (ALTI1) was used.

Measured dewpoint temperature #2 (EdgeTech)...TDM2...exhibited several  time periods of erroneous data during the flight.  For 023341Z – 023350Z, 042947Z - 043022Z and 044539Z - 044549Z the erroneous data was removed by substituting TDM3(Maycomm/TDL) output,

TDM2 = TDM3

For 214500Z – 214515Z, 221200Z – 221214Z and 042900Z - 043100Z erroneous TDM2 data was removed using statistical techniques.

For 000245Z – 000531Z  the erroneous TDM2 data was removed by substituting TDM1(Buck) output,

TDM2 = TDM1

All other instruments worked optimally during the flight.

Eleven (11) GPS dropsondes were deployed with 9 being good. Nine (9)  tempdrop messages were sent to NHC.

Takeoff		Landing

2057Z		0458Z

Aircraft Static Pressure                   1010.8mb	1012.8mb

Corrected Tower Pressure               1011.3mb	           1013.3mb

Flight Director:	A. Barry Damiano       (813) 828-3310 ext. 3073

# Text boxes

1