N43RF ERROR SUMMARY

H. PALOMA IN WESTERN CARIBBEAN SEA

Flight ID: 081107H (Second flight)

Sensor or system						Number or Name

Inertial  							INE1

Accelerometer						ACC1

Temperature Probe				                      TT1

Dew Point Probe						TDM2X (EdgeTech)

Static Pressure						PSF

Dynamic Pressure						PQF1

Vert. Wind						           GPS(MSL)

Constants File                                                                  n43_hur08.adc

Project Directory						/acdata/2008/hur08

Notes:

There were two (2) data gaps: 144100Z and 144136Z - 144514Z.

No lag was observed between INE1 and INE2 outputs.

The MSL GPS altitude from INE1 (ALTI1) was used.

Measured dewpoint temperature #2 (EdgeTech)...TDM2...exhibited several  time periods of erroneous data during the flight.  For 154110Z – 154135Z, 154408Z - 154424Z and 200421Z - 200452Z the erroneous data was removed by substituting TDM3(Maycomm/TDL) output,

TDM2 = TDM3

For 153716Z – 153722Z, 162308Z – 162320Z, 200216Z - 200221Z and

220755Z - 220832Z erroneous TDM2 data was removed using statistical techniques.

For 212412Z – 212813Z  the erroneous TDM2 data was removed by substituting TDM1(Buck) output,

TDM2 = TDM1

All other instruments worked optimally during the flight.

Twenty-three (23) GPS dropsondes were deployed with all being good but 2 sondes did quit prior to splash. Twenty-three (23) tempdrop messages were sent to NHC.

Eighteen (18) AXBTs were deployed.

Takeoff		Landing

14027Z		2217Z

Aircraft Static Pressure                   1016.6mb	1013.0mb

Corrected Tower Pressure               1017.1mb	           1013.3mb

Flight Director:	A. Barry Damiano       (813) 828-3310 ext. 3073

# Text boxes

1