## Slide 1: TROPICS Mission Implementation
Space Vehicle
Ground
Ground Network (NEN Baseline)
= NEN Sites & Coverage
= SOC @ MIT LL
= DPC @ University of Wisconsin
= MOC @ Bus Vendor Site (TBD)
Terrestrial Link
RF Link
Mission
Operations
(Bus Vendor Baseline)
Science and Payload Operations Center (MIT LL)
Data Processing Center (U. Wisconsin)
NEN = NASA Near-Earth Network
MOC = Mission Operations Center
SOC = Science Operations Center
DPC = Data Processing Center
Coverage Swath
BUS
(Commercially Procured)
Payload
(MIT LL)
TROPICS Science Team
Science Community
NASA Distributed Active Archive Center

## Slide 2: TROPICS Latency is Dominated by the Ground Station Network
Ground
Ground Network (NEN Baseline)
= NEN Sites & Coverage
= SOC @ MIT LL
= DPC @ University of Wisconsin
= MOC @ Bus Vendor Site (TBD)
Terrestrial Link
RF Link
NEN = NASA Near-Earth Network
MOC = Mission Operations Center
SOC = Science Operations Center
DPC = Data Processing Center
Coverage Swath
TROPICS is a research mission, and optimization of data latency is therefore done on as “best effort”
TROPICS will rely on two ground stations (occasionally three or four) to downlink science mission data
This results in about 6-hr average latency to the user community

## Slide 3: Other Ground Elements Add Some Latency, But Are Not Drivers
Ground
Mission
Operations
(Bus Vendor Baseline)
Science and Payload Operations Center (MIT LL)
Data Processing Center (U. Wisconsin)
NEN = NASA Near-Earth Network
MOC = Mission Operations Center
SOC = Science Operations Center
DPC = Data Processing Center
TROPICS Science Team
Science Community
NASA Distributed Active Archive Center
TROPICS will use a proven model for data networking and processing
It is highly desirable to maintain a single distribution point for simplicity

## Slide 4: Complicating Factors (For TROPICS)
Heterogeneous addition of ground stations is usually not a good solution, because of the overhead involved in folding these into the network and mission operations
“Second-order” effects are not negligible
  On the spacecraft side, there are usually implications on power, thermal, radio reliability, ground and mission ops interactions, etc.
  Conservative designs help here, and we are trying to do this where feasible/practical

## Slide 5: Thoughts and Possible Discussion Points
What is the right mix of NASA/government ground assets and those from a rapidly emerging commercial base (KSAT, Spaceflight Networks, Atlas, Globalstar, Iridium NEXT, etc.)?
How might we facilitate the sharing and homogenization of key government ground assets (NEN, NOAA ground stations, DoD ground stations, etc.)?
How can we leverage “university class” capabilities (MC3, Morehead State, etc.)
How do we think about scalability of the various assets given a potential move toward constellations?
Are there enabling technologies to consider (“Big LEO comm”, laser comm, etc.)?