## Slide 1: The expendable bathythermograph (XBT) - the biases, and their possible causes -
Shoichi Kizu
(Tohoku University, Japan)
GSOP workshop
12-14 June 2013, Hobart, Australia
On behalf of many XBT colleagues

## Slide 2
History in brief
Developed in early 1960s at the request of US Navy. Three manufacturers met
in a competition in 1965, and Francis Associates, the predecessor of
the present Lockheed Martin Sippican, won.
  “The Navy is seeking a new BT that will be more
  suitable for use aboard ASW and other vessels
  and that will improve the sonar range prediction
  capability of the fleet.” (Arthur Little Inc., 1965)
“A more specific object is to provide … a
greater depth range … with ships underway
at higher speed and higher sea state, while
maintaining flexibility of ship maneuvers.”
(Campbell et al., 1965; US patent 3221556)
TSK joined XBT business in 1970s under a license agreement with Sippican.
TSK produces several probe types basically of the same design as Sippican,
but manufacture of the two companies is independent except that they use
thermistors of the same brand, and their probes do have differences.
And, some unacknowledged manufacturers are joining... (India, China, etc.)
XBT was not developed for climate studies.

## Slide 3
・Sippican’s FRE (S65): a=6.472, b=0.00216
・IGOSS’s FRE (Hanawa et al, 1995; H95): a=6.691, b=0.00225
commonly for Sippican and TSK T4/T6/T7/DB
The fall-rate bias : early history (until 1990s)
Many works suggested negative depth bias of Sippican’s FRE for T6/T7.
20
－20
Sippican T7
Flierl and Robinson (1977)
D(t) = at – bt2
+3.36% correction to depth
Singer (1990)
“XBT wave”
Sippican T7

## Slide 4
Cowley et al. (2013)
+4%
-8%
+4%
-6%
After GK07 - Suggested histories of XBT biases
Depth
Temperature
Manu spec. (+/- 2%)
H95
Strip-chart
Strip-chart

## Slide 5: Fall rate changes with time
S65
H65
S65
H65
Sippican T7/DB probes have an slowing of fall rate from the 1990’s to now.
Slower fall rate results in warm biases
S65 = Sippican fall rate, 1965
H95 = Hanawa et al fall rate, 1995
Sippican T4/T6 profiles dominate the early records and have a slower fall rate in the mid-1970s.
Slower,
warmer
Faster,
cooler
Slower,
warmer
Faster,
cooler
Modified Cowley et al. (2013) @SOT-7
Sippican T4/T6
Sippican T7/DB
Not always similar
Newest scheme shows …
Notes: The original fall rate was set by the manufacturers and was significantly slower than the currently used fall rates.
The Hanawa 1995 fall rates were determined from XBT/CTD pairs collected during the mid 1980s to early 1990s, and we can see that both types of probes agree with the H95 fall rate during this period.
Slower means warmer

## Slide 6: “pure” Temperature bias also changes with time
The temperature bias after depth correction is highest in the pre-1990’s data.
and it’s been “positive”
The higher bias may be due to the recorder types used at the time (analog strip chart recorders were used up till the mid-1980s)
Modified Cowley et al. (2013) @SOT-7
Positive T bias remains in XBTs with pressure switches (Goes et al., 2013), too.
Sippican T4/T6
Sippican T7/DB

## Slide 7
TSK T7 shows different history of fall-rate bias (T6 does, too)
Mar 1998 (4)
Manu spec. (+/- 2%)
Mostly within +/- 2%, but in both signs.
Numbers in () are the sample size.
Aug 1998 (4)
Apr 1999 (11)
Aug 2000 (9)
Oct 2000 (5)
Jan 2001 (10)
Jan 2002 (11)
Feb 2003 (6)
Dec 2011 (3)
Jun 2012 (23)

## Slide 8
SIP
T6
SIP
T7
TSK
T6
TSK
T7
Inter-manufacturer difference:
Sippican vs. TSK, and T6 vs. T7 (recent probes)
Similar
1-1.5% different
2% different
4% different
The zero line is H95.
Recent Sippican T6/T7
fall more slowly than
H95.
Recent TSK T7 falls
more quickly than H95.
opposite!

## Slide 9
Possible causes for the biases
Depth
  Change/difference in probe weight
  Change/difference in probe structure
  Temperature dependence of fall-rates
  Launching conditions
  Strip-chart recorders?
Temperature (not originated from depth)
  Leakage
  Self-heating of thermistor
  Deck units (e.g. strip-chart, bowing)

## Slide 10
(Cowley, 2010; personal communication)
TSK T7 is heavier than Sippican T7.
Impact of variance in probe weight
The Sippican’s probe shows larger variance (batch-to-batch difference).
Manufacturer’s tolerance
Sippican: +/- 5g
TSK: +-/ 2g
740
735
730
725
Probe weight (g)
0
5
10
15
20
Sippican T7
(Tohoku)
TSK T7
(Tohoku)
Sippican T7 (CSIRO)
Frequency
10 grams
1-1.5% in fall-rates
(Kizu and Hanawa, to be published)

## Slide 11
“Hidden” differences – there’s more inside
Sippican (T4； 1992?)
TSK T6
Oct 1990
(120767)
Sep 1992
(142796)
Nov 1997
(197271)
Apr 2011
(256930)
Change in density of die cast (zinc-alloy)
Change in the inside form of the nose weight (by an effort to keep their mass constant)
They weigh the same!
but with different size of the bore.
Change in inside water flow? Change in moment of inertia?
Provided by F. Reseghetti
Could it be a cause of year-to-year fall-rate changes?

## Slide 12
Effect of launching height
from AOML’s tank experiment
Bringas et al. (2013) @SOT-7
The launching height produces some depth bias.
H95

## Slide 13
Effect of entry angle
from AOML’s tank experiment
Bringas et al. (2013) @SOT-7
The orientation of probe at launch makes small effect on depth bias.
The probes quickly turns to the straight position in the water, and also in the air when they are launched from higher position (H>3m).
25 cm
H = 1m
 = 45
H = 1m
 = 180
■ time to reach  = 0 orientation : from  = 90: 0.333 sec (50 cm)
from  = 180: 0.500 sec (75 cm)

## Slide 14
Temperature dependence of fall-rates (T7)
A test off Japan (143E)
35N
(S03)
37N
(S02)
39N
(S01)
14oC
a
b
Chart: 
| 4.8919999999999996E-3 | 2.5249999999999999E-3 | 2.2590000000000002E-3 | 1.4760000000000001E-3 | 2.751E-3 | 2.0349999999999999E-3 | 1.01E-3 | 2.8839999999999998E-3 | 3.3149999999999998E-3 | 3.137E-3 | 2.9949999999999998E-3 | 3.3180000000000002E-3
TSK T7 (S01) | 6.8096 | 6.7495 | 6.7467 | 6.6508 | 6.7664 | 6.7076 | 6.5259 | 6.7861 | 6.7354 | 6.8605 | 6.7819 | 6.8647
TSK T7 (S03) | 6.8122 | 6.9245 | 6.8269 | 6.8533 | 6.7982 | 6.8251 | 6.8374 | 6.8342 | 6.8046 | 6.849 | 6.8439 | 6.9243
LMS T7 (S01) | 6.6321 | 6.5564 | 6.5694 | 6.5482 | 6.5474 | 6.4788 | 6.5723 | 6.7127 | 6.6368 | 6.6072 | 6.6478
LMS T7 (S03) | 6.5809 | 6.5521 | 6.7574 | 6.5219 | 6.6005 | 6.6319 | 6.6016 | 6.5694 | 6.5329 | 6.645 | 6.5631 | 6.6854
Faster fall
Slower fall
XBT “feels” change of viscosity.
The time change should not be
the whole story of the fall-rate bias.
(Kizu and Hanawa, to be published)
~1%/10K

## Slide 15
Temperature dependence of fall-rates (T5)
North of KE front
(cold water)
South of KE front
(warm water)
0
30
0
1800
Kizu and Hanawa (2005b)
Temperature
Depth (m)
Cold water
Warm water
Sippican T5
TSK T5
TSK T5 showed larger temperature dependence than Sippican T5.

## Slide 16
Surface transient
Z-60-16 II (Murayama Denki)
(popularly used in Japan until ’90s)
MK-130 (TSK)
(We’ve been using this since 2000)
10m
2m
(Kizu and Hanawa, 2002a)
-1 0 1
T - TML
-1 0 1
T - TML
The transient time differs among different deck units.

## Slide 17
Bowing/Leakage
(Kizu and Hanawa, 2002b)
zero bias
XBT
CTD
Z-60-16 II
(Murayama)
Some deck units occasionally show gradual increase of positive T bias, known as “bowing”.
Sippican XBTs show leakage problem more often than TSK’s. (not shown).

## Slide 18
They weigh the same!
Can we “eliminate” the fall-rate bias?
AOML’s tank experiment
Look carefully how XBT falls. (from right to left in this video clip)
bottom
Bringas et al. (2013) @SOT-7
The XBT does not fall straight. It’s motion in the water is very complex.
surface

## Slide 19
Summary
XBT’s fall-rate has changed with time. Sippican’s probes and TSK’s probes have different histories of this bias.
The variance in probe weight can contribute to the fall-rate change. It’s impact is estimated to be about 1-1.5% / 10g.
The inter-manufacturer difference in fall-rate cannot be explained by their weight difference. This should mainly be caused by difference in their structure. (not shown)
Water temperature (viscosity) causes difference in the fall-rate. It’s impact is estimated to be about 1% for 10K.
Pure temperature bias has changed with time. It’s been positive throughout the history and most evident in the era of strip-chart recorders.
Launching height gives some impact (~a few meters) on depth bias.
Launching angle does not give major impact on depth bias.

## Slide 20: The expendable bathythermograph (XBT) - toward metadata recovery -
Shoichi Kizu
(Tohoku University, Japan)
GSOP workshop
12-14 June 2013, Hobart, Australia
On behalf of many XBT colleagues

## Slide 21
Metadata for XBT
Most important
  Manufacturer (Sippican, TSK, other)
  Probe type (T4, T5, T6, T7, DB, FD, etc.)
  Coefficients of FRE used
  Probe serial number (or Date of Manufacture)
  Deck unit (recorder)
  Launching height
Auxiliary
  Country
  Institution
  Ship
And, of course, time and position
of measurement

## Slide 22
Thank you.
Shoichi Kizu
kizu@pol.gp.tohoku.ac.jp

## Slide 23
0
-10
-20
-15
-5
-25
5
1960
1970
1980
1990
2000
2010
Boyer et al. (2011)
Impact of XBT biases on global OHC
10 23J

## Slide 24
Bias of manufacturers’ FRE for T5
The manufacturers’ FRE:
  worked well for Sippican T5, but it
  had large positive bias for TSK T5.
Then we proposed a new FRE for TSK T5:
Kizu and Hanawa (2005a)
Sippican T-5
(almost bias-free)
positive
depth error
negative
depth error
①
②
③
④
⑤
Rated depth error (2% or 5m)
TSK’s T5 is heavier
than Sippican’s T5!
TSK T5 (showing very large positive bias)

## Slide 25
TSK (nose -10g)
TSK (normal)
TSK (nose -20g)
SIP
11g lighter than TSK
Fall rate: TSK > TSK(-10g) > TSK (-20g) > LMS
Impact of weight difference
4g lighter than TSK
TSK (wire -10g)
TSK (normal)
SIP
TSK (wire -20g)
Test in 2012
Test in 2011
Manu spec. (+/- 2%)
0m
800m
Depth
50m
Depth error
-50m
10 grams = 1-1.5% in fall-rates

## Slide 26
Sippican (T7/DB)
Sippican (T4/T6)
There’s more inside
TSK T7
Sippican T7
The nose metal of Sippican T7 is not
axis-symmetric for unknown reason.
They weigh the same!
Provided by CSIRO &AOML

## Slide 27
How XBT works
wire
NOAA Photo Library
Lockheed Martin Sippican web site
TSK web site
1)
2)
3)
3)
Free fall
Ship underway
Canister
Probe
Temperature is sensed by a thermistor mounted near the front of the probe. The device has negative temperature coefficient.
The measurement starts when the probe makes contact with the seawater.
Sampling depth is not measured but is estimated by a given fall-rate equation (FRE), traditionally of the form of D(t) = at – bt2 .
D : depth [m], t： time since entry [s], a [m/s] & b [m/s2] : empirical constants.

## Slide 28
 | Speed (kt) | Range (m) | since
T5 | 6 | 1830 | ’71.8-
T6 | 15 | 460 | ’72.7-
T7 | 15 | 760 | ’78.4-
T7 (20kt) | 20 | 760 | ‘97.8-
T10 | 10 | 300 | ’79.1-
Probe types in use (as of 2013)
 | Speed (kt) | Range (m) | since
T4 | 30 | 460 | ’65.6-
T5 | 6 | 1830 | ’71.6-
Fast Deep | 20 | 1000 | ’91.9-
T6 | 15 | 460 | ’68.4-
T7 | 15 | 760 | ’67.6-
Deep Blue | 20 | 760 | ’81.4-
T10 | 10 | 200 | ’72.3-
T11 | 6 | 460 | ’06.2-
TSK
Sippican（LMS)
Rated accuracy: Temperature +/- 0.2K, Depth +/- 5m or 2%.
Common FRE
T4(?) 30 460 ?
America, Europe, Australia, etc.
Japan and some Asian countries

## Slide 29
H95
A typical comparison between recent Sippican T7 and TSK T7 (Kizu et al., 2011)
Manu spec. (2%)
Depth (m)
Depth (m)
Depth error (m)
Sippican (dashed)
TSK (thin solid)
Sippican: positive depth error TSK: negative depth error
positive error
= slower fall
Sippican
TSK
CTD (thick solid)
negative error
= faster fall

## Slide 30
T7 XBT
Structure of XBT (T7)
1st line: probe weight in air
2nd line: probe weight in water
(Kizu et al., 2011)
After-body (incl. wire spool)
LMS
TSK
51.0g
(2.9g)
52.1g
(2.8g)
LMS
TSK
729.1g
(564.1g)
740.5g
(576.5g)
Total
12g
(2%)
Nose weight
LMS
TSK
575.6g
(484.7g)
575.2g
(485.1g)
Probe wire
LMS
TSK
101.9g
(76.5g)
113.0g
(88.6g)
12g
(
Same gauge, but different coating

## Slide 31
a
b
(x103)
a, b coefficients
Sippican： a=6.472, b=0.00216
H95： a=6.691, b=0.00225
Faster fall
Slower fall
TSK T6 falls more slowly than TSK T7 by 1-1.5%.
TSK T6
TSK T7

## Slide 32
Surface transient
(Kizu and Hanawa, 2002a)
Z-60-16 II
(Murayama)
MK-130
(TSK)
Z-60-16 II
(Murayama)
Z-60-16 III
(Murayama)
2m
10m
10m
4m

## Slide 33
Surface transient
MK-130
(TSK)
MK-9
(TSK)
MK-12
(TSK)
(Kizu and Hanawa, 2002a)
2m
2m
2m

## Slide 34
Sippican： a=6.472, b=0.00216
H95： a=6.691, b=0.00225
a
b
(x103)
a, b coefficients (TSK T6)
Faster fall
Slower fall
Oct 1990 (11)
Nov 1990 (11)
Jul 1991 (7)
Sep 1992 (22)
Jun 1995 (11)
Nov 1997 (9)
Jun? 2012 (22)

## Slide 35
Sippican： a=6.472, b=0.00216
H95： a=6.691, b=0.00225
a, b coefficients (TSK T7)
a
b
(x103)
Faster fall
Slower fall
Mar 1998
Aug 1998
Apr 1999
Aug 2000
Oct 2000
Jan 2001
Jan 2002
Feb 2003
Dec 2011
Jun 2012