## Slide 1: Argo and SOOP XBT Recent Activities and Results
Frederick Bingham
Kyla Drushka
Information for this presentation obtained from D. Roemmich and G. Goni (via R. Perez!)

## Slide 2: Argo: Basic Facts
US Argo supported by NOAA, includes a 5-institution consortium and a data assembly center
US Argo activities include tech development, commercial acquisition, deployment and logistics, comms, data management, data analysis, international coordination and outreach
US operates 1890 of 3854 currently deployed floats

## Slide 3: Argo: Basic Facts
Present coverage

## Slide 4: Argo: Recent Advances
Development and early deployment of Deep Argo (see Renellys’ talk)
More biogeochemical sensors
Major format change to Argo netCDF files to accommodate different types of sensors
Several gridded Argo products are available (MOAA GPV, Roemmich and Gilson, MIMOC, etc.)
More use of iridium communications (minimizes surface time, allows two-way control of float missions)
Deployment from non-traditional platforms (e.g. sailboats)
Schooner Lady Amber
>100 floats

## Slide 5: Argo: Future Plans
Enhanced spatial coverage in marginal seas, WBCs, equatorial regions, high latitudes (~4135 floats)
Implementation of Deep Argo
Continued development and deployment of BGC sensors

## Slide 6: Argo: Synergies between Argo and other observing system elements
SSH and altimetry
Repeat hydrography. Complementary sampling and cross-calibration
Drifter network. Complementary estimates of dynamic topography
Tropical moored array. Estimates of subsurface variability
SSS – ground truth
SST
Mannshardt et al., 2015

## Slide 7: Argo: Accomplishments
2038 Research papers based on Argo
Global change assessment
Use in data assimilation models
Education

## Slide 8: Argo: Challenges
Sustaining core array under level or decreasing budgets
Deployment inside EEZs and other restricted areas
Deployment priorities. Polar oceans? Regional seas?

## Slide 9: XBT Network: Basic Facts
The XBT Network is an international program dedicated to the implementation, maintenance, enhancement, and data management of upper ocean measurements from XBTs
Science objectives: meridional heat transport, current variability (esp. WBCs), upper ocean heat content, model initialization and validation

## Slide 10: XBT Network: Distribution
28 active transects
Red = Active US

## Slide 11
XBT transects are sampling:
Western Boundary Currents:
Kuroshio (3 transects)
Gulf Stream (3 transects)
Agulhas Current, rings
Brazil Current, rings (2 transects)
East Australian Current (2 transects)
East Auckland Current and Tasman Outflow
XBT Network: Boundary, surface and subsurface currents
: Boundary currents sampled by the XBT Network
Multiple transects across one current provide critical information on spatial changes in the structure
Eastern boundary currents: California Current, Alaska Current, Leeuwin Current, …
Low latitude WBCs: Solomon Sea, Indonesian Throughflow
Equatorial System: NECC, NEUC (2 transects)
High latitude: Antarctic Circumpolar Current (3 transects)

## Slide 12
South and North Atlantic Meridional Overturning and
Meridional Heat Transport
  AX07 (North Atlantic): Started in 1994 (21 years)
  AX18 (South Atlantic): Started in 2002 (13 years):
  42 Realizations
  11,000 XBTs deployed
  First sustained observations in the South Atlantic to monitor MOC/MHT, and Brazil-Agulhas Currents
  Quarterly reports of MOC/MHT
  Carried out ocean experiments to determine optimal sampling
http://www.aoml.noaa.gov/phod/soto/mht/reports

## Slide 13: XBT Network: Recent Developments
Transition to Iridium communications
Redesign of autolaunchers, new data acquisition software
Program managed with international cooperation (US, Germany, France, Japan, …) by the SOOPIP
Important long-term datasets (10+ years)
Are the current transects the best ones to do?

## Slide 14: Deep Argo: Basic Facts
Systematic ocean observations > 2000 m are limited to ship-borne measurements sparse in time and deep moored arrays of confine spatial coverage
Coverage is not sufficient to describe the mean ocean circulation in many regions or the decadal property variations
Deep Argo Workshop
  May 5-7th, 2015 in Hobart, Tasmania
  30 participants, 6 countries
  U.S., France, U.K., Australia, New Zealand, Japan
  Information for this presentation obtained from N. Zilbermann and the Deep Argo workshop steering committee (Dean Roemmich, Susan Wijffels, Nathalie Zilberman, Guillaume Maze, Steve Riser, Toshio Suga, Katsuro Katsumata, Breck Owens, Greg Johnson, Brian King, Bernadette Sloyan)

## Slide 15: Deep Argo: Motivation
Deep ocean > 4000 m heat uptake equivalent to 0.027 Wm-2 (~5 ZJ decade-1), about half of the ocean below 2000 m
Regional signals > 4000 m are much larger
50% of the ocean volume is at depth > 2000 m
12% of the ocean
volume is at depth > 4000 m
Deep ocean warming > 2000 m
intensified
below 4000 m
Purkey and Johnson, 2010
Purkey and Johnson, 2010

## Slide 16
Operational application
Improve global ocean reanalysis and coupled ocean-atmosphere forecasting systems below 2000 m (assimilation, constraint, OSSEs, removal of deep bias)
2. Basic research
Significant progress in global heat budget and freshwater storage
Improve knowledge of regional distribution of regional sea level budget, and quantification of the causes of sea level change
Provide basin coverage of deep ocean circulation
Resolve abyssal decadal signal changes locally not just globally
Many other research topics (mixing, ice melting, TS structure, ...)
3. Mutidecadal climate change assessment
IPCC AR5, BAMS state of the climate reports, ...
4. Education (as demonstrated for Argo)
Deep Argo: Value

## Slide 17: Deep Argo: Float models
Deep NINJA
TSK Co LTD, JAMSTEC
0 – 4000 m
SBE-41 CTD
50 kg
15 deployed so far
Deep ARVOR
NKE, CNRS, IFREMER
0 – 4000 m
SBE-41 CTD
26 kg
4 Prototypes deployed
Deep APEX
TWR, UW
0 – 6000 m
SBE-61 CTD
43 cm glass sphere
2 Prototypes deployed
Deep SOLO
SIO
0 – 6000 m
SBE-61 CTD
25 kg
33 cm glass sphere
3 Prototypes deployed

## Slide 18
Technical aspects of Deep Argo floats under discussion
Cycle time – aim for array refresh time of 5 years (15-day cycle)
Collect data during ascent or descent
Parking depth. Bottom landing
Vertical resolution of profile
CTD accuracy requirements: ±0.001°C, ±0.002 salinity, ±3 dbar)
Meeting temperature accuracy goal, working towards salinity and pressure goal.
Deep Argo float cycle
Measure temperature and salinity during descent or ascent
Descend to 4000-6000 m or near bottom if shallower
Parking depth at 1000 m
Deep NINJA
Deep
Arvor
Deep SOLO
Deep Apex
Parking depth at 3000-5500 m
Deep Arvor Deep NINJA
Deep SOLO
Deep Apex
Cycle time

## Slide 19
Deep Argo
2000 m
Core Argo
4000 m
A Workshop was held to discuss technology developments for Deep Argo, scientific and operational rationales, and plans for future work
4 designs of Deep Argo floats have been developed and tested with depth ranges of 4000 m and 6000 m
A Deep Argo CTD has been developed by SBE in collaboration with NZ/US/Aus. Argo and deployed in shipboard casts and float profiling, with encouraging results.
Regional pilot arrays of Deep Argo floats have begun and will continue in 2015-2016 in the Southern Ocean, SW Pacific, and North Atlantic
Deep Argo: Recent Developments

## Slide 20
15 Deep NINJA deployed in 2012-2014
3 Deep NINJA in 2015
Engineering test (3,Pacific Ocean), water mass formation and deep MOC (12,Southern Ocean)
2 Deep SOLO in 2014
8 Deep SOLO, 2 Deep Apex in 2015
Deployment opportunity in 2016 (R/V Investigator, CSIRO, P15S)
Flat abyssal plain w/ substantial deep warming, limited eddy activity
Southwest Pacific Ocean
2 early (3500m) Deep Arvor in 2012-2013
2 Deep Arvor prototypes (4000 m) in 2014
9 Deep Arvor in 2015
North Atlantic deep water formation rates and characteristics
North Atlantic Ocean
North Pacific Ocean and Southern Ocean

## Slide 21
Deep Argo: Straw Plan
Plan: 2-3 year pilot arrays before global implementation
Sample to the ocean bottom (up to 6000 m)
5° x 5° spacing: ~1200 floats, based on decorrelation statistics
Start at high latitudes (deep-ocean warming signal) -> equator -> global
Challenges: Funding, CTD technical challenges, float endurance, leverage international collaboration between partners
Greg Johnson