## Slide 1: Realtime Dropsonde Processing with ASPEN (revised June 1, 2022)
ASPEN dropsonde processing on the aircraft is done on the Linux Centos operating system. If you are working remotely, the version of ASPEN for your operating system will have some minor differences in the configuration tabs and processing windows.
Current ASPEN version is V3.4.7
Start a new dropsonde log sheet for each flight and make sure you have the correct flight number and mission ID.
ex. Flight ID - 20220601H1 Mission ID - 0101A Alex
Get the mission id from the flight director. It will be inserted into the tempdrop in the WMM app but you should confirm that it is correct before transmitting the first drop.

## Slide 2: Setting up the work-station
Create directories on the desktop for ASPEN to grab the raw “D” files and to save output. Include the flight ID in the folder names, for example 20220601H1_ASPEN_DATA and 20220601H1_RAW_DATA.
The workstation allows you to easily navigate between 4 different desktops. Take advantage of this feature to organize the different applications you will be running. A sample configuration is given below.
Window 1 : Use for communication and monitoring of in-air dropsonde and flight-level data
XCHAT, Remote AVAPS, screen 800, KARMA
Window 2: Use for dropsonde processing
ASPEN, AVAPS_PRIMARY, flightid_RAW_DATA directory
Window 3: Use for dropsonde transmission
WMM APP, flightid_ASPEN_DATA directory and FRD directory
Window 4: internet – use sparingly
You should be constantly watching the first window for new d-files to process and be available via XCHAT. Use the headset to monitor and make note of dropsonde launch times and status and communicate with the crew.
You may need to “Enable AVAPS Shares” by clicking the icon on the desktop
Ask data tech for help if drops are not showing up in AVAPS_PRIMARY
****** if workstation freezes up restart and reconfigure to only use 2 or 3 desktops

## Slide 3: HRD Stations
Dropsonde seats
LPS & Radar
*** Read safety placards for ditching info
*** Ensure you have a Switlik and gas mask behind your seat
*** Check manifest for duty/station assignments

## Slide 4: WORK STATION Dropsonde related apps are circled

## Slide 5: Data Display Application (Screen 800)
Allows you to look at data from all the instruments on the workstation. There is a document in the flight bag with details about the available fields and variable
names. Video terminals or Ipads are mounted in front of some workstations, radar channels
are 13, 14 and 15; flight level channels are 4 and 5

## Slide 6: SETTING UP AND CONFIGURING ASPEN
If you are on the aircraft, delete the sounding file from the previous flight before opening ASPEN. It is located in /home/hrd/soundings.sqlite
Correct version of ASPEN for 2021 is 3.4.7
Click on ASPEN logo (not batch ASPEN) to open ASPEN – You will see this window
Click “OK” to create a new database file, unless you are restarting ASPEN mid-flight. In that case browse to the location of Soundings.sqlite on your computer. This is the data base that ASPEN will use to create the synoptic plots.
After the correct file name/location appears in the window Click “OK”

## Slide 7: Next you will see this window
Click “cancel”
After configuring, following the next few slides, the correct flight directory should appear in this window when you go to open a D file.

## Slide 8
Now make sure ASPEN is configured correctly
Click on File / configuration
Select editsonde then click on “Edit” button
On other systems the tabs may be edit /options or tools /configuration or ASPEN/preferences
You may get a pop-up window with “Invalid Fixed Data Source”
Click “OK” to close this window
Follow the next 6 slides to complete configuration.
“Editsonde”

## Slide 9: Go Through all the Tabs From Left to Right First Tab: “QC Parameters”
You should not have to
change anything here but
always check anyway
The values shown are correct.
They will probably differ from
what is in the ASPEN users
guide.
Make sure that the box for
“Pressure Monotonic Check”
is not checked. Click on it
to uncheck if necessary.
New value for Buddy Check Slope as of 2019 is 10m/s2
New value for Number of Satellites Limit = 6
New value for Wind Error Limit 1.5m/s >10km or <100m else 1m/s
Boxes checked are “Dynamic Correction” “Disable Outlier Check” and “Disable QC Filter”

## Slide 10: Next Tab: “Processing” (where you set your input directory)
---Set input Directory
Under “Fixed data Source”
check “Enabled” and
“Change”
Browse to your “RAW_DATA”
directory
---NEW add metadata
Project = Storm Name
Platform ID = Aircraft ID
Flight IOP = flight id
--- QC Processing set to Normal
Levels checked
WMO message checked
---Check
Dropsonde hit surface
Discard Frames with CRC
errors
Use Theoretical fall speed

## Slide 11: Next Tab: “WMO”
You should not have to
do anything in this tab,
just confirm that “TEMP”
is checked.
Correct values for Atlantic
Basin are shown here

## Slide 12: Next Tab: “Auto Save” (where you set your output directory)
Click “Auto Save Enable”
Click “Change” and browse to your ASPEN_DATA directory
Check
WMO bufr (.bfr)
WMO Text (.txt)
Levels (.csv)
NOAA FRD (.frd)
NetCDF (.nc)
PNG (.png)
Summary.txt

## Slide 13: Next Tab: “Synoptic Map” (set name for synoptic plots)
The geographical database
default location may
not be set correctly. If not, click
“change” and browse to
the correct location in
“ASPEN/ Geodata/ne1to50.sqlite”
The sounding database
is “soundings.sqlite” which was
created when you opened ASPEN
Synoptic Map Title is what
will appear at the top of the
figures and in their file names.
Suggested name is
“flightID_SynMap “

## Slide 14: Next Tab: “Visual” (adjust setting for Skew-T diagrams)
Set Plot Range
P-3
---10,000ft.
10 – 40 C
650 – 1050 mb
---20,000ft.
-10 – 40 C
400 – 1050 mb
G-IV
-40 – 40 C
100 – 1050 mb
Click “OK
***** You may need to reset in flight if altitude changes significantly
”

## Slide 15: ASPEN will go back to configuration window …. Click “OK” to complete

## Slide 16: Start a dropsonde log
Get the flight and mission ID’s from the Flight Director and AVAPS operators from the seating chart then complete the checklist:

## Slide 17: Update the Dropsonde Log
Note take off and
landing times/locations
Keep track of drop
status via the headset
(or XCHAT if on ground)
Fill in Metadata
-get the first 5 columns
from the “MAIN” tab
-get surface wind from the
“WMO” message
-get last wind height from
the “Levels” tab)
Enter SST for Combo drops
with AXBT, and
identify center, Eyewall and rainband
drops with quadrant info.
Use the comments sections to note anything interesting in the sounding or extra QC you
did to sonde (ie. Reset end time, removed flight level RH)

## Slide 18: Processing Sondes
Drag D-files from AVAPS_PRIMARY/flightID
to your flightID_RAW_DATA directory.
ASPEN will automatically go to your flightID_RAW_DATA
directory when you click “open”.
Click on the sonde that you want to process,
working in chronological order.
You should be keeping track of sondes by writing
down the launch times and locations in your log as you
hear them called over the headset.
Inform the AVAPS operator if a sonde does not appear
in AVAPS_PRIMARY/flightID shortly after splashing
Lat/Lon should be reported in degrees + fraction (some
navigation sources on the aircraft use degrees + minutes)

## Slide 19: Main Tab
Check the Launch parameters.
Ignore (check) Temperature, RH, Wind Speed and Direction.
Never ignore Pressure, Altitude, Latitude or Longitude (get correct value from raw data if necessary.)
Compare upward and downward integrated heights with altitude and pressure.
If ,after examining the data you determine that the sonde did not transmit to the surface, check “set heights missing”. Ensure that “hit surface” and “recompute” are checked when processing the next drop.
(!) Click if you change anything
Get unique sondeid
You can get Lat/Lon for your
logsheet here.
Drop time may give indication of
whether sonde transmitted
to surface, if fast fall or post-splash
data ( ~10m/s fall speed )

## Slide 20: Use the Raw tab to perform manual QC.
Check Flight Level data on the first line and compare with first good data line
Check for increasing temperature and pressure and decreasing altitude
Check last line to confirm surface transmission
Look at bottom GPS altitude and surface pressure.
Check for extra data lines at the bottom of the sounding
Mouse over QC indicators for explanation of flags

## Slide 21: Use XY Graph to Look at individual fields
Data should be smoothly varying through sounding
Compare first few data points to ensure PTH
sensor reached equilibration.
Check for wind drop-outs (Spd-dir) as nearby
data points may need to be removed. Note any
interesting features in the droplog.
Check near surface winds for unphysical increase
in wind speed.
Check for slow/fast fall, if so all winds should be removed.
Fall speeds should be 10-12 m/s from 700mb. GIV sondes
will start out at a higher fall speed (~20 m/s_
Play around with the plotting features on your first
sonde to see what graphics are available and which
might be most helpful to you.
You can toggle between raw and QC data or plot the levels
reported in WMO message.
New feature allows you to look at lat/lon

## Slide 22: Switch to “Time” Y axis and zoom in to better locate data points

## Slide 23: Select Data to Remove or Retain in RAW Tab
Left click to highlight data
Use shift button to select a
column of data
Right click to ignore (remove) data
or keep flagged data
If wind speed, temperature, or latitude
are kept/removed then wind direction,
RH, and longitude should also be
kept/removed
Click “recompute” ( ! ) to save changes
If data is recorded after sonde splashes
select the correct frame to setend time
and check that it is changed in the main
tab.
If bottom pressure and GPS altitude
lead you to conclude that sonde did
not transmit to surface go back to the
main tab and set heights missing and “!”.

## Slide 24: Look at QC Tab to See Changes
Flagged data will be removed
Surface atlitude will be set to “0”
Smoothing and Dynamic Adjustments will be applied
When data is removed manually, some previously flagged data may be retained.
Look at XY plots again to ensure that all corrections have been applied properly
Geometric altitude reported in QC – no value for Geopotential height
RAW
QC

## Slide 25: Skew-T tab is Visual WMO Message
Toggle between raw and QC to see
what data is removed.
Check for Temperature equilibration
at the top of the sounding.
Plot “levels” to look at the actual data
which will be transmitted
Look at the wind barbs
You can go back and reconfigure
the plotting parameters if the
ranges are not optimal.

## Slide 26: Check the Mandatory Levels data (Levels Tab), note surface values for dropsonde log.

## Slide 27: Remove a level by clicking on it so it is highlighted in red. This will only fix the WMO message and not the bufr data.

## Slide 28: Use the Summary Tab as a final check after making changes and before transmitting

## Slide 29: Use the COMM Tab to make Tempdrop Comments Section
Designate Environment
Indicate azimuth if
Eyewall or maxwind
Click on “Last Report”
when sending the final
tempdrop (confirm with
FD first)
Enter observation
number (sequential)

## Slide 30: Check the tempdrop in the WMO Tab before transmitting
Look over WMO before sending out
Make sure that REL and SPG are included – if not you may need to set the end of the drop
a couple of lines earlier to get a splash location.
Check that environment information is included if applicable and that it is correct
Check the surface data (99 data group on XXAA line)
Manually add 3 digit SST from at the end of the comments section, before “=“ if there was a
concurrent BT drop and save the WMO message to the correct folder
**** If either environment or SST added you must manually save the WMO message
**** Click File/save or icon browse to correct directory and save
**** You will be prompted to overwrite the old message if in the correct directory

## Slide 31: On the P3 use the WMM Application to transmit the tempdrop messages
Click on the icon to open WMM
Click “Load Tempdrop” and
browse to WMO message.
Check the message for errors a
final time.
If this is the first drop,check the
mission id on 61616 line
Click “Send Message”
Repeat process for bufr file
The tempdrop and bufr file
should now appear in Pending
Messages
Once a tempdrop is sent off the
plane it will move to sent
messages and be given an OB#an ob #
– note the ob # in your log

## Slide 32
WMM MODULE STANDARD VIEW: Flight-level data scrolls in real-time

## Slide 33
BROWSE TO SELECT MESSAGE TO TRANSMIT

## Slide 34
AFTER SENDING A TEMPDROP OR BUFR MESSAGE IT WILL APPEAR
IN PENDING MESSAGES (file name includes “snd”)

## Slide 35
AFTER TRANSMISSION, TEMPDROP AND BUFR MESSAGES WILL APPEAR IN
SENT MESSAGES HERE IS WHERE YOU GET THE OB# FOR YOUR LOGSHEET
THIS IS ALSO WHERE YOU FIND PREVIOUSLY SENT MESSAGES TO CORRECT

## Slide 36
Create Synoptic Maps at then end of each flight:
Click on globe icon to open synopic mapping
Click “Plot All”

## Slide 37
Use the mouse to zoom in on flight location
Save all levels using the “File” tab or disc icon
Browse to FlightID_ASPEN_OUTPUT directory before saving

## Slide 38: Saving Edited ASPEN output
Check your output directory to make sure that files are saved there (WMO, .frd, .nc, .bfr and skewTs)
Copy WMO .frd .bfr and skewTs to “FRD” data folder on the desktop. Files will automatically be ftp’d to the ground from there.
Do not drag and drop as files can get accidentally deleted
Check that files in FRD folder have been sent ( they will move to the “sent” folder
Create synoptic Maps
At the end of the flight tar and zip all raw and processed dropsonde data
It doesn’t hurt to re-copy files to FRD folder if you are unsure that all data was sent
Copy data to Google drive folder if you have time
Location for 2022 Field Program ……
https://drive.google.com/drive/u/1/folders/1XAgc_PV_ZhH1FGxBTHgEHpC27E6tzzL8

## Slide 39: Sending a corrected tempdrop
ON THE AIRCRAFT:
Within the WMM application go to “Sent Messages
Select the original tempdrop and click on the “correct” button
Using your new WMO message manually make the corrections to the original message (copy corrected fields over)
The software will keep track of the observation number and add “CCA” as needed
When you are sure that the message is correct press “send”
FROM THE GROUND:
manually edit the corrected WMO message so that the section beginning with 61616 has CCA OB # appended before the “=“ using the original observation number.
You will have to do this twice, once for each 61616 line
If you have to send the same drop corrected again use CCB the second time then C, D etc. if further corrections are sent.

## Slide 40: Set end of drop ~ 25% of sondes Most times ASPEN will provide a warning
Determine last good level
Altitude values can help
Right click and select “Set end
of drop time”
Recompute (“!”)
If post splash appears to have
a good SST note in your log

## Slide 41: Remove erroneous data or unflag good data in raw tab
8 seconds of bad lat/lon data
Left click on bad data (use shift button to mark multiple levels)
Right click to select “Set Ignore Attribute”
Recompute (“!”)

## Slide 42: Fast fall – Partial Fast fall
Normal fall speed is ~10-12 m/s
Fast fall winds should automatically be
removed
Temperature and humidity data can be
transmitted if it looks okay
Need to remove all winds if ASPEN does not
May be able to keep some winds if it is only a
partial fast fall
FAST
FAST
GOOD
GOOD

## Slide 43: Late Launch Detectdata
ASPEN should automatically identify
late launch detect and reset correctly.
Make note of the times in the pop-up window
Confirm correct LAU by examining the
D file.
override lat/lon using data from
D-file
Click “No” in the pop-up window when closing the sonde to keep from re-setting the configuration

## Slide 44: Satellite drop outs Since there are no surrounding data points after satellite dropouts ASPEN may miss some bad data. You will need to remove these points manually in the raw tab.

## Slide 45: Early Launch detect
ASPEN now has the ability to identify and correct ELD sondes
Override lat/lon in main tab using value from D-file
Remove first 10 seconds of wind data
Remove first 5 seconds to T and RH
Recompute (!)
When closing the sonde click “No” in the pop-up window
In some cases, ELD can only be fixed by editing the D-file
( kids don’t try this at home)
Undiagnosed ELD may be identified by high/constant pressure at top of sounding

## Slide 46: Edit Tempdrop to add SST
Click on last line in 62626 section to change then “modify
Add SST in 10ths of degrees Centigrade before “=“

## Slide 47: SST of 28.5 degrees from BT manually added to WMO message at end of “62626”
KDENUZNT13 KWBC 050848
XXAA 55082 99249 70730 08043 99009 29257 12024 00081 28457 12526
92769 23245 12535 85505 19036 14533 70149 09425 15525 50587 03957
10522 40760 14746 13027 30973 28966 12516 25100 39957 11005 20248
521// 25010 88999 77168 31063 458//
31313 09608 80826
51515 10190 15429
61616 NOAA9 2214A MATTHEW OB 11
62626 MBL WND 12029 AEV 33297 DLM WND 13522 008161 WL150 12027 08
0 REL 2491N07301W 082629 SPG 2497N07307W 084127 SST 285 =
XXBB 55088 99249 70730 08043 00009 29257 11865 20256 22850 19036
33764 14447 44579 00210 55527 00756 66458 07157 77370 19322 88342
21758 99332 22168 11245 40958 22228 45341 33205 51158 44161 625//
21212 00009 12024 11985 12030 22923 12535 33892 13530 44850 14533
55747 13526 66688 15523 77640 14023 88574 14530 99514 10022 11484
11520 22476 10018 33430 13032 44402 13028 55376 10522 66346 14525
77319 11016 88278 14019 99242 00000 11196 24510 22171 29014 33170
30024 44168 31063 55161 29010
31313 09608 80826
51515 10190 15429
61616 NOAA9 2214A MATTHEW OB 11
62626 MBL WND 12029 AEV 33297 DLM WND 13522 008161 WL150 12027 08
0 REL 2491N07301W 082629 SPG 2497N07307W 084127 SST 285 =

## Slide 48: ASPEN_TRAINING FILES ON AOML FTP SITE AND GOOGLE DRIVE
Google Drive: ASPEN_TRAINING_2022
CONTAINS:
This Powerpoint
ASPEN_AVAPS_OVERVIEW Powerpoint
PDF and Word Dropsonde Log Sheets
P3_DROPSONDE_PROCESSING_2022.docx :Detailed instruction for processing dropsondes
on the aircraft using ASPEN software
Training_sondes.docx: Guide sheet for processing practice and test dropsondes
Directory TRAINING_SONDES : Contains the raw D-files used in this training and listed in
document Training_sondes.docx
Directory TEST_SONDES: Contains raw D-files and a logsheet , you will need to demonstrate
ability to process these sondes correctly to qualify as dropsonde
scientist for operational missions
on Google Drive