## Slide 1
Bachir Annane1, Brian McNoldy2, Mark Leidner4,
Robert Atlas3 , Ross Hoffman1,Sharanya Majumdar2
1 Univ. of Miami/CIMAS and NOAA/AOML/HRD, Miami, FL
2 Univ. of Miami/RSMAS, Miami, FL
3 NOAA/AOML, Miami, FL
4 AER, Lexington, MA
Impact of Simulated CYGNSS Ocean Surface Winds on Tropical Cyclone Analyses and Forecasts in a Regional OSSE Framework

## Slide 2: What is CYGNSS?
The body of each satellite measures roughly 51x64x28 centimeters, slightly larger than a standard carry-on suitcase.
When fully assembled, the satellites will each weigh about 29 kilograms.
With its solar panels deployed, each microsatellite has a wingspan of 1.67 meters.
The Cyclone Global Navigation Satellite System (CYGNSS) is a NASA mission that consists of a constellation of 8 micro-satellites.
Rendition of a single CYGNSS observatory
in orbit over a hurricane. (NASA)
Mission Updates:
· CYGNSS successfully launched on December 15, 2016 and the eight observatories are all on orbit
· Successfully measured out first ocean DDMs on January 4, 2017, just east of Brazil.

## Slide 3: What is CYGNSS?
Capable of retrieving usable data over a large range of wind speeds (0-70 m/s) in all precipitating conditions throughout the tropics and subtropics with a frequent revisit times.
Utilize signals from existing GPS satellites to measure surface wind speeds (surface roughness affects forward-scattered signal) along the satellite ground tracks.
Basic geometry of bi-static quasi-specular
scatterometry

## Slide 4: OSSE Framework
The regional OSSE (Observing System Simulation Experiment) framework was developed at NOAA/AOML and UM/RSMAS and features a high-resolution regional nature run embedded within a lower-resolution global nature run.
Simulated observations are generated and provided to a data assimilation scheme which provides analyses for a high-resolution regional forecast model.

## Slide 5: OSSE Framework Details
Nature Runs
- ECMWF: low-resolution T511 (~40km) “Joint OSSE Nature Run”
- WRF-ARW: high-resolution 27km regional domain with 9/3/1 km storm-following nests (v3.2.1)
Data Assimilation Scheme
- GSI: Gridpoint Statistical Interpolation. a standard 3D variational assimilation scheme (v3.3).
Analyses performed at 9km resolution.
Forecast Model
- HWRF: the 2014 operational
Hurricane-WRF model (v3.5).
Parent domain has ~9km resolution,
single storm-following nest has ~3km
resolution.
DA and model cycling performed every 6, 3, 1 hours, each run producing a 5-day forecasts every 6 hours.

## Slide 6: CYGNSS data
One synthetic CYGNSS datasets generated to span the WRF nature run.
0801 00z - 0805 00z

## Slide 7: Synthetic data generated
Direction information added to CYGNSS wind speeds using 2D Variational Analysis Method (VAM)
CONTROL :
Conventional Satellite/ Surface /sounding data, no CYGNSS
Taken from T511 “Joint OSSE Nature Run”
2D
variational analysis
method
(VAM)
VAM-CYGNSS vector winds
CYGNSS scalar winds
2D vector wind background
WRF
Hurricane
Nature Run
CYGNSS
End-to-End
Simulator
Simulated
Conventional and Satellite Obs
ECMWF
T511 global JONR
Observation
Simulator

## Slide 8: Experiments

## Slide 9: Experiments
All experiments listed use identical configurations of GSI for data assimilation and HWRF for forecasts.
1) CONTROL: Conventional Satellite/ Surface /sounding data, no CYGNSS
2) CONTROL+CYG: CONTROL plus all available CYGNSS wind speed
3) CONTROL+VAM: CONTROL plus VAM wind vectors at CYGNSS retrieval coordinates. (VAM analyses use 9-km HWRF background; 6-hr forecasts)
There are a total of 16, 5-day forecasts, but first 4 forecasts runs omitted from verification to allow for model spin-up (12 cases)
Vary data assimilation cycling frequency
6 hourly cycling: 16
3 hourly cycling: 32
1 hourly cycling: 96

## Slide 10: Average Forecast Errors N = 12 five-day forecasts
6-hourly DA cycling
3-hourly DA cycling
Hourly DA cycling
10

## Slide 11: Average Forecast Errors N = 12 five-day forecasts
6-hourly DA cycling
3-hourly DA cycling
Hourly DA cycling
11

## Slide 12: Average Forecast Errors N = 12 five-day forecasts
6-hourly DA cycling
3-hourly DA cycling
Hourly DA cycling
12

## Slide 13: Statistical Significance N = 12 five-day forecasts 3-hourly DA cycling Min. central pressure error [hPa]
13
Control+CYG
Control+VAM
80%
Confidence
Interval
90%
Confidence
Interval

## Slide 14
Domain Average statistics
6-hourly DA cycling
3-hourly DA cycling
Hourly DA cycling

## Slide 15
Domain Average statistics
6-hourly DA cycling
3-hourly DA cycling
Hourly DA cycling

## Slide 16
Domain Average statistics
6-hourly DA cycling
3-hourly DA cycling
Hourly DA cycling

## Slide 17: SUMMARY
1- Analysis of TC intensity (pressure, wind) improved with addition of CYGNSS data at all DA cycling frequencies
2- DA cycling frequencies affects analyses and forecasts
3- 3-hourly cycling produces the smallest errors for this sample
4- RMS track error at 0-24 hr very slightly improved with addition of CYGNSS data
5- CYGNSS data improves the representation of the surface wind speed structure (intensity and asymmetry)
6- We have relatively a few samples from one storm, so error statistics are not robust but provide guidance.

## Slide 18: Future work
Preparations are underway for impact assessment of CYGNSS during the 2017 hurricane season
Assessment with a near-operational assimilation and forecast framework (HWRF)
Variations of assimilation strategies: nests, scalar/vector
Comparison with NCEP HWRF operational forecasts
For more, see poster 1001 tomorrow, Observation Symposium, 2:30 pm:
“Assimilation of CYGNSS Ocean Surface Winds in HWRF”

## Slide 19: QUESTIONS?

## Slide 20: Backup Slides

## Slide 21
Nature
49.5 m/s
Control
39.0 m/s
Control+CYG
43.3 m/s
Surface Layer Wind analysis 1200 UTC August 3, 2005
After 10 DA cycles (6 hourly); lowest 30 hPa
Control+VAM
43.0 m/s

## Slide 22: Hurricane Error Std. Deviation 3-hourly DA cycling N = 12 five-day forecasts
Control
Control+CYG
Control+VAM
ALL
Min.
Press.
error
[hPa]
Track
error
[km]
Max.
Wspd
error
[kts]