## Slide 1
Bachir Annane1, Mark Leidner4, Brian McNoldy2, Robert Atlas5, Sharanya Majumdar2, Lidia Cucurull3, and Ross Hoffman4
1 Univ. of Miami/CIMAS and NOAA/AOML/HRD, Miami, FL
2 Univ. of Miami/RSMAS, Miami, FL
3 NOAA/AOML, Miami, FL
4 Atmospheric and Environmental Research, Lexington, MA
5 NOAA/AOML, Retired
Forecast Impact Experiments To Optimize Utilization
of CYGNSS Wind Observations

## Slide 2
1. CYclone Global Navigation Satellite System (CYGNSS)
NASA Earth Venture Mission (PI: Chris Ruf)
8 micro-satellites launched in December 2016
Bi-static quasi-specular scatterometry
Utilizes signals (19 cm wavelength) from
GPS satellites to retrieve ocean surface wind speed
Surface roughness affects forward-scattered signal
Low-Earth orbit: 35°S - 35°N
Nominal grid spacing of gridded retrievals: 25 km
Median / mean revisit time: 2.8 h / 7.2 h
Goal of CYGNSS: to retrieve data over a large range of surface wind speeds in all precipitating conditions throughout the tropics and subtropics with frequent revisit times.
Goals of this study:
Pre-Launch: to investigate the potential for CYGNSS to improve analyses and forecasts of tropical cyclones (via OSSEs)
Post-Launch: to evaluate the actual influence of assimilating CYGNSS data into NOAA’s operational hurricane model (via OSEs)

## Slide 3
6 hours of CYGNSS data centered at 06 UTC on October 11, 2017.
24 hours of CYGNSS data.

## Slide 4
. Observing System Experiment (OSE) using 2019 HWRF (“H219”)
NOAA/NCEP FV3 GFS; 6-hourly Hybrid 3d-Var/EnKF
HWRF Model and DA nested grids: 14.5 km / 4.5 / 1.5 km
Observations
All operational observations including radiances
  CYGNSS Version 2.1
  Fully Developed Seas (FDS) and Young Seas Limited Fetch (YSLF)
  Data thinning vs no thinning with inflated error values
  CYGNSS data with retrieval errors 3 m/s or less are included
  Wind directional information from VAM
There are two criteria that are used to pick case studies.
1. Based on the OSSE results, we are looking at cases where the operational HWRF had significant errors in the intensity forecast. We want to see if CYGNSS data can improve these forecasts.
2. Only lower-wind-speed retrievals are reliable. So, we are looking for tropical cyclones in their early stages (tropical depression and tropical storm), that are poorly observed. This is where CYGNSS can contribute information to the structure of the nascent system
Investigate early in Michael’s life cycle (Tropical Storm): Oct 7th 2018
CYGNSS impact on analyses and forecasts
for TC Michael (2018)

## Slide 5: Case Study: Tropical Cyclone Michael 10/07/2018 00Z to 10/08/2018 06Z

## Slide 6
10/07 00Z
10/07 06Z
10/07 12Z
10/08 06Z
10/08 00Z

## Slide 7: Vector wind analysis method 2-D Variational Wind Analysis
An optimal fit to CYGNSS observations is constrained by:
Jb: analysis should be “close” to the a priori, or “Background”, wind field
Jo: ensure the analysis is close to CYGNSS wind speeds
Jc: impose fluid dynamical constraints on the solution (vorticity, divergence)
MIN(J = Jb + Jo + Jc)
Background winds are GFS operational analyses (0.25 x 0.25 degree).
Relative weights in minimization are consistent with CCMP analyses.
Hoffman, R. N., S. M. Leidner, J. M. Henderson, R. Atlas, J. V. Ardizzone, and S. C. Bloom, 2003: A two-dimensional variational analysis method for NSCAT ambiguity removal: Methodology, sensitivity, and tuning. J. Atmos. Oceanic Technol., 20 (5), 585–605.

## Slide 8
Key:
CYGNSS YSLF
CYGNSS FDS
6 hours of CYGNSS data: quality controlled/thinned
+/- 3 hours around 0600 UTC Oct 10, 2018

## Slide 9
Derived CYGNSS wind vectors
0600 UTC Oct 10, 2018 +/- 3 hours

## Slide 10
Experiment Name | Assimilated Data set Cycles (10/07 00Z- 10/08 06Z) |  |  | 
 | Conventional | Radiances | CYGNSS | CYGNSS-VAM
CTRL | Yes | Yes | No | No
CYG50 | Yes | Yes | Yes | No
VAM50 | Yes | Yes | No | Yes
CYG_NOTN | Yes | Yes | Yes | No
VAM_NOTN | Yes | Yes | No | Yes

## Slide 11
HWRF track and intensity forecast errors

## Slide 12
CNTRL
CYG-NOTHN
VAM-NOTHN
10/07 18UTC
CNTRL
CYG50
VAM50

## Slide 13
0712
0718
0800
0806
Forecasts
starting
CYG_50
No CYGNSS
Azimuthally averaged tangential wind cross sections of forecasts started at 6 hour intervals, all valid at the same time, 0600 UTC 10 August 2018, about 12 hours before hurricane Michael made landfall.

## Slide 14
CNTROL NO CYCGNSS
CYCGNSS NO THINNING, VAM
Moisture convergence, latent heating, secondary circulation enhanced by CYGNSS data.
Analysis
24 hour forecast
24 hour forecast
24 hour forecast
CYGNSS impact on analyses and forecast for TC Michael (2018)

## Slide 15: Conclusions & Next Steps
CYGNSS supplies critical observations early in Tropical Cyclone lifecycle
  Other observing systems are often absent when tropical storms are weak
Improved early analyses lead to the improvement in intensity forecasts (66 hr)
  Small changes to ocean/atmosphere fluxes can trigger a different evolution
  Improved surface fluxes modify the distribution of latent and sensible heat
Continue tuning of vector CYGNSS winds in regional DA (HWRF)
  Additional cases: Hurricane Dorian (2019), Typhoon Lekima (2019)
  Preparing for use of vector CYGNSS winds in global DA (FV3-GFS)

## Slide 16
Additional Slides

## Slide 17
Control
(no CYGNSS)
VAM-CYGNSS
10-m winds
Azimuthally-averaged
Tangential Wind
Azimuthally-averaged
Temperature Departure
Analysis
valid
20181007
1800 UTC

## Slide 18
Azimuthally-averaged Radial Inflow
Azimuthally-averaged Radial Moisture Flux Convergence
Control
(no CYGNSS)
VAM-CYGNSS
30-h Forecast
from
20181007
1800 UTC

## Slide 19
60-h Forecast
from
20181007
1800 UTC
Control
(no CYGNSS)
VAM-CYGNSS
10-m winds
Azimuthally-averaged
Tangential Wind
Azimuthally-averaged
Temperature Departure

## Slide 20
cntrl
cygntn
vamntn
10/07 18UTC

## Slide 21
cntrl
cyg50
vam50
10/07 18UTC

## Slide 22
cntrl
cyg50
vam50
10/07 18UTC

## Slide 23
cntrl
cygntn
vamntn
10/07 18UTC

## Slide 24: CYGNSS Measures Reflected GPS from Ocean

## Slide 25
Underside view of a CYGNSS observatory (Courtesy of Southwest Research Institute).
The CYGNSS observatories are shown as yellow spheres. The white lines represent direct GPS signals and the blue ocean surface scattered signals. The lighter blue circles on the Earth surface represent individual samples of the delay doppler map.