## Slide 1: Introduction to Global Navigation Satellite Systems reflectometry (GNSS+R )
Involves making measurements from the reflections from the Earth of navigation signals from GPS.
Applications:
  Surface wind speed
  Altimetry
  Mean square slope
  Soil moisture
  Salinity
  Sea Ice

## Slide 2: GNSS+R 2017 Conference
Day 1: Missions and Data assimilation, Calibration and Validation
Day 2: Ocean Altimetry and Ocean Scatterometry
Day 3: Land, Modeling and Theory, Cryosphere
Talks of interest: Paul Chang, Chris (storm surge)
Collaborators:
  Giuseppe Grieco (Netherlands) : The group is mainly involved in wind field remote sensing through active microwave sensors, mainly scatterometers. The group tries to expand its competences in wind field retrieval from GNSS-R measurements. One of the topic will be the impact of the assimilation of GNSS-R retrieved winds on NWP models. This could be the overlapping interest and therefore the area of collaboration.
  Shu-Chih (Taiwan): configuration GSI and VAM

## Slide 3: CYGNSS Level 2 Wind Speeds
Pre-released on JPL PO.DAAC Monday May 21
Paul and Zorana advise not using for science
Many relationships to account for in GMF
  Wind speed, incidence angle, mean square slope, SNR (signal to noise ratio), PRN (pseudo-random noise), wind direction (really small), antenna azimuth, low wind speed wave state.
Wind speeds top out at 35 m/s until validation data is available

## Slide 4
Future missions:
  GEROS-ISS launching late 2021
  FORMOSAT 7/ COSMIC 2 (Taiwan)

## Slide 5: Ella CYGNSS L2 winds

## Slide 8
X

## Slide 9
X

## Slide 10
X

## Slide 13
X

## Slide 14
X00

## Slide 16
X

## Slide 18
X12

## Slide 19: Evaluation of CYGNSS winds retrieved using an Extended Kalman Filter (EKF) and direct assimilation of Delay-Doppler Maps (DDMs)
Jim Garrison1 – Principal Investigator
Mark Leidner2, Bachir Annane3, Feixiong Huang1, Kaitie Schoenfeld1 and R. N. Hoffman4
1 Purdue University, West Lafayette, USA
2 Atmospheric and Environmental Research, Norman, OK, USA
3 Cooperative Institute for Marine and Atmospheric Studies (CIMAS), Miami, FL, US
4 Univ. of Miami/CIMAS and NOAA/AOML/HRD, Miami, FL
GNSS+R Workshop
Ann Arbor, MI
May 23-25, 2017

## Slide 20: Overview
Comparison of EKF / Level 2 winds just getting underway
  no results yet (L2 data released on 5/18)
Preparatory work for direct assimilation of Level 1 DDMs
  Why assimilate DDMs?
  Progress toward a modular DDM forward model
  Example simulated DDMs from around Cyclone Enawo
Summary

## Slide 21
Measurement geometry
Hi-resolution DDM from raw
Intermediate Frequency (IF) data
Low-resolution with 3x5
sampling region for L2 winds
Why assimilate DDMs?

## Slide 22
Measurement geometry
One sample (1 s)
Three samples (3 s)
Why assimilate DDMs?

## Slide 23: Assimilate DDMs by use of Jacobian, H
Data Assimilation:
Given
-- an observed DDM, y,
-- a simulated DDM, Hxb,
-- an analytical Jacobian of the forward model, H,
-- an estimate of background error covariance, B,
-- an estimate of observation error covariance, R,
the increment to the wind model (xa—xb) can be computed.

## Slide 24: Validate the forward model with measured CYGNSS L1 data
Gridded
90x90km
wind field
Forward model
Antenna
pattern
Tx, Rx
Geometries
HWRF
analysis
simulated
17x11 DDM
Jacobian H matrix
CYGNSS L1a DDM

## Slide 25
Cyclone Enawo

## Slide 26
cyg02
cyg03
cyg04
cyg05

## Slide 27
cyg02 – X
high wind speed
HWRF U10 ~ 40 m/s
X – cyg05
moderate wind speed
HWRF U10 ~ 8 m/s
cyg02
cyg03
cyg04
cyg05
X – cyg02
flat wind field
HWRF U10 ~ 9 m/s
high wind speed
HWRF U10 ~ 40 m/s
cyg04 – X

## Slide 28: High and moderate wind speed examples effect of CYGNSS antenna pattern

## Slide 29
2.22 km resolution
HWRF nested
domain (d02)

## Slide 31
cyg02 – X
high wind speed
HWRF U10 ~ 40 m/s
X – cyg05
moderate wind speed
HWRF U10 ~ 8 m/s
high wind speed
HWRF U10 ~ 40 m/s
cyg04 – X
X – cyg02
Flat wind field
HWRF U10 ~ 9 m/s
2.22 km resolution
HWRF nested
domain (d03)

## Slide 32
High wind speed (~40 m/s) example:
CYGNSS DDM
Forward Model:
Isotropic Antenna
Forward Model:
updated Antenna
Power Bias and differences in DDM pattern will effect Data Assimilation results.
-- variational data assimilation requires mean unbiased (observation – model) statistics

## Slide 33
Moderate wind speed (~8 m/s) example:
CYGNSS DDM
Forward Model:
Isotropic Antenna
Forward Model:
updated Antenna

## Slide 34: Low wind speed example effect of CYGNSS antenna pattern

## Slide 35
cyg05 – X
HWRF 13.88 km
resolution domain (d02)
cyg05 – X

## Slide 36
cyg05 – X
cyg05 – X

## Slide 37
cyg05 – X
HWRF 13.88 km
resolution
domain (d02)
cyg05 – X

## Slide 38
cyg05 – X
near-calm wind speed
HWRF U10 < 2 m/s

## Slide 39
Near-Calm wind (< 2 m/s) example:
CYGNSS DDM
Forward Model:
Isotropic Antenna
Forward Model:
updated Antenna

## Slide 40: Flat wind field (near uniform) example asymmetric CYGNSS DDMs

## Slide 41
Flat wind field (~9 m/s) asymmetric example:
CYGNSS DDM
Forward Model:
Isotropic Antenna
Forward Model:
updated Antenna

## Slide 42: Potential sources of differences between observed and simulated DDMs:
transmitter power / gain / eirp are not precise
Receiver antenna pattern is not accurate
HWRF differs from the real wind
forward model contains errors (empirical model between MSS and wind)
The observed DDM is under refinement

## Slide 43: Summary
Exercising a path to generate simulated DDMs from NWP wind fields
  An important step toward data assimilation
Qualifying the forward model results
  Resolve L/R difference between observed and simulated DDMs
  Examine a larger population
Develop a software path forward for modularizing
Deploy forward model inside a 2-dimensional variational vector wind field model.
  Compare to results assimilating L2 CYGNSS winds