## Slide 1: GFDL HFIP/HRH Comparison Results and Other Advances in Hurricane Modeling Isaac Ginis, Richard Yablonsky, Biju Thomas, Yalin Fan University of Rhode Island
<number>
HFIP/HRH Conference Call
21 May 2009
Notes: <number>

## Slide 2: GFDL HRH Experimental Design
Grid configurations
No asymmetries added during bogusing to the initial axisymmetric vortex (operational GFDL model includes vortex asymmetries based on the forecast fields from the previous 12-h forecast)
<number>
URI1
Mesh 1: 75ox75o – 1/2o res
Mesh 2: 11ox11o – 1/6o res
Mesh 3: 5ox5o – 1/12o res
URI2
Mesh 1: 75ox75o – 1/2o res
Mesh 2: 11ox11o – 1/6o res
Mesh 3: 5ox5o – 1/18o res

## Slide 3: GFDL HRH Test Experiments
Same physics in all URI1 and URI2 experiments
Total 58 cases run:
  Emily – 8, Felix – 7, Katrina - 6, Karen – 4,
  Ophelia - 10, Philippe - 6, Rita - 6, Wilma – 11.
<number>

## Slide 4: Small Increase in Track Skill with Higher Resolution During Days 3-5

## Slide 5: Degraded Intensity Skill with Higher Resolution (Increased Positive Wind Bias)

## Slide 6: Increased Resolution Gave Improved Intensity Prediction with Katrina during RI
2 Current Operational GFDL
1 12th Degree GFDL
3 18th Degree GFDL
August 24th, 0z
August 25th, 0z
August 26th, 0z

## Slide 7: Wind Speed Cross-Section (72h) Katrina: August 25th, 0z forecast Improved Structure with Higher Resolution
1/12th Degree Resolution
1/18th Degree Resolution

## Slide 8: Accumulated precipitation (47-48 hr) Katrina: August 25th, 0z forecast Improved Structure with Higher Resolution
1/12th Degree Resolution
1/18th Degree Resolution

## Slide 9: Summary of HFIP/HRH Tests
Increased resolution had mixed impact on GFDL model performance for HRH test cases.
Improved horizontal and vertical structure in high-resolution experiments.
Small improvements in track forecast skill.
Degraded intensity forecast skill due to increased positive bias.
Results suggest physics may need to be retuned for high resolution for better performance
<number>

## Slide 10
WCRR
WCR
Storm
WCRL
WCR
Storm
WCRC
WCR
Storm
CTRL
Storm
Speed =
2.4 m s-1
IMPACT OF WCR LOCATION ON STORM-CORE SST COOLING

## Slide 11
Coupled Model Results:
2.5 m/s environmental wind &
3-D ocean model component
Track
CTRL
WCRR
WCRC
WCRL
Legend
84-h
108-h
96-h
Central Pressure
84-h
96-h
108-h
60-km SST cooling
84-h
96-h
108-h
WCRR
WCRL
WCRC
Increased
Cooling
Increased
Intensity

## Slide 12
Hurricane Model
Ocean Model
Air-Sea Interface
Momentum flux (τ)
Sensible heat flux (QH)
Latent heat flux (QE)
Surface current (Us)
SST (Ts)
Wind speed (Ua)
Temperature (Ta)
Humidity (qa)
Momentum flux (τ)
Conventional Coupling Between
Hurricane and Ocean Models
Assumption
Atmosphere is in equilibrium
with sea state
Waves are fully-developed

## Slide 14
Coupled Hurricane-Wave-Ocean Framework for Future HWRF and GFDN Models