## Slide 1: Concerns about P-3 radar
Data tech not specializing in radar was unaware of the proper settings (20120826H1).
Eventually, with input from Paul Reasor and John Gamache, an RVP8 “task” was found that was set up by Bobby Peek (PRF 2400/1600—one trip)
Some concern that filters are eliminating too much data near surface.

## Slide 2: Software issues
Once again the vertical cross-sections of vertical wind show discontinuity across the flight track
Solution: By experimenting with angle corrections in post processing, it appears angle corrections should be somewhere between zero and value found by angle-correction software upon an earlier test flight.

## Slide 3: Software issues
Too much data in boundary layer appears to be removed in analyses—both 3D and cross-sections.
Solution: I discovered I was using the beam width of the G-IV and some inappropriate values for removing reflection of main lobe by sea surface. More coverage near surface is now in analyses.

## Slide 4: Effect of removing tilt angle correction

## Slide 5: Software issues
Script to send data to ground quickly timed out, even though I thought I had the timeout problem worked out. I now believe I understand where the problem is but it would need to be tested in a situation with tenuous SATCOM connections

## Slide 6: Script for sending via sftp
#!/usr/bin/expect
set timeout 120
set file1 [lindex $argv 0]
set file2 [lindex $argv 1]
set file3 [lindex $argv 2]
set file4 [lindex $argv 3]
set file5 [lindex $argv 4]
spawn -noecho /usr/bin/rsync -e ssh -tauz $file1 $file2@$file3:$file4
expect {
"assword:" {exp_send "$file5\r";set timeout -1;exp_continue}
"yes/no)?" {exp_send "yes\r";set timeout -1;exp_continue}
"y/n)?" {exp_send "y\r";set timeout -1;exp_continue}
}

## Slide 7: Noise in analysis (and therefore in superobs)