## Slide 1: NOAA P3 Isaac Dropsonde Performance
Outstanding- best I have ever seen!
No failed launch detects on flights I monitored
All sondes transmitted to splash
Very few data gaps
Only a few late launch detects- ASPEN V3 handles these correctly
Data quality attributable to NCAR oversight on manufacturing process and excellent pre-flight and in-flight screening by AOC

## Slide 2: Remote Dropsonde Processing and NWS Gateway Transmission Data Flow
AOC FTP Ground Server
Remote
ASPEN
User
ASPEN Data Products:
TEMPDROP
NOAA FRD,
SKEW-T
Synoptic maps
AOML Anonymous FTP Server
AOC FD
Software
NWS
Gateway
Raw Sonde
D-file
Raw Sonde
D -file
Stored on Local Machine
All Data Products
and Graphics
WMO
TEMPDROP
Message
Formatted WMO
TEMPDROP
Message
1
2
3
4
5
6
7
8
AOC Ground
Software
7A
Not yet tested
Not yet tested

## Slide 3: Remote Dropsonde Processing Overview
Raw sonde D-files automatically sent from plane via ftp to AOC ground server right after splash- within < 2minutes - sorted in folders by date (no missing data from Isaac flights)
Remote ASPEN user can process sondes and FTP data products anywhere there is a reliable internet connection
Two-way X-chat comms worked well with HRD LPS, AOC FD, and CARCAH
Only missing info for remote user is sonde environment, e.g., eye, eyewall, etc.- can get that from LPS or FD via X-chat
Less stressful work environment than on P3, e.g., Work, Home, Starbucks
Less expensive! - fewer man hours and no travel costs
Can track flight progress using Google Earth (stand alone or browser plugin) in near-real time via TropicalAtlantic.com
Remote user can access a variety of weather products- satellite, radar, weather maps, upper-air soundings quickly via internet to assist in sonde data control

## Slide 4: Recommendations and needs for the future
HRD should adopt remote dropsonde processing as the favored method for P3 missions and G-IV research flights
Backup person on plane (HRD, AOC) should be ready to fill in if needed
HRD LPS or AOC FD should send short X-chat message when sonde is released, e.g, Sonde # at HHMM out - eye (or other environment) or state no env if applicable
If sonde is released along with an AXBT then SST need to be reported via X-chat
Remote users sends via X-chat that sonde # HHMM is on AOML FTP- and short comments regarding sonde data, eg., sfc press, max winds (ht), eye, eyewall, etc. - and anything that might stand out when viewing the sounding
Synoptic map images should be automatically created (NCAR is working on this)
FTP of products can be automated
Better video and text instructions need to be created