## Slide 1
HRD Science Meeting
October 12th, 2022
Joseph J. Cione1
Josh Wadler2, Jun Zhang1,3, Altug Aksoy1,3, Patrick Sosa4, Nick Liccini4
1NOAA/AOML/Hurricane Research Division
2Embry Riddle Aeronautical University
3University of Miami/CIMAS
4Anduril/Area-I
Recent sUAS Observations in Hurricane Ian (2022)

## Slide 2
small Uncrewed Aircraft System (sUAS) Operations
in Hurricanes…
Observational Objective:
Leverage key attributes of NOAA’s existing Hurricane Hunter aircraft to develop emerging uncrewed technologies designed to enhanced data coverage of the critically important, yet sparsely-sampled tropical cyclone boundary layer environment.
End goal:
Through enhanced observation, improve basic understanding, operational situational awareness and ultimately, hurricane intensity forecast performance.
2

## Slide 3
2022-3 NOAA/AOML/HRD Hurricane Field Program
Advancing the Prediction of Hurricanes Experiment
RESEARCH IN COORDINATION WITH OPERATIONS
SMALL UNCREWED AIRCRAFT VEHICLE EXPERIMENT
(RICO SUAVE)
Science Team: Joseph Cione, Jun Zhang, George Bryan (NCAR), Ron Dobosy (NOAA/ARL-ret), Altug Aksoy, Frank Marks, Kelly Ryan, Brittany Dahl, Josh Wadler, Rosimar Rios-Berrios (NCAR), Gijs deBoer (NOAA/PSL), Evan Kalina (NOAA/DTC), Don Lenschow (NCAR), Xiaomin Chen, Chris Rozoff (NCAR), Eric Hendricks (NCAR), Falko Judt (NCAR)
Plain Language Description: Use small drones to sample the lowest and most dangerous regions of the tropical cyclone. Observations from these unique platforms have the potential to improve basic understanding and enhance situational awareness. Analyses of data collected from these small drones also have the potential to improve the physics of numerical models that predict changes in storm intensity.

## Slide 4
2022-3 NOAA/AOML/HRD Hurricane Field Program - IFEX
MATURE STAGE EXPERIMENT
RICO SUAVE
Objectives:
Eyewall Module: Provide sUAS HDOBS at multiple altitudes and azimuths to NHC in near real time for visualization in AWIPS II. Post storm, comparing sUAS atmospheric and SST high wind observations with operational analysis and forecast fields (coupled HWRF, HAFS).
Inflow Module: Provide sUAS HDOBS in near-real-time to NHC for visualization in AWIPS II. Post storm, compare sUAS TC boundary layer thermodynamic, kinematic and SST radial structure to improve TC boundary layer parameterizations and ocean response in HWRF and HAFS.
Center Fix/Eye-Eyewall Module: Provide sUAS HDOBS and center fix estimates in near-real-time to NHCfor visualization in AWIPS II. Post storm, compare sUAS TC boundary layer thermodynamic, kinematic and SST structure within the eye and eye/eyewall interface with mode output to improve TC boundary layer parameterizations and ocean response in HWRF and HAFS.

## Slide 5
NOAA’s WP-3D Orion N43RF
“crewed” aircraft (aka “Miss Piggy”)
Area-I’s Altius 600
small “uncrewed” aircraft
ConOp: Deploy a small, semi (eventually fully) autonomous
“uncrewed” aircraft from a “crewed” aircraft

## Slide 6
Launch!

## Slide 7
Post-Launch:
video courtesy of Raytheon Corporation

## Slide 8
ALTIUS-600 Overview
  Air and ground launchable
Fully integrated with the Air Force Common Launch Tube (CLT)
Modular Payload:
  Weight: 3-6lbs
  Volume: 6” diameter by 7” length
  ISR, C-UAS, EW, Kinetic, METOC, etc.
Successfully air launched from C-130A, AC-130J Ghostrider, UH-60M Blackhawk, Cessna Caravan, Beech A36, and others
Endurance: 3-4 hrs
Cruise speed: 55 KIAS
Dash speed: 90 KIAS
Cruise range: 220 Nm
  Excludes launch descent glide distance
Tube-stowed dimensions: 6”x40”
Deployed wing span: 100”
Deployed length: 40”
Gross Weight: 23-27 lbs

## Slide 12
The following slides show the leg of the P-3 with ‘extreme turbulence’

## Slide 13
P-3 Flight Level Data: E-W Eyewall Penetration into Major Hurricane Ian
(September 28, 2022)

## Slide 14
P-3 FL Data:

## Slide 15
P-3 FL Data:

## Slide 16
P-3 FL Data:

## Slide 17
15-m resolution visible imagery
Key West Radar
The P-3 likely went through the ‘scallops’ on the W-SW eyewall…

## Slide 18
Courtesy: Reuters

## Slide 25: Requirements for All Future sUAS TC Operations
Cost: Improvement over GPS dropsonde (~$300/min; $900/3 min) (PBL)
Command/Control: 150nmi range between sUAS and P3 (C130)
Payload: High QC, reliable (Vaisala RD41; NOAA GPS Drop/Up Sondes)
Survivability_1: Consistency, 210-220kt air-deployed launch (P3/C130)
Survivability_2: Severely turbulent, high wind hurricane conditions
Full Autonomy : No onboard sUAS pilots (Similar to Dropsonde release)
Where are we right now (October 12, 2022)?
- Cost: Area-I and Blacks Swift have met cost requirements (~$40- $200/minute)
- C2: Altius: CAT 3.5h, 189 nmi (P3-to-sUAS range); Ian 1.75h* (130 nmi)
- Payload: Both have made progress (ground testing); Altius CAT, Ian
- Survivability (1): Altius: CAT, Ian success; Blackswift: (Unknown)
- Survivability (2): Altius: 100% yes, Blackswift: (Unknown)
- Automation: Altius: partial (Center fix, RMW hunt); Blackswift: (in progress)
What's Next?
Altius: post-processing, lessons learned in Ian, add multi-hole turbulence probe and video capability for 2023.
Blackswift: CAT in March 2021, prep for first TC flights in 2023.

## Slide 26: Summary
Observations from small Unmanned Aircraft Systems (sUAS) have the potential to enhance the basic understanding of dangerous and difficult to observe regions of the Tropical Cyclone, including the critical air-sea transition zone.
These unique data have the potential to improve situational awareness and future forecasts of Tropical Cyclone intensity change using NOAA’s operational coupled-ocean atmosphere modeling system.
As technology advances, small drones (such as the two new platforms highlighted today) will be able to fly longer, lower and for less money.
Working with public and private sector partners, NOAA will continue to explore this promising technology over the coming years in order to help the Agency better meet its ultimate goal of protecting property and saving lives.
Project Support: NOAA/OMAO/AOC, NOAA/SBIR, NOAA/OAR/WPO,
NOAA/JPA