## Slide 1
NOAA sUAS Operations in Tropical Cyclones:
A Recap of 2022 and Plans for 2023
Joseph J. Cione
NOAA/AOML/Hurricane Research Division
AVAPS Annual Meeting
April 13, 2023

## Slide 2
small Uncrewed Aircraft System (sUAS) Operations
in Hurricanes…
Observational Objective:
Leverage key attributes of NOAA’s existing Hurricane Hunter aircraft to develop emerging uncrewed technologies designed to enhanced data coverage of the critically important, yet sparsely-sampled tropical cyclone boundary layer environment.
End goal:
Through enhanced observation, improve basic understanding, operational situational awareness and ultimately, hurricane intensity forecast performance.
2

## Slide 3
NOAA’s WP-3D Orion N43RF
“crewed” aircraft (aka “Miss Piggy”)
Area-I’s Altius 600
small “uncrewed” aircraft
ConOp: Deploy a small, (eventually fully) autonomous
“uncrewed” aircraft from a “crewed” aircraft
Endurance: 3-4 hrs
Cruise/Dash Speed: 55 kt/90 kt
Comms to P:3 120-195 nmi
Deployed wing span: 100”
Deployed length: 40”
Gross Weight: 23-27 lbs
Modular Payload:
  Weight: 3-6lbs
  PTH; IR/SST; BAT
  Image and Streaming Capable

## Slide 4
Launch!

## Slide 6
Recent sUAS Observations in Hurricane Ian:
September 28th, 2022…

## Slide 7
Hurricane Ian - Regional 88-D Composite

## Slide 10
Courtesy: Reuters

## Slide 11
The P-3 likely went through the ‘scallops’ on the W-SW eyewall…
15-m resolution visible imagery

## Slide 12: P3 Doppler Profile Data

## Slide 13: P3 Doppler Profile Data

## Slide 14
Hurricane Ian Visible Satellite Imagery: 1151Z
Altius in-flight period: 1030z - 1212z

## Slide 15
P-3 Flight Level Data: NW-SE Eyewall Penetration into Major Hurricane Ian
(September 28, 2022)
The following slides show the leg of the P-3 with ‘extreme turbulence’…

## Slide 16
P-3 FL
Data:

## Slide 17
P-3 FL
Data:

## Slide 18
P-3 FL
Data:

## Slide 23: Ian (2022) Summary
small Unmanned Aircraft Systems (sUAS) observations can improve scientific understanding of dangerous and difficult to observe regions of the Tropical Cyclone, including the critical air-sea transition zone.
These unique data have the potential to improve operational situational awareness, boundary layer physics and future forecasts of Tropical Cyclone intensity (and possibly short term track with enhanced center fix capabilities).
As this technology advances towards operational transition, small drones will fly lower, longer and for less money.
What's Next for Altius?
Altius: post-processing, Ian sUAS data impact, BL analysis, add multi-hole turbulence probe and possible video for 2023. Incorporate Ian lessons learned.
Project Support: NOAA/OMAO/AOC, NOAA/SBIR, NOAA/OAR/WPO,
NOAA/JPA
sUAS Records set:
Wind speed 216mph (@2150 ft)
Endurance (102 min)
sUAs-P3 distance (130nmi)

## Slide 24
NEw and Improved Observing Technologies And Enhanced Concept of Operations Working Group
Federal civilian and DoD partners, Academic Institutions, Private Sector collaborators
V2.0 (ongoing)
Field testing for the
most promising
technologies

## Slide 25
BLACK SWIFT TECHNOLOGIES “S0” sUAS
NOAA SBIR 8.2.13 - Developing a Cost Effective Air-Deployed
UAS for use in Turbulent Environments

## Slide 26
2023 Clear air testing Black Swift S0 (Florida, March 2023)

## Slide 27: StreamSonde
INTEGRATED SENSORS:
Pressure
Temperature
Humidity
Accurate, custom built GNSS
3D Gyro
3D Accelerometer
3D Magnetometer
Air Quality sensor
Ambient light sensors
FEATURES:
Weight: < 15 gram
Size: 66mm in diameter
Terminal free-fall velocity: below 5m/s (a.s.l.)
403MHz meteorological band
1.5h operation time
Re-chargeable Li-Ion battery
Ultra-low power consumption
OPERATIONS:
Deployment from airplanes equipped with AVAPS launchers.
No parachute needed
Descent with natural winds
Floats on water surface
4 patent applications filed

## Slide 28
2023 NOAA/AOML/HRD Hurricane Field Program
Advancing the Prediction
of Hurricanes Experiment (APHEX)
RESEARCH IN COORDINATION WITH OPERATIONS
SMALL UNMANNED AIRCRAFT VEHICLE EXPERIMENT
(RICO SUAVE)
Science Team: Joseph Cione, Jun Zhang, Josh Wadler (ERAU), George Bryan (NCAR), Ron Dobosy (NOAA/ARL-ret), Altug Aksoy, Ed Dumas (NOAA/ARL), Rosimar Rios-Berrios (NCAR), Gijs deBoer (NOAA/PSL), Kelly Ryan (CIMAS), Xiaomin Chen (UAH)
Plain Language Description: Use small drones to sample the lowest and most dangerous regions of the tropical cyclone. Observations from these unique platforms have the potential to improve basic understanding and enhance situational awareness. Analyses of data collected from these small drones also have the potential to improve the physics of numerical models that predict changes in storm intensity.

## Slide 29
2023 MATURE STAGE EXPERIMENT
RICO SUAVE
Objectives:
Eyewall Module: Provide sUAS HDOBS at multiple altitudes and azimuths to NHC in near real time. Post storm, comparing sUAS atmospheric and SST high wind observations with operational analysis and forecast fields from coupled HWRF and HAFS.
Inflow Module: Provide sUAS HDOBS in near-real-time to NHC. Post storm, compare sUAS TC boundary layer thermodynamic, kinematic and SST radial structure with model output to improve TC boundary layer parameterizations and ocean response in HWRF and HAFS.
Center Fix/Eye-Eyewall Module: Provide sUAS HDOBS and center fix estimates in near-real-time to NHC. Post storm, compare sUAS TC boundary layer thermodynamic, kinematic and SST structure within the eye and eye/eyewall interface with mode output to improve TC boundary layer parameterizations and ocean response in HWRF and HAFS.

## Slide 30
Questions ?