## Slide 1: What is the bumpiest flight on the P-3 (at least since 2012)?
Joshua B. Wadler1, Lauren Villafane1, Joe Cione2
HRD July Science Meeting
1Embry-Riddle Aeronautical University
2NOAA/Hurricane Research Division

## Slide 2: Motivation
The flight into Hurricane Ian (2022) was so turbulent that a group of us on the flight were informally discussing if it was the worst flight ever. Why not try to figure that out?
A video from Nick Underwood at NOAA/AOC went viral on Twitter following the flight

## Slide 3: Background
The first step to defining ‘bumpiness’ is to characterize the motions an aircraft can experience
There are three rotational motions and three translational motions
Can we combine them into one reference frame?
Rotational Motions
Translational Motions
(Y-axis)
(Z-axis)
(X-axis)

## Slide 4: Building the Algorithm
P-3 flight-level data files include pitch angle, roll angle, and yaw angle. They also include accelerations in x (front-back), y (side-side), and z (up-down), all at 1 Hz.
To put everything into aircraft-centric coordinate system, we can use a 3-D rotation matrix to turn the pitch, roll, and yaw angles into a Δx, Δy, Δz displacement due to the rotational motions.
γ = pitch angle
β = roll angle
α =yaw angle
.
Each seat has a Δx, Δy, Δz relative to the center of gravity of the aircraft
We obtained the average center of gravity from the flight engineer and measured the distances for all 19 seats.
x

## Slide 5: What do we actually feel on the plane?
Recall, the flight-level files give ax, ay, az due to translational motions which are the same for each seat (mostly)
We can get ax, ay, az due to rotational motions by numerically taking the derivative of Δx, Δy, Δz from rotational motions. Each seat gets a different value.
I believe that ‘bumpiness’ is some combination of acceleration and jerk (da/dt; also calculated numerically)
  Constant accelerations can be uncomfortable (e.g., constant turning) but they don’t throw you around. Sudden changes in acceleration do.
We built 16 different definitions of bumpiness. Some examples:
  (Pro: Classical definition of vectors, Con: Completely z-dominant)
  (Pro: Better accounts for changes in all directions, Con: One zero component and the whole term goes away)
  (Final Version)

## Slide 6: Going back to our Preferred Definition
Top 10 missions since 2012
 | For Seat 1 |  | 
 | Storm Name | Mission ID | Maximum Value (m/s2)
1 | 'IAN' | '20220928H1' | 5.45
2 | 'SAM' | '20210929H2' | 4.33
3 | 'IRMA' | '20170908H2' | 4.04
4 | 'TEDDY' | 20200918I1' | 3.83
5 | 'MICHAEL' | '20181010H1' | 3.81
6 | 'DORIAN' | '20190904H1' | 3.63
7 | 'PATRICIA(EP)' | '20151023I1' | 3.54
8 | 'MATTHEW' | '20161006I2' | 3.52
9 | 'SALLY' | '20200914I1' | 3.40
10 | 'TEDDY' | '20200917H1' | 3.40
Subjective List
Storm Name | Flight ID | Person Identified
Allen | 800806H | Bob Black, Frank Marks
Allen | 800805H | Pete Black (Claims it is worse than the 6th)
Irene | 810926H | Bob Black
Emily | 870922H | Bob Black, John Gamache, John Kaplan
Emily | 870922I1 | John Gamache
Claudette | 910908I | Bob Black
Felix | 070902H | Sim Aberson
Irene | (landfall mission in 1999, likely 10/15) | Joe Cione
Michael | 20181010H1 | Andy Hazelton
Michael | 20181009H2 | Josh Wadler
Dorian | 20190901H1 | Jon Zawislak
Cristobal | 140826I1 | Heather Holbach
Irma | 170908H1 | Heather Holbach
Lane | 180822H1 | Heather Holbach
Sam | 210929H2 | Jun Zhang
Patricia | 20151023I1 | Rob Rogers
Ian | 220928H1 | Josh Wadler

## Slide 7: Going back to our Preferred Definition
Top 10 missions since 2012
 | For Seat 1 |  | 
 | Storm Name | Mission ID | Maximum Value (m/s2)
1 | 'IAN' | '20220928H1' | 5.45
2 | 'SAM' | '20210929H2' | 4.33
3 | 'IRMA' | '20170908H2' | 4.04
4 | 'TEDDY' | 20200918I1' | 3.83
5 | 'MICHAEL' | '20181010H1' | 3.81
6 | 'DORIAN' | '20190904H1' | 3.63
7 | 'PATRICIA(EP)' | '20151023I1' | 3.54
8 | 'MATTHEW' | '20161006I2' | 3.52
9 | 'SALLY' | '20200914I1' | 3.40
10 | 'TEDDY' | '20200917H1' | 3.40
Subjective List (since 2012)
Michael | 181010H1 | Andy Hazelton
Michael | 181009H2 | Josh Wadler
Dorian | 190901H1 | Jon Zawislak
Cristobal | 140826I1 | Heather Holbach
Irma | 170908H1 | Heather Holbach
Lane (EP) | 180822H1 | Heather Holbach
Sam | 210929H2 | Jun Zhang
Patricia (EP) | 151023I1 | Rob Rogers
Ian | 220928H1 | Josh Wadler
(#12 with B=3.36)
(different mission)
(different mission)
(different mission)
(small x,y motions)

## Slide 8
What were the contributing components?
 | Storm Name | Mission ID | Maximum Value
1 | 'IAN' | '20220928H1' | 4.06
2 | 'IRMA' | '20170905H1' | 3.15
3 | 'PATRICIA(EP)' | '20151023I1' | 2.93
4 | 'DORIAN' | '20190901H1' | 2.92
5 | 'SAM' | '20210929H2' | 2.66
6 | 'MATTHEW' | '20161006I2' | 2.65
7 | 'LANE(EP)' | '20180822H1' | 2.51
8 | 'TEDDY' | '20200917H1' | 2.47
9 | 'MICHAEL' | '20181010H1' | 2.42
10 | 'ISAIAS' | '20200801I2' | 2.41
x-total motions
(front-back)
z-total motions
(up-down)
y-total motions
(side-side)
 | Storm Name | Mission ID | Maximum Value
1 | 'IAN' | '20220928H1' | 7.70
2 | 'IRMA' | '20170908H2' | 4.97
3 | 'RAFAEL' | '20121015H1' | 4.83
4 | 'TEDDY' | '20200917H1' | 4.02
5 | 'LANE(EP)' | '20180822H1' | 3.88
6 | 'DORIAN' | '20190904H1' | 3.86
7 | 'SAM' | '20210929H2' | 3.67
8 | 'EARL' | '20220905I1' | 3.66
9 | 'MATTHEW' | '20161006I2' | 3.52
10 | 'IRMA' | '20170908H1' | 3.45
 | Storm Name | Mission ID | Maximum Value
1 | 'SAM' | '20210929H2' | 18.83
2 | 'LARRY' | '20210906I1' | 15.09
3 | 'MICHAEL' | '20181010H1' | 14.55
4 | 'CRISTOBAL' | '20140826I1' | 14.50
5 | 'PATRICIA(EP)' | '20151023I1' | 13.79
6 | 'EARL' | '20220905I1' | 13.67
7 | 'NICOLE' | '20221108I2' | 13.28
8 | 'MICHAEL' | '20181009H1' | 12.82
9 | 'HARVEY' | '20170824H1' | 12.78
10 | 'LAURA' | '20200826H2' | 12.63

## Slide 9: We can also look at differences between seats
Comparison Between Seats in Ian
Seat | max Bumpiness (m/s2)
1 | 5.45
2 | 5.48
3 | 5.37
4 | 5.26
5 | 4.85
6 | 4.88
7 | 4.24
8 | 4.27
9 | 4.23
10 | 4.23
11 | 4.20
12 | 4.23
13 | 4.43
14 | 4.39
15 | 4.43
16 | 5.06
17 | 5.10
18 | 5.09
19 | 5.66

## Slide 10: We can also look at differences between seats
Seat | max Bumpiness (m/s2)
1 | 5.45
2 | 5.48
3 | 5.37
4 | 5.26
5 | 4.85
6 | 4.88
7 | 4.24
8 | 4.27
9 | 4.23
10 | 4.23
11 | 4.20
12 | 4.23
13 | 4.43
14 | 4.39
15 | 4.43
16 | 5.06
17 | 5.10
18 | 5.09
19 | 5.66
~30% worse near the front of the plane than the back
Comparison Between Seats in Ian

## Slide 11: Limitations and Next Steps
Top 10 missions since 2012
 | For Seat 1 |  | 
 | Storm Name | Mission ID | Maximum Value (m/s2)
1 | 'IAN' | '20220928H1' | 5.45
2 | 'SAM' | '20210929H2' | 4.33
3 | 'IRMA' | '20170908H2' | 4.04
4 | 'TEDDY' | 20200918I1' | 3.83
5 | 'MICHAEL' | '20181010H1' | 3.81
6 | 'DORIAN' | '20190904H1' | 3.63
7 | 'PATRICIA(EP)' | '20151023I1' | 3.54
8 | 'MATTHEW' | '20161006I2' | 3.52
9 | 'SALLY' | '20200914I1' | 3.40
10 | 'TEDDY' | '20200917H1' | 3.40
Expanding the data before 2012: Flight-level data files do not have an ax or an ay but we may have a solution for that.
The ranking is based on the maximum value at one time. Perhaps we switch to a cumulative value?
We’ve also been exploring the idea of ‘queasiness index’
  Thank You!

## Slide 12: Extra Slide

## Slide 13
The Aircraft Orientation Term Did Not Perform As Expected
  We also tried an aircraft orientation factor:
  *(1+pitch_Angle+roll_Angle)
The maximum bumpiness observed was during 60 deg bank angle turns