## Slide 1: Coupled Ocean-Wave Model Team (Team 8) Report
George Halliwell (co-lead, NOAA/AOML/PhOD)
Hendrik Tolman (co-lead, NOAA/NCEP)
Isaac Ginis (URI)
Chris Fairall (NOAA/ESRL)
Shaowu Bao (NOAA/ESRL)
Jian-Wen Bao (NOAA/ESRL)
Nick Shay (UM-RSMAS)
Daniel Melendez (NOAA/OAR)
HFIP Meeting, Miami, FL., 8-10 Nov. 2010

## Slide 2: Team 8 Milestones
Evaluate existing HYCOM-HWRF for operational implementation
Port coupled HWRF to East Pacific
Develop, evaluate, and improve new coupled atmosphere-wave-ocean forecast models
  New HYCOM-HWRF including WWIII wave model
  COAMPS-TC
Evaluate and improve air-sea flux parameterizations
Evaluate and improve ocean model performance
Improve ocean model initialization

## Slide 3: 1. Evaluate Existing HYCOM-HWRF
Pre-op testing conducted for 2010
Upgrades
    GFS physics
    GFS resolution
    HWRF stress
Tentatively accepted in 2011 baseline

## Slide 4: 2. Port Coupled HWRF to EastPac
RTOFS-Global to replace RTOFS-Atlantic
  Use for initial and boundary conditions for regional HWRF models including EastPac
Adopting existing 1/12° model from NRL.
  GFS forcing (including diurnal cycle).
  NAVOCEANO provides initialization from global HYCOM.
Timeline:
  FY2011Q4: operational
    Begin testing East Pacific coupled HWRF
  FY2014: Initialization performed at NCEP.

## Slide 5
HYCOM - WWIII - HWRF
  Framework exists – already implemented in GFDL model
  Begin testing in 2011
(URI/NCEP Collaboration)
3. New Coupled Atm.-Wave-Ocean Models
Notes: <number>

## Slide 6
Couple COAMPS-TC configuration
Atmosphere:
3 nests (45, 15, 5 km), 40 vertical levels. 15 and 5 km domains automatically follow TC
Ocean:
1 nest (10 km), 46 vertical levels and 30 sigma layers
Naval Research Laboratory
Coupled COAMPS-TC (Sue Chen)
FY 2010 accomplishments:
  Continue testing and evaluation of coupled COAMPS-TC
  Upgrade the ocean data assimilation system to 3DVAR NCODA
  Incorporate recent COAMPS-TC improvements to the coupled version (improved tracker, precipitation output on the moving nests, and total liquid water output)
  Perform coupled model evaluation using the 2009 season hurricane cases
  Tested and integrated air-ocean coupled COAMPS-TC in low resolution over the Atlantic basin in real-time

## Slide 7
Naval Research Laboratory
Summary & FY11 Milestones
Test the impact of two-way air-ocean coupling using the 2010 season hurricanes in the 45-15-5 km atmospheric and 9 km ocean configuration
Test and evaluate the six-way coupled (atmos+NCOM+SWAN) and four- way coupled (atmos+NCOM+WW3) COAMPS-TC system
Track
Intensity
Hurricane Bill (2009), track and intensity forecast to 72hr, uncoupled (red) vs. coupled (blue)

## Slide 8: 4. Improving Air-Sea Flux Parameterizations
URI Air-Sea Interface Model (ASIM)
  Explicit wind-wave-current interaction effects
  Fully implemented in GFDL model
  Available soon for HYCOM-HWRF
NOAA/ESRL sea spray parameterizations
  Tested at GFDL in collaboration with URI

## Slide 9
Impact of Sea Spray Parameterizations on Coupled Forecasts
As the wind speed increases, the droplet size increases and the overall wind speed in the surface layer above the level of sea-spray generation increases, indicating that the increase of droplet size due to the increase of wind speed enhances the vertical mixing. This is consistent with observations and results from previous numerical model simulations of the microphysical characteristics of sea spray in the atmospheric boundary layer.

## Slide 10
This 6-panel figure depicts the impact of the sea spray scheme on the surface momentum, sensible heat and moisture fluxes associated with an idealized, intensifying storm at 72h into the simulation. In the left column are the spatial distribution for the friction velocity (u*), Hs (<w’t’>) and Hq (<w’q’>) from the run of the coupled model without the sea spray scheme, while in the right column are the counterpart from the run of with the sea spray scheme. The effects of sea spray to reduce the friction velocity and increase the overall enthalpy flux in the storm inner core are obviously shown in this figure.

## Slide 11: 5. Evaluate and Improve Ocean Models
Ongoing efforts at several institutions
  AOML and RSMAS (uncoupled HYCOM)
  AOML (HYCOM-HWRFx) – starting soon
  NCEP/EMC (HWRF with POM & HYCOM)
  NRL-Monterey (COAMPS-TC with NCOM ocean)
  URI (POM & HYCOM)
POM/HYCOM joint evaluation
  Led by R. Yablonsky, GSO/URI

## Slide 12: Other Ocean Model Evaluation Efforts
AOML/RSMAS (HYCOM)
URI (POM)

## Slide 13: POM/HYCOM Joint Evaluation
Partnership: URI/GSO, NOAA/AOML, FSU/COAPS, NOAA/NCEP/EMC
Ocean models forced by idealized wind stress only
Storm-core SST cooling compared to cooling predicted by buoy-based climatological SHIPS statistical algorithm (Cione & Uhlhorn)
Model vs. climatological maximum ΔT within 60 and 200 km radii of storm center plotted
Relatively idealized evaluation – represents a first step toward comprehensive ocean model evaluation

## Slide 14
Both models overcool in 30-40% of all cases
POM overcools in ~50% of all cases for both 60
And 200km radii
HYCOM undercools in ~40% of all cases for
200km diameter case

## Slide 15: 6. Improve Ocean Model Initialization
AOML/RSMAS ocean model evaluation efforts determined that SST forecast accuracy is very sensitive to ocean model initialization
The Deepwater Horizon oil spill motivated an intensive observational effort in the Gulf of Mexico
  Unprecedented dataset to evaluate data-assimilative ocean analysis products for use in ocean model initialization
  Includes NOAA P3 AXBT, AXCTD, AXCP profiles designed for synoptic ocean sampling
    9 flights between 8 May and 9 July 2010
  Also cruises, surface drifters, MMS-funded moorings

## Slide 17
Evaluation of Five Data-Assimilative Ocean Model Analyses
MODELS:
Navy 0.04-degree GOM HYCOM
Navy 0.08-degree global HYCOM
NOAA/NCEP/EMC RTOFS HYCOM
Navy IASNFS NCOM
NOAA/NOS NGOM POM
This evaluation compares temperature
from all AXBT profiles over the depth
range from 30 to 360 m.

## Slide 18
RTOFS develops a spurious anticyclone SE of Louisiand and a spurious cyclonic gyre in the western GOM. Hendrik Tolman is aware of the problem and it will be corrected when the existing 1/12-degree NRL model is adopted for global RTOFS.
Sea Surface Height, 9 July 2010
Navy HYCOM Analysis
RTOFS HYCOM Analysis

## Slide 19: Future Efforts for Improving Ocean Model Initialization at AOML and RSMAS
Further evaluate existing ocean model analysis products for use in initialization
Test improved ocean data assimilation techniques
Perform observing system evaluation and design studies
  Effort to quantify the impact of targeted P3 upper ocean observations is now underway

## Slide 20
Data Denial Experiment Using NRL GOM HYCOM Analysis System
MODELS:
P3 profiles denied
P3 profiles assimilated
These experiments were performed at
NRL-Stennis by Ole Martin Smedstad
and Pat Hogan.
Impact is relatively modest considering
that these P3 temperature profiles were
assimilated.
Question: Does the impact of synthetic
T, S profile assimilation limit the
improvement resulting from P3
assimilation?