## Slide 1: UW Stream 1.5 Candidacy
2010 HFIP Annual Meeting
William Lewis and Greg Tripoli
9 November 2010

## Slide 2
UW-NMS and why it’s different
Where we are currently
  Current configuration / physics / datasets
  Initialization
Where we plan to be Spring 2011
Demonstrated real-time operation

## Slide 3: University of Wisconsin Nonhydrostatic Modeling System
Enstrophy, entropy and kinetic energy conserving dynamics core – unique among regional models
Would add diversity to roster dominated by WRF players (good thing for multi-model ensemble)

## Slide 4: Enstrophy Conserving Dynamics
Lamb Vector Form of Momentum Equations employed

## Slide 5: Enstrophy Conservation (continued)
3D enstrophy and KE conserving operator employed
3D dynamic balance better represented
Numerically consistent vorticity production by Lamb vector curl
Perfect numerical 2D potential vorticity conservation
Numerical coupling with entropy prediction to ensure near perfect Ertel potential vorticity conservation
Numerical erosion of vortex reduced or eliminated

## Slide 6: Current Operational Configuration
3 grids
  60km (145 x 145 points)
  12km (92 x 92 points)
  4km (122 x 122 points)
33 vertical levels
  200m stretched to 1000m (model top ~ 24km)
Coupled to 1.5 layer ocean
Currently, 126-hr forecast requires ~5 hours

## Slide 7: Current Physics
RRTM shortwave / longwave
NOAH LSM
Tripoli / Flatau 2-moment bulk microphysics
CMEE cumulus parameterization (grid 1 and 2)*
Andreas Sea-Spray parameterization*
New level 1.5 TKE scheme*
*under stream 2 development

## Slide 8: Datasets
GFS 1-degree analysis and forecasts
FNMOC 9-km SST (updated 4X daily)
Levitus 0.25 degree monthly ocean climatology (NODC)

## Slide 9: Bogus Vortex Initialization
Implemented Kwon and Cheong (2010) bogus vortex for use with UW-NMS
Fewer spin-up problems than GFDL bogus, and no need to wait for GFDL files (saves ~2 hours)
Potential for further refinement and ensemble generation (free ensemble forecast and DA)

## Slide 10: EnKF
Implementation of the UW-NMS EnKF will begin on Jet during the next few weeks
Assimilation of raw geostationary satellite observations (IR, WV, SWIR) is our priority, but other satellite (passive microwave, satellite winds) as well as conventional and airborne data to be assimilated as well
Testing thru spring 2011, plan to be ready for real-time summer 2011

## Slide 11
10.7μ Brightness Temperature
10m wind speed

## Slide 12: Real-time Capability
Stream 2 provided opportunity to demonstrate capability for executing and delivering forecasts 4X daily
> 500 forecasts since June (AL, EP, CP)
Completion of Retro Case runs anticipated spring 2011 (after completion of remaining stream 2 goals: physics and data assimilation)