## Slide 1: Satellite Microwave Sounding Systems for Hurricane Applications
Fuzhong Weng
Center for Satellite Applications and Research (STAR)
National Environmental Satellites, Data and Information Service (NESDIS)
National Oceanic and Atmospheric Administration (NOAA)
JCSDA-HFIP Workshop, Miami, Florida, December 2-3, 2010
Notes: <number>
1.

## Slide 2: Advantages of Microwave Remote Sensing from Space
Sensors can penetrate through non-precipitating clouds
Instrument calibration is of highly stable
Radiance is nearly a linear function of temperature
O2 absorption line is ideal for temperature sounding due to its uniform distribution within the atmosphere
Notes: <number>
To meet this challenging requirements, we must think about current and future earth observing systems. Microwave sensors are of particularly interests because….

## Slide 3: Polar Missions with MW Sensors for Operational Uses
<number>
5
5
2009
2010
2004
2005
2006
2007
2008
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
PM Orbit
NOAA 17
Mid-AM Orbit
Early-AM Orbit
DMSP 17
DMSP 19
DMSP 20
METOP-B
METOP-C
METOP-A
DMSP 13
DMSP 16
DMSP 18
NOAA 18
NOAA 19
JPSS: ATMS
DoD MIS ?
NOAA 16
EOS AQUA AMSR-E
DMSP SSMI/S
METOP: AMSU-A/MHS
NOAA: AMSU-A/MHS
NPP: ATMS
Notes: <number>

## Slide 4: Atmospheric Transmission at Microwave Wavelengths
The frequency dependence of atmospheric absorption allows different altitudes to be sensed by spacing channels along different absorption lines.
ATMS channels

## Slide 5: Accuracy of Temperature/Moisture Profiles Retrieved from NOAA-18 AMSU/MHS - Clear Sky Conditions
<number>
<number>
Temperature profiles from microwave sounders meet user requirements while water vapor profiles do not in low troposphere due to limited channels
Temperature
Water Vapor
Sea
Land
Sea
Land
Standard Deviation (K)
Standard Deviation (K)
Pressure (mb)
Pressure (mb)

## Slide 6: Spectral Differences
Ch | GHz | Pol | Ch | GHz | Pol
1 | 23.8 | QV | 1 | 23.8 | QV
2 | 31.399 | QV | 2 | 31.4 | QV
3 | 50.299 | QV | 3 | 50.3 | QH
 |  |  | 4 | 51.76 | QH
4 | 52.8 | QV | 5 | 52.8 | QH
5 | 53.595 ± 0.115 | QH | 6 | 53.596 ± 0.115 | QH
6 | 54.4 | QH | 7 | 54.4 | QH
7 | 54.94 | QV | 8 | 54.94 | QH
8 | 55.5 | QH | 9 | 55.5 | QH
9 | fo = 57.29 | QH | 10 | fo = 57.29 | QH
10 | fo ± 0.217 | QH | 11 | fo±0.3222±0.217 | QH
11 | fo±0.3222±0.048 | QH | 12 | fo± 0.3222±0.048 | QH
12 | fo ±0.3222±0.022 | QH | 13 | fo±0.3222±0.022 | QH
13 | fo± 0.3222±0.010 | QH | 14 | fo±0.3222 ±0.010 | QH
14 | fo±0.3222±0.0045 | QH | 15 | fo± 0.3222±0.0045 | QH
15 | 89.0 | QV |  |  | 
16 | 89.0 | QV | 16 | 88.2 | QV
17 | 157.0 | QV | 17 | 165.5 | QH
18 | 183.31 ± 1 | QH | 18 | 183.31 ± 7 | QH
19 | 183.31 ± 3 | QH | 19 | 183.31 ± 4.5 | QH
20 | 191.31 | QV | 20 | 183.31 ± 3 | QH
 |  |  | 21 | 183.31 ± 1.8 | QH
 |  |  | 22 | 183.31 ± 1 | QH
Exact match to AMSU/MHS
Only Polarization different
Unique Passband
Unique Passband, and Pol. different
from closest AMSU/MHS channels
MHS
AMSU-A
AMSU/MHS
ATMS has 22 channels and AMSU/MHS have 20, with polarization differences between some channels
− QV = Quasi-vertical polarization vector is parallel to the scan plane at nadir
− QH = Quasi-horizontal polarization vector is perpendicular to the scan plane at nadir
Notes: An overview of the principal differences between ATMS and AMSU.
<number>

## Slide 7: Microwave Temperature Sounding Vertical Resolution
<number>
MSU+SSU (1978-2007)

## Slide 8: From AMSU/MHS to ATMS
<number>
  70x40x60 cm
  110 W
  85 kg
  8 year life
AMSU-A1
AMSU-A2
MHS
Volume reduced by 3x
75x70x64 cm
24 W
50 kg
3-yr life
73x30x61 cm
67 W
54 kg
3-yr life
75x56x69 cm
61 W
50 kg
4-yr life
From Bill Blackwell, MIT

## Slide 9: Spatial Differences: ATMS vs. AMSU/MHS
Beamwidth (degrees)
 | ATMS | AMSU/MHS
23/31 GHz | 5.2 | 3.3
50-60 GHz | 2.2 | 3.3
89-GHz | 2.2 | 1.1
160-183 GHz | 1.1 | 1.1
Spatial sampling
 | ATMS | AMSU/MHS
23/31 GHz | 1.11 | 3.33
50-60 GHz | 1.11 | 3.33
89-GHz | 1.11 | 1.11
160-183 GHz | 1.11 | 1.11
Swath (km) | ~2600 | ~2200
ATMS scan period: 8/3 sec; AMSU-A scan period: 8 sec

## Slide 10: Conical vs Cross Track Sounding
<number>
<number>
Large scan swath width (no orbit gap)
Same resolution for all frequencies
Mixing pol as scan from nadir to limb
Res varies with scan angle
Narrow scan swath width with orbit gap
FOV size is the same for all positions but
varies with frequencies
Same pol for all scan positions
Notes: <number>
<number>

## Slide 11: Comparison of Cross-track and Conical System for Hurricane Applications
<number>
Small gaps between orbits
Limb brightness or darkening effects
Lower noise due to an end2end calibration
Have the same FOV for all frequencies but varies with angle
Mixing polarization
Larger gaps between orbits
Uniform brightness temperature
Large noise due to its current calibration system
Have the same FOV at all scan positions but varies with frequency
Pure polarization
Cross track
Conical

## Slide 12: Hurricane Katrina from SSMIS at 54 GHz
Liu and Weng, 2006, GRL
Warm core features can be best observed from upper tropospheric conical sounding channels

## Slide 13: Hurricane Katrina from AMSU-A at 54 GHz
Warm core cannot not easily be identified from upper tropospheric cross-track sounding channels

## Slide 14: Warm Core of Hurricane Katrina Observed by AMSU-A at 54 GHz (Limb-Adjusted vs. Original)
Liu and Weng, 2006, JAMC
Hurricane warm is observed from limb-adjusted measurement AMSU-A
Original
Limb-Adjusted

## Slide 15: Trails and Traits of Hurricane Thermal Structure
<number>
When a hurricane reaches its mature stage, a warm core occurs near 200 hPa according to Hawkins, 1964

## Slide 16: Use AMSU-A/MHS in Microwave Integrated Retrieval System (MIRS) Typhoon Megi (Oct 16-29, 2010)
With MHS
Without MHS
In strong typhoon and hurricane conditions, strong scattering at MHS channels can’t be accurately simulated in forward model thus the retrievals near eye walls are often ill-performed and not convergent

## Slide 17: Hurricane Isabel Temperature Anomaly
Vertical cross section of temperature anomalies at 06:00 UTC 09/12/2003. Left panel: west-east cross section along 22N, and right panel: south-north cross section along 56 for Hurricane Isabel
Without Cloud/Precipitation Scattering
Notes: <number>
If the radiative transfer model does not include scattering scheme, the lower level max cold anomaly cloud go up to -12 K, which is physically not real.

## Slide 18: Hurricane Isabel Temperature Anomaly
Vertical cross section of temperature anomalies at 06:00 UTC 09/12/2003. Left panel: west-east cross section along 22N, and right panel: south-north cross section along 56W for Hurricane Isabel
With Cloud/Precipitation Scattering
Notes: <number>
We applied this scheme in the study of Hurricane Isabel (2003). This is the retrieved temperature anomaly. We found the max warm core anomaly is up to 12 K at about 250-hPa level. The max cold anomaly is about -8 K inside the lower level hurricane eyewall.

## Slide 19: Impacts of Forward Models on Hurricane Isabel
T(200hPa) – Emission only
T(200hPa) – Scattering
T(850hPa) – Scattering
T(850hPa) – Emission only
Notes: <number>

## Slide 20: Surface and Low-Level Winds of Hurricane Isabel
HRD surface wind analysis
at 0730 UTC 16 Sept. 2003.
AMSU derived 950 hPa wind
at 0600 UTC 16 Sept. 200316 Sep 2003.
Notes: <number>
We found the retrieved wind pattern can reproduce the realistic asymmetric structure, maximum wind speed, RMW. But the high wind speed area is larger than the observed.

## Slide 21
Validation with Dropsonde Data
0000 UTC 09/15/03, Isabel at 24.3N 67.9W, Pmin=933 hPa
AMSU-
derived
Dropsonde
measured
* Plotted by Bin Fu & Tim Li (University of Hawaii)

## Slide 22: Hybrid Variational Scheme for Assimilating AMSU/ AMSR-E Data
Background data:
Global Analysis-GDAS
Satellite observations:
AMSU and AMSR-E
4DVAR Analysis
plus quality control
Physical retrieval:
temperature profile
sea-surface wind
where X(ti) is observed atmospheric temperature and SSW; Wb and Wx are the error covariance for ackground and satellite measurements
Cost function:

## Slide 23: Hurricane Ophelia 2005
Above two figures compare GDAS analysis temperature field near 250 hPa with 1DVAR & 4DVAR analysis. The temperature field from analysis shows hurricane warm core is about 2 degree warmer than GDAS analysis. Uses of cloudy radiances under storm conditions dramatically improve warm core structure. At 0600 UTC September 07, 2005, Ophelia was at tropical storm intensity, with the minimum central pressure of 1003 hPa.

## Slide 24: Hurricane Katrina Analysis from AMSU/AMSR-E
Above two figures compare GDAS analysis temperature field near 250 hPa with 1DVAR& 4DVAR analysis. Uses of cloudy radiances under storm conditions dramatically improve warm core structure. At 0600 UTC August 25, 2005, Katrina was at tropical storm intensity, with the minimum central pressure of 1000 hPa.
Notes: <number>

## Slide 25: Hurricane Ophelia 2005
The 1DVAR plus 4DVAR analysis shows asymmetric surface temperature distribution, with a 2 K cooling rainband at northeastern side, which is consistent with the deep convections shown on NOAA-17 satellite AVHRR channel 4 image. This surface feature is attributed to uses of more AMSR-E radiances at 6 and 10 GHz which are sensitive to SST
4DVAR
GDAS

## Slide 26: Impacts of SSMIS LAS on Hurricane Temperature Analysis using WRF/GSI
Liu and Weng, GRL, 2006b
Control
Test

## Slide 27: Perspectives for Future Satellite Microwave Sounding Systems
<number>
MW sounders on Metop/NOAA/FY-3/DMSP can offer more observations
Use ATMS oversampling information for hurricane studies
Improve forward model for variational analysis
Propose to add more sounding channels on JPSS 2+ (e.g. 118 Ghz, 220 GHz)
Develop geostationary microwave sounding systems (e.g. GEOMAS and GEOSTAR)
Near-term
Long-Term

## Slide 28: Geostationary Microwave Array Spectrometer (GEOMAS) – MIT
<number>
“Hyperspectral” measurements allow the determination of the Earth’s tropospheric temperature with vertical resolution exceeding 1km
  ~100 channels in the microwave
Hyperspectral infrared sensors available since the 90’s
  Clouds substantially degrade the information content
  A hyperspectral microwave sensor is therefore highly desirable
Several recent enabling technologies make HyMW feasible:
  Detailed physical/microphysical atmospheric and sensor models
  Advanced, signal-processing based retrieval algorithms
  RF receivers are more sensitive and more compact/integrated
The key idea: Use RF receiver arrays to build up information in the spectral domain (versus spatial domain for STAR systems)
Bill Blackwell, 2010 MicroRad
Notes: <number>
Comparison of GeoMAS weighting functions with traditional 60-GHz bands (AMSU/ATMS sensors, for example).
<number>

## Slide 29: Geostationary Synthetic Thin Array Radiometeor (GeoSTAR) - JPL
<number>
All-weather soundings @ 2-4 km vertical resolution
  Full hemisphere @ ≤ 50/30 km every 30-60 min (continuous) - easily improved
  Standalone soundings; Also complements any GEO IR sounder
Rain
  Full hemisphere @ ≤ 30 km every 30 min (continuous) - easily improved
  Measurements: scattering from ice associated with precipitating cells
  Real time: full hemispheric snapshot every 30 minutes or less
Tropospheric wind profiling
  Surface to 300 mb; adjustable pressure levels
  Primarily horizontal wind vectors (at pressure levels)
  Very high temporal resolution possible
  Vertical winds may also be feasible (requires some research)
Rapid-cycle NRT storm tracking
  Scattering signal from hurricanes/convection detectable in < 5 minutes
  Switch to detect/track mode -> Update every 5 minutes (continuous)
4
Bjorn Lambrigtsen 2010 MicroRad

## Slide 30: Concluding Remarks
<number>
Satellite observations from cross-track and conical microwave sounding systems are vital for improvements in weather forecasts and climate monitoring
70-80% of measurements from satellite microwave sounding data are cloud-free and can be effectively used in current NWP systems
Extraction of hurricane thermal and water vapor structures requires a highly accurate radiative transfer model that can separate O2/H2O emission from hydrometeor scattering and emission
New microwave sounding technologies need to focus on better instrumentation and achieving lower noise (i.e., NEDT less than 0.2K)
Developments of new microwave sounding systems are significantly falling behind, compared with satellite infrared sounding systems