## Slide 1: Power spectra and eddy dissipation rate measured by the Coyote Unmanned Aircraft System in Hurricane Edouard (2014)
Evan Kalina
NOAA’s Hurricane Research Division and Physical Sciences Division
16 December 2016
AGU Fall Meeting
Collaborators: Joe Cione (NOAA/HRD/PSD), George Bryan (NCAR), Don Lenschow (NCAR), and Chris Fairall (NOAA/PSD). This research was performed while the author held a National Research Council Research Associateship Award at AOML/ESRL.

## Slide 2: Goal: Turbulence measurements in the boundary layer in hurricane conditions
Height (km)
3 km
2 km
1 km (Boundary layer)
Model
Heat, moisture, & momentum fluxes, power spectra, eddy dissipation rate are needed to evaluate/improve model parameterizations
w’θ’
____
Sensible heat flux = ρacp
w’q’
____
Latent heat flux = ρaLv
w’u’
____
Momentum flux = -ρa
Power spectral density of wind speed, eddy dissipation rate

## Slide 3: During CBLAST, the NOAA P-3 collected BL measurements
Height (km)
3 km
2 km
1 km (Boundary layer)
NOAA P-3
The Coupled Boundary Layer Air-Sea Transfer (CBLAST) experiment (French et al. 2007)
P-3 flew as low as 70 m in 2 storms
18-30 m s-1 wind speeds
Underscored need for additional data

## Slide 4: Today, the NOAA P-3 flies at 3 km. How do we obtain additional BL measurements?
Height (km)
3 km
2 km
1 km (Boundary layer)
NOAA P-3
Model
Coyote UAS
Measures p, T, RH, winds
Power spectrum?
Eddy dissipation?
Fluxes (not yet)
Dropsonde:
(10-20 per mission)
Snapshot at any one height

## Slide 5: Two methods for estimating dissipation Can each be applied to both wind components* separately
1) From power spectral density (Suu, Svv):
2) From second-order velocity structure function (Duu, Dvv):
*Here, u (v) is the wind component parallel (perpendicular) to the true heading of the Coyote.

## Slide 6: Several challenges exist in calculating spectra and dissipation rate from Coyote data
Winds were recorded at 1 Hz.
Data dropouts were frequent. 62% of the 1-second samples are missing.
Winds were derived from true air speed and GPS measurements.
How would we know if the estimates were reasonable?
The Coyote winds compare well with winds from dropsondes.
Multiple ways of estimating dissipation yield similar answers.
The power spectra used to estimate dissipation have well-defined inertial subranges with five-thirds scaling.
The ratio of the power spectra Svv:Suu = 4:3.
The structure functions used to estimate dissipation exhibit two-thirds scaling.
Dissipation in an LES model agrees with our estimates.
Other ways?

## Slide 7: Coyote and dropsonde analysis wind speeds agree to within 0.5 m s-1
COYOTE ALTITUDE
WIND SPEED
Δv = -0.5 m s-1
Dropsondes
Coyote
From Cione et al. (2016), ESS
Sept. 17, 2014: Inflow Exp.
Use this to calculate dissipation

## Slide 8: Suu: Well-defined inertial subrange with five-thirds scaling
Inertial subrange
Five-thirds line
Suu
Smoothed Suu
Epsilon (Suu)
Lines:
Epsilon (Duu)

## Slide 9: Svv: Well-defined inertial subrange with five-thirds scaling
Inertial subrange
Five-thirds line
Svv
Smoothed Svv
Epsilon (Svv)
Lines:
Epsilon (Dvv)
Poor agreement;
epsilon from Dvv is dependent on r

## Slide 10: Estimates of dissipation range from 0.1–3.5×10-4 m2 s-3
Epsilon from Dvv (distance dependent)
Epsilon from Duu
Epsilon from Svv
Epsilon from Suu

## Slide 11: In agreement with theory, mean(Svv:Suu) ≈ 4:3 in the inertial subrange
Svv:Suu
4:3
Mean(Svv:Suu)

## Slide 12: Duu scaling is 0.67, but Dvv scaling is 1.33 Theory requires two-thirds scaling for each
✅ Duu
❌Dvv
Recall that epsilon from Dvv did not agree with other estimates
Structure function value (m2 s-2)

## Slide 13: (Valid) estimates of dissipation range from 2–3.5×10-4 m2 s-3
Epsilon from Dvv (distance dependent)
Epsilon from Duu
Epsilon from Svv
Epsilon from Suu

## Slide 14: We can also use LES to analyze HBL turbulence characteristics
Created by Dr. George Bryan of PSU-NCAR
3D, non-hydrostatic, time-dependent, numerical model
Designed for deep convective systems
Two simulations:
“Complex” (CM1C) and “Simple” (CM1S)
Adequate measurements are rare due to instrument limitations & hazardous conditions during low-altitude reconnaissance flights
Large-eddy simulations (LES) can be used to analyze hurricane boundary layer (HBL)  simulate 3D-field of turbulent winds
Cloud Model Version I (CM1)1
1For more information: Bryan and Rotunno (2009), MWR
Slide courtesy of R. Worsnop

## Slide 15: CM1S simulation shows eddy characteristics in a small 6x6 km domain (dx = 20 m) Can be repositioned to analyze eddies at any wind speed
≈ 3000 km
≈ 6 km
LES domain
Slide courtesy of R. Worsnop

## Slide 16: (Valid) estimates of dissipation range from 2–3.5×10-4 m2 s-3
Epsilon from Dvv (distance dependent)
Epsilon from Duu
Epsilon from Svv
Epsilon from Suu
Epsilon from LES model

## Slide 17: Summary
Dissipation rate estimates from Coyote data at z = 760 m and v = 15–25 m s-1 are 0.1–3.5 × 10-4 m2 s-3.
The scaling of the transverse velocity structure function (1.33) departs from the theoretical expectation of two-thirds scaling; thus, the dissipation rate estimates from this structure function are likely incorrect.
Valid dissipation rate estimates are therefore 2–3.5 × 10-4 m2 s-3.
Large eddy simulations conducted with CM1 at comparable wind speeds to those observed by the Coyote suggest a dissipation rate of 3 × 10-4 m2 s-3, within the range estimated from the Coyote data.