## Slide 1
Robert Rogers
NOAA/AOML Hurricane Research Division
Miami, FL
Aircraft Observations of
Tropical Cyclones

## Slide 2
Motivation
Why are observations important?
Many important physical processes within hurricanes span scales that cover many orders of magnitude, ranging from thousands of kilometers to millionths of meters
Observations can span these scales, and are a key component of a balanced approach toward advancing understanding and improving forecasts of hurricanes (observations, modeling, theory)
Provide real-time information on TCs, assess performance of models, and provide a check on theories
Three primary platforms for observations –
airborne, spaceborne, and land-based
-- focus here on airborne

## Slide 3
Outline
Tools for observing hurricanes
Use of observations to improve hurricane forecasts
Flight profiles
Views from the aircraft

## Slide 4
In-situ
  Wind, press., temp.
Expendables
  Dropsondes
  AXBT, AXCP, buoy
Remote Sensors
  Tail Doppler Radar (TDR)
  SFMR
  Doppler Wind Lidar (DWL)
  Scanning Radar Altimeter
  Scatterometer/ profiler
Platforms
  Unmanned Aerial Systems (UAS)
UAS
1. Tools for observing hurricanes
5
P-3
G-IV
DWL
DWL
TDR
dropsonde

## Slide 5
“Kermit” Built in 1975 at Lockheed-Martin, Marietta, Georgia
“Miss Piggy” Built in 1976 at Lockheed-Martin, Marietta, Georgia
“Gonzo” Built in 1994 at Gulfstream Aerospace Corporation in Savannah Georgia
Tools for observing hurricanes

## Slide 6
Airborne radar
Radars on WP-3D

## Slide 7
eyewall
spiral rainbands
LF image of Hurricane Ivan (2004)
Lower Fuselage (LF) Radar

## Slide 8
Tail Doppler Radar
outward-sloping eyewall

## Slide 9
GPS dropsonde

## Slide 10
Steering flow
Variation in moisture content of environment around hurricane
Environmental structure
Synoptic-surveillance using dropsondes
Scales sampled by Airborne Observations
11

## Slide 11
Highest rain rates normally in eyewall, mostly convective, cover small area
Lighter rain rates in stratiform areas outside eyewall, cover larger area
eyewalls
stratiform
inner
eyewall
stratiform
Vortex Structure
Double eyewalls seen from airborne radar
outer
eyewall
Scales sampled by Airborne Observations

## Slide 12
Strong convection seen from radar
Convective Structure
ER-2 EDOP
P-3 TA
Vertical velocity (m/s)
Reflectivity (dBZ)
ER-2 EDOP
P-3 TA
Scales sampled by Airborne Observations

## Slide 13
Flight track and LF image
Cloud physics particle images
Microphysical Structure
Concentration of cloud physics (ice and water) particles
Scales sampled by Airborne Observations

## Slide 14
Global Hawk Aircraft (Unmanned Aerial System)
First Global Hawk landing at Wallops Flight Facility, Sept. 7, 2012.
can stay airborne for >24 h, compared with 8 h for P-3 and G-IV
New Airborne Platforms

## Slide 15
Global Hawk Operations Center (NASA Armstrong Base, CA)
New Airborne Platforms

## Slide 16
Long range of Global Hawk
Nadine’s track
21
26
32
28
30
(Hurricane and Severe Storm Sentinel, HS3, from 2012)
New Airborne Platforms

## Slide 17
MODIS
1640Z
1341Z
1420Z
1638Z
1316Z
1259Z
Coyote (Unmanned Aerial System)
released from P-3 like a dropsonde, can be controlled for ~2 h
can get measurements down to surface, where manned aircraft can not reach
Coyote measurements in Hurricane Edouard (2014)
New Airborne Platforms

## Slide 18
New Airborne Platforms
Depiction of Coyote launch

## Slide 19
Improving the specification of the initial state of the atmosphere (Data Assimilation)
Evaluating and improving the performance of numerical models (Model Evaluation)
Improving the understanding of tropical cyclone behavior (Hypothesis Testing)
2. Use of observations to improve hurricane forecasts

## Slide 20
25
Vertical cross section of wind speed in Isaac (2012) at start of model forecast
Without radar data
Improved representation of vortex tilt
With radar data
Use of Observations – Data assimilation
Impact of assimilating inner-core observations into forecast model
without radar
with radar
Forecast hour
Intensity forecast error
Use of airborne Doppler improved initial vortex structure
Resulting intensity forecast was improved
Many more cases must be evaluated, DA system must be improved (ongoing)

## Slide 21
Radial inflow for different model runs
0
1
2
30
90
150
210
270
radius (km)
height (km)
Old mixing version
modeled inflow
Inflow depth based on observations
Inflow layer too deep
Inflow strength too weak
Use of Observations - Model evaluation
Sensitivity of radial wind to mixing processes in low levels
peak radial inflow stronger with more accurate mixing
depth of inflow layer more consistent with dropsonde composites using more accurate mixing
30
90
150
210
270
radius (km)
New mixing version based on observations
Inflow depth based on observations
height (km)
0
1
2
modeled inflow

## Slide 22
Reflectivity, echo tops, and upper-level updrafts in Hurricane Edouard (2014)
Use of Observations – Hypothesis testing
Hypothesis: TC intensification is favored when convection exists upshear inside RMW
Lower fuselage reflectivity (shaded, dBZ)
20 dBZ echo top heights from airborne Doppler (shaded, km)
Peak updrafts in 8-16 km layer from airborne Doppler (shaded, m/s)
RMW
144 km
144 km
14 Sept - RI
shear
shear
RMW
144 km
144 km
16 Sept - SS
14 Sept (RI period): Strong updrafts, high echo tops upshear left and inside RMW
16 Sept (SS period): Weaker updrafts, mostly downshear left, at RMW
Can we predict likelihood of persistence of convection upshear based on obs, model?
shear
shear
high echo tops
RMW
RMW
strong updrafts

## Slide 23
3. Flight profiles

## Slide 24: Aircraft sampling of TCs
10 mi
Notes: Aircraft provide the best way to observe hurricane wind and pressure.
Aircraft flights into hurricanes began near the end of WWII (1945) to provide location, movement, and intensity observations for forecasters. We fly through the storms near the bottom to enable estimates of surface winds using flight-level, radar, dropsondes and SFMR observations.
AF WC-130s and P-3s fly at or below 2 mi altitude (10,000 ft), G-IV flies at 9 mi altitude (45,000 ft)

## Slide 25
P-3 and G-IV Atlantic bases of operations
Assuming 2 hours of on-station time
P-3
G-IV

## Slide 26
Sample P-3 Flight track into Hurricane Hermine
September 1, 2016
Lower fuselage reflectivity (shaded, dBZ) and flight-level winds (kt)
Flight track and flight-level winds (kt)
(5) Offshore intense convection module:
NW IP, upwind to SW, cross band, downwind to NE endpoint. Drops at turns and midpoints
(bad drop at end of upwind leg)
IP
2
3
4

## Slide 27
4. Views from the aircraft

## Slide 28
Inside the P-3 Aircraft

## Slide 29
Dropsonde release on P-3

## Slide 30
Inside the G-IV Aircraft

## Slide 32
low clouds above
sea-surface
eyewall
Within the Eye of Hurricane Georges (1998)

## Slide 33
In the Eye of the Hurricane Isabel (2003)

## Slide 34
Wind-blown streaks
Breaking waves
Sea state under Hurricane Isabel (2003)

## Slide 35
Low-level flight

## Slide 36
Stadium effect

## Slide 37
Impressed scientists

## Slide 38
Thank you!