## Slide 1: SFMR Re-calibration
Heather Holbach
AVAPS Users group meeting
April 14, 2021

## Slide 2: Motivation
Inconsistencies noted between the dropsonde, SFMR, and flight-level surface wind speed estimates
  Especially in major hurricanes
Avila et al. (2020) Fig. 2

## Slide 3: How does the SFMR algorithm work?
SFMR Measured TBs
Compute Modeled TB
Minimize Error in Fit
Across Frequencies
Wind Speed and Rain Rate
Air Temperature, Salinity, Altitude, Roll Angle, SST (satellite)
Wind Speed and Rain Rate Guess
Wind-Induced Emissivity Curve

## Slide 4: Wind Speed Fit to Sondes
2004 to 2018
19.4 kt
38.9 kt
58.3 kt
77.8 kt
97.2 kt
116.6 kt
136.1 kt
155.5 kt
Klotz and Uhlhorn (2014) Fig. 11b

## Slide 5: Collocation Challenges in High Winds

## Slide 6: Dropsonde Overflights

## Slide 7: Dropsonde WL150

## Slide 8: New Wind-Induced Emissivity Curve
Note: SFMR values are 10-sec centered average
Revised = Klotz and Uhlhorn (2014)
Operational = Uhlhorn et al. (2007)

## Slide 9: Hurricane Dorian (2019)

## Slide 10: Hurricane Dorian (2019)
9.7 kt
19.4 kt
29.1 kt
19.4 kt
38.9 kt
58.3 kt
77.8 kt
97.2 kt
116.6 kt
136.1 kt
155.5 kt
175.0 kt

## Slide 11: Summary
Increased dropsonde collocation time period from 2005–2012 (1513 sondes) to 2004–2018 (2390 sondes)
  Collocations are with SFMR at time of dropsonde launch
    Storm-relative collocations require more accurate surface storm center locations
Dropsonde overflights will help reduce spatial errors in collocations
WL150 surface reduction methodology may need updating
Interpretation of eyewall near-surface dropsonde observations is challenging
New curve results in reduced wind speeds above ~40 m/s (~77 kt)
  Is there anything else we need to account for at these wind speeds?

## Slide 12: Extra Slides

## Slide 13: Storm-relative Collocations
Previous algorithm updates used SFMR at time of dropsonde launch
Assuming wind speed is azimuthally similar around a TC, using same radial position of SFMR as the dropsonde from the center should provide improved match-up
  Very sensitive to accuracy of center

## Slide 14: Updating Wind-Induced Emissivity Curve
Klotz and Uhlhorn (2014) Criteria:
  Usfc ≤ 35 m/s: RR ≤ 2 mm/hr
  35 m/s < Usfc ≤ 60 m/s: RR ≤ 10 mm/hr
  Usfc > 60 m/s: all RR
Current Emissivity Curve:
Usfc: WL150 surface-adjusted wind speed
RR: SFMR rain rate
wl = 7.0 m/s wu = 37.0 m/s
a1 = 0. 1232e-2 a2 = 0. 3440e-2 a3 = 0. 02492e-2
a4 = 0. 007020e-2 a5 = -0.9266 a6 = 0.5444e-2

## Slide 15: New Wind-Induced Emissivity Curve
New Rain Rate Criteria:
  Usfc ≤ 35 m/s: RR ≤ 2 mm/hr
  30 m/s < Usfc ≤ 50 m/s: RR ≤ 10 mm/hr
  Usfc > 50 m/s: RR ≤ 40 mm/hr
New wu: 47.0 m/s
a1 = 0.1205e-2 a2 = 0.2670e-2 a3 = 0.03298e-2
a4 = 0.007046e-2 a5 = -0.1396 a6 = 0.6669e-2
Note: SFMR values are 10-sec centered average

## Slide 16: Frequency Dependence
Using 0 mm/hr
Using SFMR rain rate

## Slide 17: Wind-Induced Emissivity Curves

## Slide 18: Hurricane Irma (2017)

## Slide 19: Hurricane Irma (2017)
19.4 kt
38.9 kt
58.3 kt
77.8 kt
97.2 kt
116.6 kt
136.1 kt
155.5 kt
175.0 kt
9.7 kt
19.4 kt
29.1 kt

## Slide 20: Hurricane Maria (2017)

## Slide 21: Hurricane Maria (2017)
19.4 kt
38.9 kt
58.3 kt
77.8 kt
97.2 kt
116.6 kt
136.1 kt
155.5 kt
175.0 kt
9.7 kt
19.4 kt
29.1 kt

## Slide 22: Hurricane Michael (2018)

## Slide 23: Hurricane Michael (2018)
19.4 kt
38.9 kt
58.3 kt
77.8 kt
97.2 kt
116.6 kt
136.1 kt
155.5 kt
175.0 kt
9.7 kt
19.4 kt
29.1 kt