## Slide 1
NOAA/AOML XBT Operations
XBT Network Review. AOML, Miami. Feb. 7, 2017
Francis Bringas, on behalf of the AOML XBT Network team

## Slide 2
50 Years of XBT Operations
50 Years of XBT Operations
XBT Network Review. AOML, Feb. 2017
NOAA/AOML XBT Operations
AOML started XBT operations in 1967 with deployments along AX10 (Newark to San Juan).
XBT operations have since been conducted in different modes (low density, frequently repeated, high density) according to scientific and operational needs, and have expanded to global coverage.
XBT-derived temperature profiles represent now between 10% and 15% of all global, non-mooring, temperature profiles. The main contribution of the XBT network is to provide temperature measurements to:
 Monitor changes of key surface and subsurface currents,
 Assess meridional heat transport in all ocean basins,
 Help initialize and validate climate and weather numerical forecast models, and
 Supplement other observational platforms to assess the variability of the global upper ocean heat content.

## Slide 3
OceanObs09
50 Years of XBT Operations
50 Years of XBT Operations
XBT Network Review. AOML, Feb. 2017
NOAA/AOML XBT Operations
Number of global XBT deployments since 1965. US XBT operations have been consistently responsible for at least 50% of these global deployments (68% in average).

## Slide 4
AX08
AX01
IX01
AX10
AX07
AX97
AX18
AX25
AX32
AX02
AX90
MX04
50 Years of XBT Operations
Status of AOML XBT Operations
XBT Network Review. AOML, Feb. 2017
Frequently Repeated:
6 - 8 deployments per day
1/100 km – 1/150 km
12 - 18 transects per year
High Density:
1 deployment every 25 - 50 km
18 - 35 deployments per day
4 transects per year
NOAA/AOML XBT Operations
The Global XBT Network

## Slide 5
50 Years of XBT Operations
Status of AOML XBT Operations
XBT Network Review. AOML, Feb. 2017
Location of the AOML XBT deployments and AOML-supported XBT deployments and/or transmissions during FY2016 carried out by AOML or in partnership with national and international collaborators.
NOAA/AOML XBT Operations

## Slide 6
50 Years of XBT Operations
Status of AOML XBT Operations
XBT Network Review. AOML, Feb. 2017
Name | Since… | No. of Cruises* | No. of XBTs*
AX01 | 1997 | 90 | 2,438
AX02 | 2008 | 24 | 1,181
AX07 | 1994 | 89 | 20,437
AX08 | 2000 | 65 | 22,777
AX10 | 1996 | 78 | 7,894
AX18 | 2002 | 48 | 10,013
AX20 | 1995 | 9 | 1,463
AX25 | 2004 | 33 | 4,267
AX32 | 1975 | 149 | 3,277
AX97 | 2004 | 65 | 2,771
MX01 MX02 MX04 | 1999 | 223 | 11,135
IX01 | 1983 | 203 | 13,722
* Since 2000; AX01 in FR, all other in HD mode.
1. More than 100,000 XBTs deployed during ~1100 cruises since 2000.
2. Operations in partnership with 8 countries during recent years.
3. All data distributed in near real-time (GTS) in delayed mode (NCEI).
4. XBT data has been used in more than 1500 scientific and technical publications since 2000.
NOAA/AOML XBT Operations

## Slide 7
50 Years of XBT Operations
Ship Recruitment, Logistics, Ship Riders
XBT Network Review. AOML, Feb. 2017
More than 15 shipping companies
Between 30 and 40 ships per year
More than 45 cruises per year in high density mode
Operations in partnership with 10 institutions from 8 countries
Approximately 20 riders from US and our partners
Luis Yurquina from the Argentine Hydrographic Service during an AX18 Cruise on MOL Triton Ace
NOAA/AOML XBT Operations
CMA CGM Rabelais and NYK Prometeus Leader ships used during AX07 and AX10 cruises
AX07 cruise starting at the Strait of Gibraltar
High Density XBT cruise equipment installation

## Slide 8
50 Years of XBT Operations
Engineering Developments
XBT Network Review. AOML, Feb. 2017
AOML XBT Autolauncher
Deployments at fix time or distance intervals, or at fixed locations.
Allows 24h operations with a single rider doing frequent deployments for weeks.
Portable. Easy installation and removal.
AOML Iridium Transmitter
Developed at AOML in 2010-2012, fully transitioned into operations since 2015.
Reliable and efficient transmissions of arbitrary types and amounts of data.
Reduced costs from $15 to $0.95 per profile (saving of over $200,000 a year).
Development team received a NOAA Team Member of the Month award and a NOAA Administrator’s Award during 2016.
AOML XBT Data Recorder (AXR)
Under development, prototype already tested on the field.
Will replace current recording units ($9,000 per unit).
NOAA/AOML XBT Operations
AOML XBT Autolauncher
AOML Iridium Transmitter
AOML XBT Data Recorder
Notes: AL saves money for using a single rider working 24h a day operations. Can install multiple ALs

## Slide 9
50 Years of XBT Operations
Software Developments
XBT Network Review. AOML, Feb. 2017
AMVERSEAS and SEAS Server
AMVERSEAS software developed at AOML to collect and transmit XBT, TSG and MET observations
Installed in more than 50 ships of the XBT Network (14,000 XBT profiles per year)
Also used to send Amver bulletins to the US Coast Guard for search and rescue
AMVERSEAS and the SEAS server also distributes 500,000 marine weather reports obtained from 800 ships of the Voluntary Observing Ship program
Crew of the M/V Cape Nelson and survivors from the fishing vessel Abound that sank 625 miles off the coast of San Francisco, whose rescue was facilitated through AMVERSEAS on October 26, 2005
NOAA/AOML XBT Operations

## Slide 10
50 Years of XBT Operations
Software Developments
XBT Network Review. AOML, Feb. 2017
Locations of the approximately 500,000 marine weather reports obtained from 800 ships of the VOS distributed through the GTS using SEAS software during FY2016.
NOAA/AOML XBT Operations

## Slide 11
50 Years of XBT Operations
Data Flow and Data Management
XBT Network Review. AOML, Feb. 2017
Almost 100% of XBT profiles are transmitted in real-time using Iridium Transmitters.
AOML and SIO XBT profiles undergo near-real time automatic quality control (AQC) procedures at AOML + Visual QC for profiles that fail the AQC.
Good profiles (95%) are transmitted to the GTS in near real-time and distributed / archived at NCEI (WOD and GTSPP).
AOML XBT profiles collected in HD cruises also undergo a science quality delayed time QC. Final QCed profiles are delivered to NOAA/NCEI for archival and replacement into the “Best Quality” GTSPP data set.
Transmission into the GTS are done according to all data format requirements, including data in BUFR format and additional meta-data.
Data management procedures ensure that the XBT data reaches the operational and scientific community in a timely manner and with the highest possible quality.
NOAA/AOML XBT Operations

## Slide 12
50 Years of XBT Operations
Data Quality Improvements
XBT Network Review. AOML, Feb. 2017
AOML conducts experiments in order to improve XBT data quality.
AOML maintains a strong collaboration with Sippican for the improvement and development of new, more accurate, XBT probes.
AOML is actively involved in the use of new technologies for data collection and transmission, including the development of a new XBT data recorder.
New file formats (i.e. BUFR) are constantly used in order to include additional metadata needed for data corrections.
The integration of meteorological sensors in some cruises will increase the value of the XBT data collected.
NOAA/AOML XBT Operations

## Slide 13
50 Years of XBT Operations
Meetings and International Panels
XBT Network Review. AOML, Feb. 2017
AOML XBT Network is implemented through the Ship Of Opportunity Program, a participating member of JCOMM and JCOMMOPS.
AOML XBT Network is represented during bi-annual WMO/IOC Ship Observations Team (SOT) meeting. Dr. Gustavo Goni is the vice-chair of the WMO/IOC Ship Of Opportunity Program Implementation Panel (SOOPIP).
Other members of the AOML XBT group are part of Meta-T panel and the JCOMM Data Management Programme Area (DMPA) Task Team on Table Driven Code Forms, JCOMM DMPA Task Team on Table Driven Code Forms, the SOT Task Team on Instrument Standards and the SOT Task Team on Training.
Dr. Gustavo Goni is the co-chair for operations of the XBT Science Team, together with Dr. Janet Sprintall (SIO, for science) and Ms. Rebecca Cowley (CSIRO, for data management). Other members of the AOML XBT group are also part of the XBT Science Team.
AOML conducts an annual XBT Operations meeting.
AOML participate in other data management groups including GTSPP and IQuOD.
NOAA/AOML XBT Operations
GTSPP
Notes: Participation on these international panels provides an important mechanism for integrating and coordinating with other national or regional programs which, in the long run, improves our national climate mission by making more efficient and effective use of available resources.

## Slide 14
50 Years of XBT Operations
Future Work
XBT Network Review. AOML, Feb. 2017
Continue the application/development of new technologies for data acquisition and transmission (Amverseas, Iridium Transmitter, AOML XBT recorder).
Continue the development and maintenance of a flexible XBT data management system that meets all the community requirements for data dissemination and applications.
Add atmospheric sensors in some cruises to increase the value and applications of XBT data.
Take advantage of the BUFR format capabilities for the dissemination of XBT data in near real time in full resolution and with a complete set of meta-data and quality control (QC) flags.
Apply to the XBT profiles the QC experience and software development currently underway at AOML for glider observations.
NOAA/AOML XBT Operations