New AOML visual quality control software

The Visual Quality Control (VQC, Figure) is a Graphical User Interface (GUI) developed at AOML Miami that allows a user to approve or reject XBT profiles that have not met the minimum specified standards of the Automatic Quality Control System.  Accepted profiles are automatically sent to the GTS.  When the operator rejects a profile, the data-flow process automatically receives a message to not place that profile in the GTS.  AOML does a VQC for an average of 2 profiles every day, which can vary dramatically if there are high-density cruises being done or communication problems.  A useful advantage of the VQC is the real-time ability to recognize systemic and random problems with the XBT operations, such as electrical faults in the XBT hand-launchers, or bad weather carrying the XBT wires to contact the hull of the ship.  The AOML VQC system is an upgrade to the previous VQC Matlab script used in Silver Spring, with additions of incorporating geographical position, proximity to other profiles in time or position, and an easy to use GUI.  The VQC GUI allows the user to evaluate the profile based on seeing error envelopes for both 5 and 10 standard deviations. Additionally, all flagged profiles in the queue are shown in a secondary graph to easily visually compare physical features.  The GUI also has user-friendly mouse enabled features such as zoom and profile selection.

Figure.  Screen shot of the new AOML Visual Quality Control (VQC) for XBT profiles. The main graph displays an envelope of 5 and 10 standard deviations, the climatology (blue line) and the XBT profile (red line).

\

Implementation of Iridium transmissions in SEAS XBT transects

Most XBT profiles from AOML SEAS operations are sent through the Thrane Standard C units.  AOML is now continuously using Iridium transmission in the XBT and TSG operations in the Oleander (AX32) using a direct Internet connection and SMTP e-mail.

Implementation of TSG transmissions using Iridium

During 2008 the TSG Iridium transmission system was successfully tested in the M/V Explorer and on the M/V Oleander.    The SEAS 2000 software was implemented for easy setup and to require no user input once started.  The TSG computer resides in the engine room and collects data from the TSG junction box and time/position stamps the TSG data.  The TSG Server can read GPS data in two possible ways either from the Time Server or from the TSG junction box.  If the TSG module collects GPS data from the junction box it can pass on this GPS data to the Time Server for use by SEAS 2K if necessary.  The TSG data is transferred to the bridge over the ship intranet and can then be transmitted. TSG collection and transmission was added as a standalone component interfacing to the SEAS 2K Time/Position Server.