# GasEx 98 Leg 3 pCO2 Data Reduction Notes

Cruise start:	June 28, 1998	Punta Del Gado, Azores

Cruise end	July 7, 1998	Miami, Fl

Standard Tanks:

Set 1

Low:	275.63	CC114999	1920 PSI

Mid:	297.74	CC117904	800 PSI

Hi:	360.62	CC106641	1990 PSI

Set 2

Low:	297.74	CC117904	800 PSI

Mid:	360.62	CC106641	1990 PSI

Hi:	408.35	CC111795	1050 PSI

Equilibrator Mercury Thermometer:	Brooklyn Serial No. 75293

Thermistor Algorithm:	102.04 – 48.88V + 10.785V2 – 1.2714V3

Thermistor Calibration performed on April 8, 1998.

Notes from Green Log Book:

Gas flow thru sample cell in water phase was low from beginning of leg until June 30 at 1100.

7/3/98, 0230:		System down due to power failure.

Changed STD tanks at 1545 on July 5, 1998.  (See Set 2 above).

Below are rows where fixes have been made:

551-3:		Changing desiccant, flagged concentrations as bad.

- Interpolated SCS Temp and Sal.

1593-1603:	System down for power failure.  Added Rows, interpolated lat, lon, Jday, SCS, and Eq Temp.

2449-51:	Changed STD tanks.  Added rows.  Interpolated lat, lon, Jday, SCS, and Eq Temp.

2453:		Added row.  Interpolated lat, lon, Jday, SCS, and Eq Temp.

3075-7:	Extrapolated previous hour’s average air value.