Cruise:  VICARAM VI 2003

Ship:  unknown

Dates:  April 10-22, 2003

Chief Scientist:  not applicable

Equipment:  24 bottle CTD with dual C, T, and O2 sensors and LADCP

Number of Stations:  7

Sample Collection

DIC:

5 stations, 20 samples each 500-ml

PI:  Dr. Rik Wanninkhof, AOML

Analyzed by:  Esa Peltola, AOML

Sample Analysis

DIC:

Analysis Date: June 9-10, 2003.

Coulometers used: AOML1 and AOML2

Blank range: 12.0-16.1 counts/min

CRM # used and assigned value (include both DIC and salinity): Batch 59, c:2007.1 umol/kg, S:33.316

CRM value measured:  AOML 1: offset 4.8 umol/kg (2002.2 umol/kg, Batch 59)

AOML-2: offset 13.0 umol/kg (1994.1 umol/kg, Batch 50)

The average run time was 11 minutes, the minimum run time was 8 minutes and the maximum run time was 15 minutes.

Reproducibility: (# samples and average difference): 0 sets of duplicate samples

CRM, salinity and HgCl2 correction applied: yes

Comments

The Sample_ID is the rosette niskin bottle number from which the discrete samples were drawn.