Cruise:  WBTS  KN11-

Ship:  R/V Knorr

Dates:  April 26– May 2, 2011

Chief Scientist:  Bill Johns U. Miami/ Chris Meinen, AOML

Equipment:  Samples collected from Niskins.

Total number of stations:  4

Sample Collection

The discrete samples were collected by AOML PhOD personnel, Kyle Seaton, Chris Hughes, Pedro Pena and Greta Leber from Niskins bottles.  Salinities are those reported by the CTD. Temperatures are from CTD annoted on the sample log sheets.

The date and time listed in the data file are UTC when each sample bottle was collected.

DIC:

4 locations, 40 samples each 500-ml, 5 sets of duplicate samples. A total of 4 stations;  one cast to 4900 m was sampled at 23 depths; 3 stations had 4 samples to a depth of ≈  700-500 m

PI:  Dr. Rik Wanninkhof

Analyzed by:  Robert Castle

TAlk:

4 locations, 40 samples each 500-ml, 5 sets of duplicate samples. A total of 4 stations;  one cast to 4900 m was sampled at 23 depths; 3 stations had 4 samples to a depth of ≈  700-500 m.

PI:  Dr. Rik Wanninkhof

Analyzed by:  Dr. Leticia Barbero

Sample Analysis

DIC:

Analysis date: July, 2011

Coulometer used: AOML3 &4  (DICE 3 &4)

Samples were run on two DICE that each were experiencing problems with high blanks and interface issues causing the loop temperatures not to be read and, by using a default of “0” causing  incorrect cal. Factors.  All calculations had to be done from scrap.  Sample bottles 179,178,and 180 had quality flags of “4” . The calculated value looks OK but CRM  was > 165 too high.

Blank: average = 24; minimum = 14; maximum = 30 counts

Run time: average = 13; minimum = 8; maximum = 20 minutes

CRM # used and assigned value (include both DIC and salinity):

Meas CRM	cert CRM	meas sal	cert sal		batch

2171.53	2006.5		32.801		33.357		80

for bottles 179,178, 181: all QC’d as “4”

2005.98	2006.5		33.114		33.357		80

2006.47	2006.5		32.049		33.357		80

2002.01	2000.44	33.11		33.326		85

Reproducibility: (# samples and average difference): 4 sets of duplicate samples, average difference 1.3 umol/kg  (standard deviation of 4 differences = 1.1 umol/kg). One duplicate discarded.

CRM, salinity and HgCl2 correction applied: Salinity correction was applied using salinity from CTD  (that is, corrected the density)

Remarks-

The volume correction was applied due to added HgCl2 (Measured DIC*1.00037).

The first CRM of each cell was used for a CRM correction.

Comments

TAlk:

The results posted are duplicate analyses from the same DIC sample bottles.

Analysis date: 08/15/2011 to 08/17/2011

Titration system used: Open cell

CRM # used and assigned value:

Meas CRM	cert CRM	batch

2175.90	2212.40	96

2145.12	2184.03	85

2152.75	2184.03	85

Reproducibility: (# samples and average difference): 5 sets of duplicate samples, average difference 2.4 umol/kg ± 1.6 umol/kg.

CRM correction applied. CRMs ran at start and end of the analyses were used for the CRM correction.

Remarks-

Comments

I assume oxygen data was obtained- get data