Expocode	AGSK20061014

Cruise name 	SKO611

README file for Skogafoss cruises 609 through 721.

This dataset is heavily edited, manipulated, and screened compared to the original files because the thermosalinograph (TSG) temperatures are believed to be inaccurate.  The data of 11 cruises is merged in to a single file. The individual original files  can be found at http://www.aoml.noaa.gov/ocd/gcc/skogafoss_introduction.php.

Name			Wanninkhof, Rik

Organization		NOAA/AOML

Address		4031 Rickenbacker Causeway, Miami Fl 33149

Phone			305-361-4379

E-mail			rik.wanninkhof@noaa.gov

DatasetID		SKO610

Submission		2013/04/01

Experiment name	Skogafoss underway pCO2 data

Geographic Region	Northwest Atlantic between Norfolk, USA and Reykjavik, Iceland

Bounds West_long     -77.5 E (that is 77.5 W)

East_long	-20  E

North_lat	66.40 N

South_lat	36.84 N

Start date		2006/08/18

End date		2007/06/02

Ports of call		CITY                          		LATITUDE     LONGITUDE

Reykjavik, Iceland            	64.150       -21.855

Argentia, Newfoundland        47.296       -53.984

Shelbourne, Nova Scotia       	43.753       -65.322

Boston, Massachusetts         	42.390       -71.054

Philadelphia, Pennsylvania    39.850       -75.341

Newport News, Virginia        	36.963       -76.417

Richmond, Virginia            	36.517       -77.417

Vessel			Skogafoss

Vessel ID		SKO	 callsign V2XM

Country		Iceland

Vessel owner		Eimskip lines

Variable Info:

COLUMN  HEADER             	EXPLANATION

1.      EXPOCODE			Universal unique cruise identifier

2.      GROUP_SHIP:                    	AOML/SKOGAFOSS

3.      CRUISE_ID:      		SKOYNN (where Y is Year and NN is 								the cruise #).

4.      Year_Fractional			Decimal year (XXXX.YYYYY)

5.      JD_GMT:                        	Decimal year day

6.      DATE_DDMMYYYY:             UTC Date

7.      TIME_HH:MM:SS:                  UTC Time

8.      LAT_DEC_DEGREE:              Latitude in decimal degrees (negative

values are in southern hemisphere).

9.      LONG_DEC_DEGREE:           Longitude in decimal degrees (negative

values are in western latitudes).

10.      xCO2_EQU_PPM:                     Mole fraction of CO2 in the equilibrator at

equilibrator temperature (Teq) in parts per

million.

11.     xCO2ATM_PPM_measured:   Mole fraction of CO2 in air in ppm measured

12.     xCO2_ATM_PPM_assigned:	Average monthly air value for midpoint of 									cruise 	determined from average of ESRL-									GMD flask values in Macehead, Ireland; the 								Azores; and Reykjavik, Iceland.

13.     PRES_EQU_hPa:                	Barometric pressure measured in the 									equilibrator in 	hectopascals (1 hectopascal = 							1 millibar)

14.     PRES_SEALEVEL_hPa:         Barometric pressure from ship's 									barometer. No ship barometer was logged so 							it was assumed to be (Pres_equil-3mB) 								throughout

15. 	TEMP_EQU_C:                     Temperature in equilibrator water in degrees

centigrade. (SEE NOTES HOW THIS IS								DETERMINED)

16.     SST_C:      	                  	Sea Surface Temperature in degrees 									centigrade (SEE NOTES HOW THIS IS 								DETERMINED)

17.     SAL(TSG)_PERMIL:               Salinity from the ship's thermosalinograph 								on the Practical Salinity Scale.

18.     fCO2_SW@SST_uATM:         Fugacity of CO2 in seawater in microatm

19.     fCO2_ATM_uATM:                 Fugacity of CO2 in air in microatm

20.     dfCO2_uATM:                    	Seawater fCO2 - air fCO2 in microatm

21.     QC_flag				Quality control flag 2= good, 3=

questionable; 4=  bad

22.      QC_sub_flag			Indication of problem. Note the primary QC

can be 2,3, or 4 depending on nature and magnitude of problem.

(0= no problem, 1 = outside standard range, 2 = bad SST, 3 = bad EqT, 4 = bad ΔT, 5 = excess warming, 6 = bad salinity, 7 = bad

pressure, 8 = low gas flow, 9 = bad air

value, 10 = interpolated standard, and

11 = miscellaneous)

note: the default value is -999

Method description:

Equilibrator						showerhead  0.7 L water, 0.8 L headspace

Water flow rate					1-3 l/min

Headspace gas flowrate				≈ 100-200 ml/ min

Vented							Yes

Measurement methods				stop flow analysis with venting

Gases							Scott Marin- calibrated against 4 primary 								standards produced by CD Keeling SIO

From April 16, 2006 to October 24, 2006

STANDARDS/CONC    TANK #

Std 1    197.74	    fa02271

Std 2    455.18	    fa02435

Std 3    373.20	    ja02282

Std 4    293.50	    fa02255

From October 24, 2006 to Jun 2, 2007

STANDARDS/CONC    TANK #

Std 1    197.74	    fa02271

Std 2    453.77	    ja02299

Std 3    373.20	    ja02282

Std 4    249.51	    fa02450

CO2 Sensor						LI-6262 s/n 1241

UW pCO2 system name				"CNN generation 1"

positioned in engine room of Skogafoss  Temperature sensor					Hart model 1521

Steinhart-Hart thermistor polynomial, YSI 								400 (2252 ohms) 0 °C to 50 °C: ±0.005 °C  								Sensor   inserted through top of equilibrator 								and tip submerged about 6 cm below water 			surface

Pressure sensor					Vaisala pressure trans PTB 210C6C1M 								connected to headspace of equilibrator 				       Accuracy ±0.20 hPa

Data link:  http://www.aoml.noaa.gov/ocd/gcc/skogafoss_introduction.php

Data reduction of QC procedures for file SKO_609_721:

The xCO2ATM and xCO2_EQU  values as recorded were retained and only the fCO2 values were corrected or deleted.  For entries were xCO2ATM is presented the QC flag refers to the air value and is only a reflection of the measurement and will be flagged 2 even if it, for instance, appears to be contaminated by stack gases .

1. Correction of SST by -0.16 C

From comparison cross-overs with the  Nuka Artica (Olsen, U. Bergen Norway) and XBT surface temperatures from the Skogafoss (Reverdin and Colbiere, U. Paris) that the SST measured with the TSG (without a remote probe) on the Skogafoss were too high. This is due to the TSG being positioned well away from the intake on a shunt line. Olsen estimated a temperature offset ranging from 0.3 C in the wintertime to 0.1 C in the summertime for 2004 and 2005 data.  To estimate the offset we for the cruises 609-721 J. Trinanes co-located Reynolds optimal interpolated (OI) SST (1/4 degree daily resolution) with the Skogafoss. The average offset was 0.16 +- 0.87 C ((SST_TSG)-SST_(Reynolds OI)) n= 51095.  While cruise to cruise differences were discerned there was no consistent trend with any other measured parameter (time of year, SST etc).  Thus we corrected all the TSG_SST by  -0.16 C in the attached file.  The resulting biases between Reynolds IO SST and the corrected SST (= TSG_SST-0.16) per cruise is:

| cruise | Count | Avg ((TSG-0.16)-Reynolds) | Stdev |
| --- | --- | --- | --- |
| 609 | 2774 | 0.12 | 0.62 |
| 610 | 3985 | 0.01 | 0.70 |
| 611 | 6417 | 0.30 | 0.83 |
| 612 | 6159 | 0.22 | 0.80 |
| 613 | 4081 | 0.10 | 0.86 |
| 701 | 2113 | -0.18 | 0.60 |
| 705 | 5546 | -0.09 | 0.87 |
| 709 | 7157 | 0.12 | 0.98 |
| 713 | 4328 | 0.09 | 1.07 |
| 717 | 5806 | -0.04 | 1.15 |
| 721 | 2729 | -0.20 | 1.14 |

The average difference between the corrected SST (=TSG- 0.16 C) and equilibrator temperature (EqTemp) is :

| cruise | Count | Avg(EQT-(TSG-0.16)) | Stdev |
| --- | --- | --- | --- |
| 609 | 2751 | 0.38 | 0.07 |
| 610 | 3829 | 0.35 | 0.06 |
| 611 | 6237 | 0.30 | 0.05 |
| 612 | 5831 | 0.31 | 0.05 |
| 613 | 4003 | 0.35 | 0.04 |
| 701 | 1980 | 0.31 | 0.02 |
| 705 | 5229 | 0.34 | 0.04 |
| 709 | 6997 | 0.35 | 0.07 |
| 713 | 4180 | 0.35 | 0.05 |
| 717 | 5853 | 0.32 | 0.06 |
| 721 | 2539 | 0.33 | 0.04 |
| Average |  | 0.34 |  |
| St Dev |  | 0.02 |  |

The tight correlation between the EqTemp and SST suggests that the cruise-to-cruise differences in SST and Reynolds can be attributed to the large uncertainty in this comparison and that a single offset of 0.16 C is warranted rather than applying offsets per cruise.

2. Faulty Teq reading.

For about 100 instances (primarily cruise 721) the Hart Teq was not logged properly by deleting one or two digits. In these instances fCO2w was not calculated and flagged as 4.

3.   Large difference Teq-SST   note: SST = TSG-0.16

If  ABS(Teq-SST) > 1 the fCO2w value was deleted. This caused 239 values to be flagged as 4

4. Use of XCO2air values from ESRL_GMD

XCO2 air values were variable throughout the cruise. Because no relative wind directions were available screening for stack gas is difficult.  The xCO2A_PPM in column 10 contains the measured air values.  The interpolated values are the average value from ESRL-GMD flask network  for Azores, Ireland (Mace Head), and Iceland (http://www.esrl.noaa.gov/gmd/ccgg/flask.html).  The Table below shows the average observed values from the ship with stdev. along with the minimum values and average values for each cruise is shown below . Note, before the cruise averages were calculated all XCO2 values > 400 ppm (137 data points) and values < 357 ppm (40 data points) were deleted.

| Date | Cruise | Minimum air per cruise | Avcruise | Std | JD ESRL | Av3sta | Std3sta |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2006.63 | SKO609 | 367.75 | 374.37 | 1.98 | 2006.63 | 374.28 | 0.90 |
| 2006.75 | SKO610 | 377.07 | 378.96 | 1.24 | 2006.71 | 374.64 | 0.51 |
| 2006.79 | SKO611 | 378.54 | 382.16 | 1.85 | 2006.79 | 379.01 | 0.68 |
| 2006.86 | SKO612 | 382.07 | 384.80 | 1.71 | 2006.88 | 382.88 | 1.32 |
| 2006.97 | SKO613 | 385.55 | 387.63 | 1.18 | 2006.96 | 385.19 | 1.34 |
| 2007.02 | SKO701 | 386.14 | 388.23 | 0.92 | 2007.04 | 386.59 | 0.67 |
| 2007.09 | SKO705 | 387.13 | 388.95 | 0.82 | 2007.13 | 387.26 | 0.81 |
| 2007.17 | SKO709 | 387.64 | 389.69 | 1.52 | 2007.21 | 387.78 | 1.22 |
| 2007.25 | SKO713 | 386.85 | 389.87 | 1.75 | 2007.29 | 388.12 | 0.86 |
| 2007.32 | SKO717 | 384.31 | 389.21 | 0.96 | 2007.38 | 387.31 | 0.90 |
| 2007.40 | SKO721 | 382.39 | 388.25 | 1.09 | 2007.46 | 384.69 | 0.49 |

Legend:

Date:				Midpoint of cruise in decimal year

Cruise:				Cruise designation

Minimum air per cruise:	Minimum air XCO2 value measured on the cruise

Avcruise:			Average air XCO2 value measured on the cruise

Std:				Standard deviation of air XCO2 values measured on the cruise

JD ESRL:			Time of flask sampling from ESRL-GMD network

Av3sta:			Average of flask samples from Azores, Ireland (Mace Head), and 					Iceland

Std3sta:			Standard deviation of air XCO2 for the 3 flask stations

5.  Pressure sealevel is Pequil- 3 mB

Based on Takahashi et al (2008) and our experience on the Explorer of the Seas, we assume that the pressure outside the ship (sealevel pressure) that was not measured equals  (Pequil- 3 mB).  That is, inside the  ship there is a slight overpressure.  All fCO2a values were calculated using Pequil-3mB.

6. All entries that have QC flag =4 have fCO2_SW@SST_uATM and dfCO2 set to -999. The xCO2_EQU values are retained.

7. Anomalous changes in xCO2_EQU

If   subsequent XCO2w values changed by more than 20 ppm, the anomalous value was deleted.  and flagged as 4. This mostly occurred upon startup of system (158 data points deleted).