Summary of cruise AX080519 between Durban and Newark

AX080118 was conducted aboard the Maersk Vilnius. I boarded the ship at Cape Town on the morning of the 25rd of May 2019 and did the installation and testing of the equipment. Tw0 test drops were done when leaving Cape Town on the 25th May and the drops for the AX080519 commenced on the 26h May 2019 until the ship arrived at Newark on the 11th June 2019

A total 496 XBT’s were deployed. High density deployments commenced from a depth of 200m once passing Cape Town on the 26th May and continued until a depth of 200m was reached before Newark on the 11th June 2019. The trip went very well. Unfortunately one of the boxes wasn't loaded so I had to make a plan with mounting the A/L without the H-frame . 8 XBT's never passed the tube check and 5 re-drops were done due to wire snaps. 3 XBT's passed the tube check but were faulty on release. On the mornings of the 31st May and 1st June the Iridium set the dates one day ahead. This only effected a few drops since I picked up the error and corrected the date quite early. The Iridium was used for date/time and position since the 2 NMEA need to be reprogrammed. Other than the above no problems were experienced. The MK21 card and A/L gave no troubles.

No SVPB drifters or Argo floats were deployed.

We had fine weather for most of the trip. The Maersk Vilnius is an ideal ship for XBT deployments since it maintains a very steady speed and the point of release is close to the water resulting in very few faulty drops due to launching position. The distance from the cabin to the launcher and antenna isn’t far making installation a lot simpler.

The Captain and crew were hospitable and helpful during the voyage.

F. Mckay