## Slide 1: Development of new technologies for real-time monitoring of tropical cyclone intensity, structure, and environment
Jason Dunion

## Slide 2: Sensing Hazards with Operational Unmanned Technology
Demonstrate an Unmanned Aircraft Systems (UAS) concept of ops
Data impact studies
Observing System Experiments (UAS data)
Observing System Simulation Experiments
(simulated UAS data)
Global Hawk
SHOUT MISSON SCIENCE TEAM (2015-2016):
NOAA HRD, NOAA AOC, NOAA PSD, NOAA EMC, MRL-Monterey, Naval Post Graduate School, UW-CIMSS, NASA Goddard, University of Miami, University at Albany-SUNY, Pennsylvania State University, University of Utah

## Slide 3: NOAA SHOUT Field Campaigns (2015-2016)
Hurricanes 2015
El Niño Rapid Response 2016
Hurricane Rapid Response (HRR) 2016
3 missions- 2 tropical cyclones (TCs)
3 missions- targeting 2 high-impact weather events
9 missions- 4 TCs
Notes: Mention that SHOUT’s operational conops followed (2012-2014) NASA HS3

## Slide 4: NOAA SHOUT: Global Hawk Aircraft
Duration: ~24 hr
Flight Level: ~55-65,000 ft
Range: 8-10,000 nm
Payload: 1,500+ lbs

## Slide 5: Global Hawk SHOUT Instrumentation
GPS Dropsondes
Measurements:
In situ P, T, H, & wind
90 dropsondes per flight
HAMSR Microwave Sounder
2016 Hermine
warm core
Measurements:
25 channels (50-60, 118, & 183 GHz)
3-D T, water vapor, & CLW
55 GHz Channel (~250 hPa)
HIWRAP Doppler Radar
Measurements:
Dual frequency (Ka & Ku band)
3-D winds & precipitation
Radar Reflectivity (dBZ) & 1 km wind
2016
Matthew
Notes: Airborne Vertical Atmospheric Profiling System (AVAPS)
High Altitude Monolithic Microwave Integrated Circuit (MMIC) Sounding Radiometer (HAMSR): 2km vertical res; 40 km wide swath;
High-Altitude Imaging Wind and Rain Airborne Profiler (HIWRAP) : dual beam, conical scanning; 60 m vertical res; 1 km horizontal res

## Slide 6: Sampling the Tropical Cyclone Environment
15 km
20 km
10 km
5 km
1 km
10 km
5 km
1 km
Temperature
Dewpoint
Temperature
Dewpoint
Temperature
Dewpoint
P-3 Orion
AF C-130
G-IV
Global Hawk
Mid Latitude
Dry Air
Outflow
Layer
Tropopause

## Slide 7: Impact of Global Hawk Dropsondes on GFS Track Forecasts
Track Forecast Skill (%)
0
12
24
-12
-24
12
24
48
72
96
120
Forecast Hour
15%
Global Hawk
No Global Hawk
GH Dropsonde Impact: GFS Track
Notes: Shown here is the impact of the GH dropsonde data only on the GFS track forecast when added to the full current observing system (i.e., includes all routine observations from satellites, RAOBS, and other aircraft)
NOAA EMC views these as notable improvements
Results courtesy Jason Sippel and Vijay Tallapragada, NOAA/NCEP/EMC
FV3 GFS results are ongoing and will be available soon

## Slide 8: Targeting Dropsondes to Improve Model Forecasts*
Where do you sample and will the model be sensitive to your added data?
Where is there uncertainty in the model forecast?
Where is the model more vs less sensitive to observations?
* Research (NOAA SHOUT) to operations (NOAA Joint Hurricane Testbed)

## Slide 9: TROPICS Satellite Mission Time-Resolved Observations of Precipitation structure and storm Intensity with a Constellation of Smallsats
8 Temperature Channels
(91-118 GHz)
5 WV Channels
(91-205 GHz)
Rapid-refresh microwave obs
(temperature, moisture, & precipitation)
TROPICS Applications Workshop: February 19-20, 2020 University of Miami
Notes: 1) the baseline mission will have six satellites
2) we have built a seventh satellite that is fit for flight – we could launch it early (my preference, but need concurrence from NASA) or use it as a spare, TBD
3) all hardware will be complete in December, and NASA hopes to launch us in 2022 but hasn’t issued a contract to a launch provider yet

## Slide 10: THANK YOU